## Slide 1
Hub calculation
February 28, 2018

## Slide 2: Introduction
Purpose of this presentation is to explain technical details of the situation with DAM Hub SPPs discussed in market notice M-A021618-01 sent on February 16, 2018.
  There are two ways in which Hub prices/MW distribution may diverge between the Protocol definition and DAM implementation:
    DAM uses power flow buses instead of Electrical Buses in the calculation for both base case and contingency cases.
    If a contingency disconnects an Electrical Bus, the DASPP formula for Hubs in Protocol section 3.5.2 may not be correct because the distribution factors may differ from the base case, even if the Electrical Bus is accurately mapped to the power flow bus.
  All the scenarios in this presentation discuss only the base case.
Important to note:
  Published DAM Hub prices and awards have always been consistent.
  DAM and CRR are in alignment with regards to distribution of MWs and pricing.
  Real-Time is using Electrical Buses.

## Slide 3: Protocol language - definitions
Section 2.1-
Hub
A designated Settlement Point consisting of a Hub Bus or group of Hub Buses and the associated Settlement price calculation methodology prescribed in the definition of the Hub in Section 3.5.2, Hub Definitions. Hubs may only be created by an amendment to Section 3.5.2. The list of Hub Buses and the Settlement price calculation methodology that define a Hub can never be modified, and a Hub, once defined, exists in perpetuity.
Hub Bus
An energized Electrical Bus or group of energized Electrical Buses defined as a single element in the Hub definition. The Locational Marginal Price (LMP) of the Hub Bus is the simple average of the LMPs assigned to each energized Electrical Bus in the Hub Bus. If all Electrical Buses within a Hub Bus are de-energized, the LMP of the Hub does not include the de-energized Hub Bus. This is used solely for calculating the prices of existing Hub Buses defined in Section 3.5.2, Hub Definitions.

## Slide 4: Protocol language - definitions
Section 2.1-
Electrical Bus
(1) A physical transmission element defined in the Network Operations Model that connects, using breakers and switches, one or more:
(a) Loads;
(b) Lines;
(c) Transformers;
(d) Generators;
(e) Capacitors;
(f) Reactors;
(g) Phase shifters; or
(h) Other reactive control devices to the ERCOT Transmission Grid where there is negligible impedance between the connected Transmission Elements.

## Slide 5: Normal Base Case Scenario
Consider this example of the hypothetical station “Alpha”. In this case, Alpha is a Hub Bus of hub, HUB_1.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Station C
Station B
Circuit Breakers
Connectivity Nodes

## Slide 6: Normal Base Case Scenario
Consider this example of the hypothetical station “Alpha”. In this case, Alpha is a Hub Bus of hub, HUB_1. The Hub Bus definition of Alpha consists of one Electrical Bus: Alpha_1. (Certain nodes are designated in the CIM/Network Operations Model as Electrical Buses.)
When converted to DAM’s PSSE Bus/Branch model, Station Alpha consists of just one 345kV PSSE bus.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1 in Station Alpha

## Slide 7: Normal Base Case Scenario
Consider this example of the hypothetical station “Alpha”. In this case, Alpha is a Hub Bus of hub, HUB_1. The Hub Bus definition of Alpha consists of one Electrical Bus: Alpha_1. (Certain nodes are designated in the CIM/Network Operations Model as Electrical Buses.)
When converted to DAM’s PSSE Bus/Branch model, Station Alpha consists of just one 345kV PSSE bus.
In this scenario, the Hub Bus Alpha price calculation is the same for these two models.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1 in Station Alpha
where

## Slide 8: Split Bus Base Case Scenario
The first example of Hub Bus price divergence is when a split occurs in the 345kV section of a station that is designated as a Hub Bus.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1 in Station Alpha

## Slide 9: Split Bus Base Case Scenario
The first example of Hub Bus price divergence is when a split occurs in the 345kV section of a station that is designated as a Hub Bus. When 345kV model is split, DAM creates two PSSE buses to represent the 345kV in the station.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1
PSSE Bus #2

## Slide 10: Split Bus Base Case Scenario
The first example of Hub Bus price divergence is when a split occurs in the 345kV section of a station that is designated as a Hub Bus. When 345kV model is split, DAM creates two PSSE buses to represent the 345kV in the station.
345kV split impact:
Real-Time calculation doesn’t change. LMP of Alpha_1 is the only price used.
DAM calculation of Hub Bus Alpha includes LMPs of both Bus#1 and Bus#2.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1
Hub Bus Alpha LMP =
where
and
PSSE Bus #2

## Slide 11: Split Bus Base Case Scenario
345kV split impact:
Real-Time calculation doesn’t change. LMP of Alpha_1 is the only price used.
  Example: Alpha_1 LMP = $15. Hub Bus Alpha LMP = $15.
DAM calculation of Hub Bus Alpha includes LMPs of both Bus#1 and Bus#2.
  Example: Alpha_1 LMP = $15. PSSE Bus #1 LMP = $15. PSSE Bus #2 = $16. Hub Bus Alpha LMP = $15.50
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1
Hub Bus Alpha LMP =
where
and
PSSE Bus #2

## Slide 12: Split Bus De-energized Base Case Scenario
The second example of Hub Bus price divergence occurs when an Electrical Bus of the Hub Bus is de-energized due to an outage, but there are still energized 345kV connectivity nodes in the station.
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
PSSE Bus #1 in Station Alpha

## Slide 13: Split Bus De-energized Base Case Scenario
The second example of Hub Bus price divergence occurs when an Electrical Bus of the Hub Bus is de-energized due to an outage, but there are still energized 345kV connectivity nodes in the station.
De-energized Electrical Bus Impact:
Real-Time Hub calculation does not include Hub Buses with zero energized Electrical Buses. Hub Bus Alpha will not be used at all in the price calculation of HUB_1.
PSSE Bus #1
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
De-energized bus

## Slide 14: Split Bus De-energized Base Case Scenario
The second example of Hub Bus price divergence occurs when an Electrical Bus of the Hub Bus is de-energized due to an outage, but there are still energized 345kV connectivity nodes in the station.
De-energized Electrical Bus Impact:
DAM calculation of Hub Bus Alpha will only use the LMP of Bus#1. De-energized PSSE buses are not included in the Hub Bus price calculation. Hub Bus Alpha will still be used in the price calculation of Hub_1.
PSSE Bus #1
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
HubBus Alpha LMP = ,
where
De-energized bus

## Slide 15: Split Bus De-energized Base Case Scenario
De-energized Electrical Bus Impact:
Example:
RT – Hub Bus Alpha LMP = n/a
DAM – PSSE De-energized bus LMP = n/a. PSSE Bus #1 LMP = $15. Hub Bus Alpha LMP = $15
PSSE Bus #1
Real-Time Station Example – Alpha (345kV)
DAM PSSE Station Example – Alpha (345kV)
Station B
Station C
Electrical Bus - Alpha_1
Station C
Station B
HubBus Alpha LMP = ,
where
De-energized bus

## Slide 16: Distribution of MWs - CRR/DAM vs Protocols
Issue 1 – Hub Bus distribution
Hub
300 MW
Hub Bus 1
100 MW
1/3
1/3
1/3
Hub Bus 3
100 MW
Hub Bus 2
100 MW
CRR/DAM
PF1 = 50MW
Protocols
eb1 = 33.33 MW
eb2 = 33.33 MW
eb3 = 33.33 MW
PF1 = 33.33 MW
PF2 = 66.66 MW
PF2 = 50MW
eb2
PF2
eb1
eb3
PF1

## Slide 17: Distribution of MWs - CRR/DAM vs Protocols
Issue 2 – Hub Bus distribution under contingency that de-energizes an electrical bus
eb2
PF2
Hub
300 MW
Hub Bus 1
100 MW
1/3
1/3
1/3
Hub Bus 3
100 MW
Hub Bus 2
100 MW
eb1
eb3
PF1
CRR/DAM
PF1 = 100 MW
Protocols
eb1 = 33.33 MW
eb2 = 33.33 MW
eb3 = 33.33 MW
PF1 = 33.33 MW
PF2 = 66.66 MW
PF2 = 50MW
Contingency de-energizes PF2, eb2/eb3

## Slide 18: Distribution of MWs - CRR/DAM vs Protocols
Issue 2 – Hub Bus distribution under contingency that de-energizes an electrical bus
eb2
PF2
Hub
300 MW
Hub Bus 1
100 MW
1/3
1/3
1/3
Hub Bus 3
100 MW
Hub Bus 2
100 MW
eb1
eb3
PF1
CRR/DAM
PF1 = 100 MW
Protocols
eb1 = 33.33 MW
PF1 = 33.33 MW
PF2 = 50MW
Contingency de-energizes PF2, eb2/eb3
De-energized 66.66 MW goes to the slack bus.

## Slide 19: Summary
Real-Time uses Electrical Buses to determine Hub prices
DAM uses PSSE buses to determine Hub MW distribution and prices. In some scenarios, this distribution can diverge from one based on Electrical Buses.
  The protocols state that Electrical Buses should be used.
  DAM and CRR both use a PSSE model for the optimization.
  There are a number of issues with attempting to use Electrical Buses rather than PSSE buses.
    ERCOT:
      is continuing to evaluate, particularly with regard to contingency cases.
      has not yet taken a vendor patch on this issue.
      will pursue a protocol change.