## Slide 1: Nuts and Bolts of Connecting Projects to ERCOT
Bill Bojorquez
VP, System Planning
November 28, 2007
Impacts of CREZ on Transmission Build-out
and Wind Power Opportunities in the Texas Market
Workshop

## Slide 2: Transmission Policy Background
ERCOT-wide postage-stamp transmission rate, paid by load
Generators post security for new interconnection facilities
Utilities are responsible for transmission upgrades
Transmission upgrades (including interconnection-related) are ultimately rolled into regional rate

## Slide 3: Texas Renewable Energy Program
1999 legislation established Renewable Portfolio Standard
  Renewable energy goal of 2,000 MW of new renewables by 2009
  Renewable Energy Credit (REC) program to facilitate liquidity and tracking
  Load serving entities must buy sufficient RECs to meet their share of the RPS requirement

## Slide 4: TX Senate Bill 20 (2005)
Increased renewable energy goal
  5,880 MW in 2015
  10,000 MW target in 2025
Set up process to allow PUCT to pre-approve transmission for renewables through the designation of Competitive Renewable Energy Zones (CREZs)

## Slide 5: Current Wind Development
~4,150MW installed capacity of wind generation in-service
~2,629MW additional wind development with signed interconnection agreements
Additional bulk transmission lines will be
required for > ~6,000MW
~35,000 MW additional wind development in interconnection study process
Some overlap with CREZ nominations

## Slide 6: Summary of “Planned” Wind Generation (as of 9/15/2007)
2007-2010
2011+
MW Nominated in CREZ
MW
in I/C Process
7,650 MW
26,897 MW
8,892 MW
6,850 MW
~26,000 MW
In-Service Dates
In-Service – 4,150 MW
Signed IAs – 2,629 MW

## Slide 7
ERCOT Load
~62,000 MW summer peak demand
Majority of load is concentrated in eastern half of state
  Dallas
  Austin
  Houston
  San Antonio

## Slide 8: Potential Wind Resource
10600
8300
12000
9600
7900
6900
6000
6200
4700
2900
4600
3000
2200
2700
Nearly 100,000 MW above 35% capacity factor (CF)
Concentrated in western half of state
Approximate wind capacity (in MW) potential in each area is indicated by pink bars
Nearly 100,000 MW above 35% capacity factor (CF)
Concentrated in western half of state
Approximate
west to east transfer
capacity – 3200MW

## Slide 9: New Transmission Required
10600
8300
12000
9600
7900
6900
6000
6200
4700
2900
4600
3000
2200
2700
Existing system from west Texas is significantly congested
Significant distances and costs associated with adding bulk transmission
200 miles
150 miles

## Slide 10: ERCOT CREZ Study
ERCOT led study during 2006 to support PUCT determination
  Hired wind modeling consultant to identify best wind resource sites and provide expected characteristics of wind generation
  Developed transmission plans through open stakeholder process to accommodate many of the potential zones in various combinations
  Filed results with PUCT in December 2006

## Slide 11: PUCT CREZ Case
Initiated in January, 2007
PUCT issued interim CREZs zone designations last month considering:
  Renewable resource and suitable land
  Financial commitments of developers
PUCT requested ERCOT Transmission Optimization Study prior to designating transmission lines
Notes: <number>
<footer>
<header>

## Slide 12: PUCT Interim Order
Designates CREZs in five areas of the Panhandle and West Texas
Identifies parties who demonstrated financial commitment
Orders ERCOT to develop transmission plans for four different levels of installed wind in these CREZs
  CREZ Transmission Optimization Study to be filed with PUCT by 4/2/2008

## Slide 13: Selected Zones - Geographically
Panhandle B (CREZ 4)
Panhandle A (CREZ 2A)
Central (CREZ 9A)
Central West (CREZ 19)
McCamey (CREZ 5&6)

## Slide 14: Designated Zones and Scenario Wind Levels
Capacity of New CREZ Wind by Scenario (MW) |  |  |  | 
Wind Zone | Scen. 1 | Scen. 2 | Scen. 3 | Scen. 4
Panhandle A | 1,422 | 3,191 | 4,960 | 6,660
Panhandle B | 1,067 | 2,393 | 3,720 | 0
McCamey | 829 | 1,859 | 2,890 | 3,190
Central | 1,358 | 3,047 | 4,735 | 5,615
Central West | 474 | 1,063 | 1,651 | 2,051
Total* | 12,053 | 18,456 | 24,859 | 24,419
* Assumes 6,903 MW of existing wind capacity |  |  |  | 

## Slide 15: CREZ Transmission Optimization (CTO) Study
ERCOT Staff initiated Study in anticipation of written Interim Order at Regional Planning Group (RPG)
Have initiated subgroup of RPG for more frequent meetings and communications related to CTO Study
  Sign up for RPG-CREZ distribution list at http://lists.ercot.com
  Website at http://www.ercot.com/committees/other/rpg/crez/index.html

## Slide 16: Generation Interconnection Requests Process
I. Interconnection Feasibility Request submitted to ERCOT
II. ERCOT performs steady state analysis and provides rough estimate of facility additions
III. Generation owner reviews information and incorporates it into its decision – making process
IV. Generation owner requests a full interconnection study
V. Transmission Owner (TO) performs detail analysis and determine final cost estimate.
VI. Generation owner signs interconnection agreement with TO
VII. Transmission Projects are approved

## Slide 17: Qualified Scheduling Entities (QSEs)
  The entities with which ERCOT directly communicates for planning and executing daily power transactions
  Represent Resources Entities and/or Load Serving Entities.
  Establishes and submits schedules for meeting planned demand and generation.
  Financial settlement of the market is performed between ERCOT and QSEs.

## Slide 18
Load
Generation
LSE 1
LSE 2
Residential
Commercial
Commercial
Industrial
PGC
Retail Market
Wholesale Market
ISO
SCADA Data
Customer Meter
Loss Information
TDSP
Awards
Settlement
Schedule & bids
QSE 1
QSE 2
QSE Functions and Market Players

## Slide 19
QUESTIONS?