| PRR Number | 282PRR | PRR Title | Define OOME as an Instructed Deviation |
| --- | --- | --- | --- |
| Recommended Action |  |
| Recommended Effective Date |  |
| PRR Background | Provide clarification on the definition of OOME. |
| Protocol Revision Subcommittee Recommendation | PRS recommends approval of the clarification as amended by ERCOT and directs WMS to draft the Protocol change to implement the clarification on the calculation of the SCE. |

Recommended Language

#### 6.10.4.4	Schedule Control Error

ERCOT will calculate the following for each QSE for each two-second period:

SCE	=	 Actual Generation

+    Load Resource Response to Instructions

- Base Power Schedule

- Sum of any Dynamic Resource Power Schedules

- Expected Governor Response due to frequency of the QSE’s portfolio of Resources

- Instructed Ancillary Services power

PIP112: Add the following paragraph to the equation when BUL language is implemented:

-- The signal sent to ERCOT that is estimated in real-time representing the real power interrupted in response to the deployment of Balancing Up Load (BUL) for Dynamically Scheduled Load

Instructed Ancillary Services 	=	Instructed (Regulation Service

- Responsive Reserve

- Non-Spinning Reserve

- Balancing Energy power schedule)

PIP112: Add the following when BUL is implemented:

ERCOT will determine Load Resource Response to Instructions for Loads that are providing Responsive Reserve, Non-Spinning Reserve or Replacement Resources from the information submitted in the Resource Plan and the telemetry of the real power consumption of the Load Resource. Load Resource Response to Instructions is calculated for each Load Resource that is indicated available in the Resource Plan according to the following formula:

Load Resource Response to Instructions  =

MAX [0, MIN((upper operating limit -real power consumption), (upper operating limit -  lower operating limit))]

Balancing Energy Up - Load deployments are not considered in the Instructed Balancing Energy power schedule.

| PRR Evaluation |
| --- |
| Non-ERCOT Market Comparison | No Comparison conducted. |
| Comments Author | Comments Summary |