| PRR Number | 309PRR | PRR Title | Demand Reporting Requirement for TDSP |
| --- | --- | --- | --- |
| Recommended Action | Approve. |
| Recommended Effective Date | October 1, 2002 |
| System Impact | No |
| PRR Background | Wording changes in demand reporting requirements that better reflect the intent of the current Protocol language. |
| Protocol Revision Subcommittee Recommendation | PRS recommends approval of PRR309 as amended. |

Recommended Language

10.3.3 TDSP Metered Entities

10.3.3.1 Data Responsibilities

TDSPs are responsible for:

- Providing consumption data for each ESI ID and RID on a monthly basis according to the data timeliness and accuracy standards defined in this Section and in the Operating Guides.

- Providing start date, stop date, ESI ID or RID, and consumption data in kWh as well as an identifier for “estimated” reads as applicable.

- Submitting a single demand value for each non-IDR ESI ID that has a demand register to ERCOT if and only if a demand value is required for TDSP tariffs or for CR customer billing.  If the CR and TDSP do not require a demand value, then the TDSP shall not submit a demand value to ERCOT even if the meter has a demand register.

- Validating, Estimating and Editing (VEE) meter data according to the standards in this Section before submitting data to the settlement process.

- Calculating consumption for any unmetered services by ESI ID and submitting such data monthly to ERCOT, subject to ERCOT audit.  These calculations will be based on TDSP approved tariffs.

- Metering all Loads by May 1, 2001, unless the Load meets the following criteria:

  - Energy consumption by substation Facilities and equipment for the purpose of transporting electricity (e.g., substation transformers, fans, etc).

  - Unmetered energy consumption represented by an ERCOT-approved Load Profile.

--------------------------------------------------------------------------------------------------------------------

18.6.6 Peak Demand Determination for Non-IDR Premises

For the purpose of determining the peak demand level…

A Premise (ESI ID) has a peak demand…

ERCOT shall be responsible for receiving and storing demand information necessary for determining mandatory IDR installations.

| PRR Evaluation |
| --- |
| Non-ERCOT Market Comparison | No Comparison conducted. |
| Comments Author | Comments Summary |
| Load Profiling Working Group | The Load Profiling Working Group, the sponsor of this PRR, would like to recommend the implementation date of October 1, 2002 for this request. The group feels that adequate time should be allocated to allow TDSP system changes to be completed. The group also recommends that the revised language be gray-boxed until it goes into effect on October 1, 2002. |