# ROS report to TAC for August 6th 2003 meeting

……………………..OGRR’s………………………

| OGRR Number | 129OGRR | OGRR Title | Transmission Operator (TO) / TDSP Emergency Communication |
| --- | --- | --- | --- |

Adds requirement for Transmission Operators to notify the appropriate TDSPs of ERCOT declared emergency events.

| OGRR Number | 130-OGRR | OGRR Title | Automatic Voltage Regulator (AVR) and Power System Stabilizers (PSS) Status Reporting Requirements |
| --- | --- | --- | --- |

Revision is meant to make Operating Guides consistent with Protocol 6.5.7 (9), which requires each QSE to “promptly inform ERCOT” when the QSE changes the status of the Generation Resource’s AVR or PSS.

| OGRR Number | 131OGRR | OGRR Title | LaaR Qualification Procedure for Responsive Reserve Service, Non-Spin Service, and Replacement Reserve Service. |
| --- | --- | --- | --- |

Specifies LaaR requirements to qualify as a provider of Responsive Reserve Service, Non-Spin Service, and Replacement Reserve Service. Fulfills requirement of Protocol 6.10.1 that specifies ancillary service qualification programs will be approved by the Technical Advisory Committee and will be included in the Operating Guides.

| OGRR Number | 134OGRR | OGRR Title | Calculation of Transmission Equipment Limits |
| --- | --- | --- | --- |

Defines equipment ratings for TDSP’s facilities and ERCOT’s use of the ratings.

………….….ROS Activities - Highlights…………………

OGRTF - ROS was instructed by TAC to ensure that RAP/SPS requirements language is clarified in the ERCOT Operating Guides so that all affected parties are notified.  The OGRTF was directed to compare the Operating Guides to the ERCOT RAP/SPS Document and resolve any differences.

SSWG    - The ROS discussed the use of seasonal ratings as an interim step working toward implementation of dynamic ratings.  The SSWG was directed to review the use of seasonal ratings and provide feedback to the Dynamic Ratings Task Force (DRTF).  It was suggested that the first year (first after Set A) of SSWG Data Set B to support the CSC and Congestion Management Zone calculations also be included in the above methodology of keeping track of the Continuous, Emergency, and 15-Minute Ratings for Market use.  The ROS discussed this suggestion and the SSWG will also review and make a recommendation.

PDCWG - .  In an effort to find an additional way for ERCOT staff to spot check the voltage support status of AVR’s; the PDCWG suggested the AVR mode of operation might be determined by trending MVAR output of generators and observing changes in output (MVAR) as voltage is adjusted on neighboring generators. Sydney Niemeyer ( the PDCWG chair) will discuss the trending of generating unit data with John Adams so that a standard can be developed to allow ERCOT to monitor the status of AVRs.

FCTF - The FCTF is continuing to work with the PDCWG to analyze the events of February 24th-26th. Confidentiality issues with data needed by the FCTF to analyze frequency events have not yet been resolved.  ERCOT has been asked to inform the FCTF which data is available and not confidential at this time.

Henry Wood ( FCTF chair) reviewed proposed Protocol Revision language for Sections 5.6.3, 5.6.4, and 5.6.6 to reference system wide fuel curtailments and shortages.  Wood was asked to develop a PRR to incorporate the proposed Protocol Revision language presented.

Letter from NERC - The ROS discussed a letter from NERC announcing that a review has been initiated of 0600 and 2200 frequency excursions that are occurring in all three Interconnections.  These are occurring on a regular basis.  One contributing factor to the frequency decline seen at the 2200 hour is the abrupt ending of large amounts of 16 hour block sales which overwhelms the ability of replacement generation to compensate for the change.  These excursions are causing some Control Areas, including ERCOT, to have poor CPS performance during these hours.  This could eventually cause ERCOT to fail the CPS 1 Standard.  The ROS discussed the need to develop standards and metrics to allow Control Areas to limit the size of schedule ramps to the capability of its capacity to follow the ramps.  The FCTF was directed to review the NERC letter and determine a course of action to address the issue in ERCOT.

Frequency Control study budget - Because ERCOT Staff is currently preparing its 2004 budget, ROS Representatives were asked whether ERCOT should budget to engage a consultant to complete Phase 2 or similar study of frequency control performance in 2004. It was noted that many fixes proposed in Phase 1 have not been implemented so Phase 2 would have little to validate at this time.  A motion was made that the ROS requests that ERCOT submit funding in the 2004 Budget to address Frequency Control Issues as identified by the ROS in 2004.  The motion was approved with one abstention.

BSTF- The BSTF proposes that Black Start Training for 2004 be conducted in much the same manner as 2003.  The BSTF recommends that ERCOT provide Black Start Training to a primary target of TDSPs, Black Start QSEs, and Black Start Resources. Next start Resources or other Market Participants will be accommodated as space in each session allows.  The training sessions will be exclusively dedicated to system restoration.  The BSTF proposes that ERCOT training personnel conduct the training sessions and that the sessions be hosted by TOs at four locations.  It was suggested that more emphasis be placed on next start Resources.  This will be added to the BSTF Proposal.  A motion was made that the ROS endorse the BSTF Proposal as amended (more emphasis on next start Resources).  The motion was approved by a unanimous voice vote.

# Footnotes

Operating Guides Revisions Task Force

Steady State Work Group

Performance Disturbance Compliance Work Group

Frequency Control Task Force

Black Start Task Force