|  | Integrated Model | Auction Model |
| --- | --- | --- |
| PROs | Allows price certainty for load and resources cleared for congestion in the day-ahead Assures resources of receiving no less than their bid price for energy Results in greater day-ahead market liquidity since TCRs could only clear in Day-ahead market (strong financial incentive) Provides somewhat more operational data to ERCOT to use in system planning than today’s market design It is more transparent for decision-making Allows virtual bidding. Creates greater efficiency for the market by developing an ERCOT wide integrated resource plan Energy and A/S can be co-optimized on a locational basis Allows the proper incentives for mid-load plants to commit and allows for their ramping through train reconfigurations | Simple and least cost to implement overall. Requires no mitigation or market monitoring due to lack of interaction between bids, congestion, CRRs and SCED in day-ahead and real-time. Is a centralized auction clearing exchange similar to Nord Pool DAM and UKPX, by far the most liquid electricity markets in the world. Allows for flexibility in congestion cost hedging until real-time since CRRs don’t expire day-ahead. Any changes in individual operating plans or schedules due to outages, changes in market conditions, fuel constraints or weather conditions from the day-ahead plan can still be hedged until real-time. Allows for Dynamic Scheduling which is consistent with current protocols – NOIEs can avoid the problem of buying and selling imbalance energy. Keeps the DAEM voluntary as required by the PUCT Rule – the activities of others in the DAEM does not impact non-participants. Non-participants are not economically “forced” to participate in the DAEM to counter the actions of others. Allows price certainty for load cleared day-ahead at load zone or generation cleared at generation node Model is simple and straightforward to implement for both ERCOT and market participants. Settles CRRs on actual congestion and sets LMPs on the true real-time SCED. The financial model better matches physics of the system Allows virtual bidding. |
| CONs | Can be easily gamed since the day-ahead SCED resolves congestion based on bilateral schedules and bids and offers that may be either physical or virtual. Requires greater sophistication on the part of market participants to effectively counter the actions of others in day-ahead market – participants are forced to virtual bid to counter the adverse impacts of the virtual bidding of others. Requires extensive market mitigation and daily market monitoring at ERCOT due to manipulative activities surrounding CRRs and virtual bidding resulting in market inefficiency. Is more complex to implement and much more expensive to monitor. Resource costs cannot be accurately represented in SCUC leading to market inefficiency– e.g. tiered Natural Gas contracts cannot be accurately represented by multi-part bids used in any centralized unit commitment and ERCOT is heavily dependent on Natural Gas fired Resources (over 60% compared to 6% for PJM). Dynamic Scheduling by NOIEs are not readily accommodated under IDAM. To this point no acceptable solution has been suggested. May require a bid sufficiency mechanism to assure that adequate resources are offered into the market. This would not meet the PUCT Rule requirement for a voluntary market. | May not have much liquidity due to supply-side risk A formalized exchange market creating limited value above today’s broker market at a potentially higher cost Will likely take longer than the integrated model to develop a liquid market. Less likely to have full market transparency, therefore, it will not enhance forward contracting No RTO/ISO uses as day-ahead market Cannot lock in day-ahead the cost of transmission congestion without CRRs Creates a ‘lumpy” unit commitment that may lead to inefficiencies for dispatched units leading to improper bidding incentives Main issue little to no value added over today’s model |