## Slide 1: Agreed Market Design Parameter for Vote at Future TNT Meeting January 13, 2004

## Slide 2: Real-Time Operations
LMP dispatch every 5 minutes with nodal prices and resource setpoints
LFC operating and moving regulation every 4 seconds
State estimator running approximately every 5 minutes just prior to SCED
State estimator provides load bus data and other network parameters to SCED (LMP calculator)
SCED (LMP calculator) will run every 5 minutes based on state estimator output, linearized binding constraints from security analysis and may include a 5-minute load forecast based on best practices of other ISOs.
Security analysis is run at least every hour or when major network topology changes occur to explore a prescribed set of contingencies on the then current network configuration to identify binding constraints and linearize their modeling for SCED. The number of linearized binding constraints should not be severely limiting (e.g., 100’s not 10’s)
Dynamic line ratings will be supported by ERCOT for all TDSPs
<number>

## Slide 3: Reliability Unit Commitment – Day Ahead
<number>
Run after close of day-ahead energy market and day-ahead ancillary services. Procurement should be run as early in the day as possible and in a manner that reflects the nomination deadlines of the gas markets.
Resource capacity nominations will be provided by participants to reflect self-committed resources indicating ancillary services commitments, day-ahead market and/or bilateral transactions between participants.
ERCOT will perform the day-ahead RUC and will use its forecast of hourly load.
A security constrained unit commitment technique will be utilized.
The optimization of resources committed for the next day’s operation above those self-committed include the minimization of startup costs, no load operating costs, and minimum output energy costs subject to both transmission security constraints and reserve constraints. All units self-committed or still on line from previous days will have their energy bids set to zero for day-ahead RUC.

## Slide 4: Reliability Unit Commitment – Day Ahead
<number>
The output will be a list of units committed for tomorrow’s 24-hour operating period and the hours they need to be operational. It is assumed the units operate at minimum load unless instructed otherwise by the ERCOT dispatcher.
The resources committed will have a “make whole” provision.
(continued)

## Slide 5: Reliability Unit Commitment – Hour Ahead
<number>
Run every hour approximately one hour ahead of the operating period after the security analysis is run.
The run period will be for the operating hour period plus the remaining hours of the approved day-ahead RUCs (could be up to 35 hours).
The optimization of this RUC will be the same as the day-ahead RUC. All previously committed units will have their energy price set to zero.
ERCOT will update load forecasts during the day as required for the next 36 hours and accept changes for unit and transmission outages.
Resources committed will have “make whole” provisions.