## Slide 1: Open Market Operations Issues
Discussion for
Texas Nodal Team
January 20, 2004

## Slide 2: Open Market Operations Issues
RUC Price Components
“Make Whole” Provision
Assignment of RUC Charges
Overlap with Market Mitigation

## Slide 3: RUC Price Components

## Slide 4: RUC Price Components
RUC requires information on each generating unit to determine if it should be committed
  Some price parameters
  Energy bids
The following terms have been discussed as bidding components for the RUC:
  start up prices
  no load prices
  energy bid curves
Currently these terms are not defined in the ERCOT Protocols

## Slide 5: RUC Price Components
The PJM Cost Development Guidelines do address most of these terms and could be used as examples, as these terms are developed and defined in ERCOT

## Slide 6: RUC Price Components
Start Up is defined in Section 6 of the PJM Guidelines as : The dollars per start as determined from start fuel, total fuel-related cost, performance factor, electrical costs, start maintenance adder, and additional labor cost, if required above normal station manning levels
  NOTE: terms such as start fuel, performance factor and total fuel related costs are defined within the PJM Guidelines

## Slide 7: RUC Price Components
No Load Cost (in $/Hr) is defined in Section 2 of the PJM Guidelines as : the total theoretical heat or fuel input at zero net output multiplied by the performance factor, multiplied by the total fuel related cost plus the no-load additional labor cost
  The zero net output is derived from test data or through extrapolation of the theoretical input-output curve
  Terms such as no-load additional labor cost are defined within the PJM Guidelines

## Slide 8: RUC Price Components
Minimum Load/Minimum Energy are not defined with the Guidelines, however there is a formula for minimum energy costs wherein it is defined as: the hourly cost to operate at a minimum rating
  Minimum rating is defined within the calculation
ERCOT Protocols do have a definition of “Low sustainable limit” perhaps that could equate to the minimum load definition.

## Slide 9: “Make Whole” Provision

## Slide 10: “Make Whole” Provision
For a generator (resource) committed by ERCOT to be online for the RUC, the following will apply:
  ERCOT will honor each QSE’s start-up status, ramp rates and minimum run times established for specified off-line status of the unit (cold, warm, hot)
  ERCOT will notify the QSE when and for how long the unit is to be online for RUC purposes

## Slide 11: “Make Whole” Provision
  ERCOT will calculate for a 24-hour basis the difference between
    The actual energy revenue received by the unit based on the LMPs and the unit’s operating output; and
    The instructed energy output of the unit from the commitment process times the bid of the unit at that output
      The energy output instructed by ERCOT will include any additional hours to equal the unit’s minimum runtime (additional hours only at minimum output)

## Slide 12: “Make Whole” Provision
  Any positive difference (Actual LMP $ > Bid $) from the above will be used to offset the start-up and no load costs of the committed unit
  If the start-up and no load costs are fully offset, ERCOT does not owe the QSE a “make whole” payment
  If the start-up and no load costs are not offset, ERCOT owes the QSE the difference for the 24-hour period

## Slide 13: “Make Whole” Provision
  If the energy tracking for the 24-hour period results in a negative difference (Actual LMP $ < Bid $), then ERCOT owes the QSE the start-up, no load and negative difference of energy recovery (Bid Energy $ - Actual Energy $)
  If the minimum run requirement requires a unit to run into the next 24-hour period, then the tracking for the following day will account for any financial losses that ERCOT owes the QSE for the day before commitment

## Slide 14: “Make Whole” Provision
  The start-up and no load bids are essentially recovery of estimated unit costs plus a small percentage to account for error
  These bids should not be changeable for a 3-6 month period except for fuel price (index) adjustments
  The energy bid curve submitted by the resource immediately prior to the RUC should be “locked” for the entire operating day except for an actual unit outage or unavailability

## Slide 15: “Make Whole” Provision
  The unit must come online in the designated window to receive a “make whole” guarantee
    If the unit is on-line early, the “make whole” provision considers all the hours the unit is on-line
  The energy bid curve used in the “make whole” will be the RUC bid curve which are the actual bids for competitive units or mitigated bids for units with local market power

## Slide 16: Assignment of RUC Charges

## Slide 17: DaRUC Charge Assignment
DaRUC charges (startup, no load and minimum load not recovered through LMP) caused by system resource capacity insufficiency and/or transmission security violations
Goal is to appropriately assign these charges in a manner that follows cost causation principles, thus providing market incentives that promote overall efficiency

## Slide 18: DaRUC Charge Assignment
ERCOT conducts two studies: one to solely determine system resource capacity sufficiency and the other to determine system resource capacity sufficiency with the solution of any transmission security violations

## Slide 19: DaRUC Charge Assignment
System resource sufficiency charges arise when the total capacity self-committed is insufficient to meet the ISO load forecast plus required reserves

## Slide 20: DaRUC Charge Assignment
Transmission security charges arise from the ISO’s commitment of units not self-committed to solve transmission security violations
  The difference between the System Resource Capacity Sufficiency and the System and Transmission Security Cases represents the increase in RUC charges due to transmission security.
  This increase must be assigned appropriately on a cost causation basis

## Slide 21: DaRUC Charge Assignment
  A ratio based on the two cases determines the assignment of make whole payments to system sufficiency and to transmission security.
  System component will be assigned similar to to the current Replacement Reserve service.
  The transmission security component will be assigned to the QSEs in the LSA that do not cover their load with resources capably serving load in the LSA

## Slide 22: DaRUC Charge Assignment
Transmission security charges can be linked to local transmission constraints
  ERCOT determines Local Security Areas (LSA) annually using its load forecast and distribution to load buses (these may be subsets of Load Zones)
  Each resource is assigned to a LSA based on the units impact on local congestion

## Slide 23: Overlap with Market Mitigation

## Slide 24: Overlap with Market Mitigation
Some have proposed mitigation of energy bids to incent suppliers/QSEs to self-commit instead of allowing ERCOT to commit the resource through the RUC process
  Competitive Units
    Self-Committed: Their energy bid curve, if self-committed, is limited only by the $1K bid cap
    Not Self-Committed: A proxy bid for energy such as OOME if there is no self-commitment

## Slide 25: Overlap with Market Mitigation
  Non-Competitive Units
    Self Committed: A proxy bid cap for energy such as a heat rate (15K-18K MMbtu/kwh) times a fuel index if they self-commit
    Not Self-Committed: A mitigated energy curve such as tested heat rate times a fuel index times 110% if ERCOT commits the resource

## Slide 26: Overlap with Market Mitigation
  Comments By Others On Proposal
    Forcing a competitive resource or QSE to self-commit when it believes there are better opportunities to buy from the market is counter to a competitive wholesale market
    Creating an incentive for a non-competitive resource to self-commit instead of being committed in RUC may be an alternate solution to assigning congestion commitments for non-competitive constraints directly to those that caused them.
      However, the incentive must be sufficient to result in self-commitment and the level if a non-competitive unit is committed by RUC must allow a recovery of costs

## Slide 27: Overlap with Market Mitigation
  When should the start-up, no load, minimum run and minimum start times, etc. be allowed to change?
    Monthly
    Quarterly
    Semi-Annually
  When should energy bids be allowed to change?
    Each day prior to RUC
    Each Hour
    Both directions or only downward