## Slide 1: Hybrid DAM Models Comparison
Original HDAM | Enhanced HDAM
All CRRs default to RT settlement, but any CRR may be offered at a strike price for “cash out” in Daily energy and CRR auction | All CRRs default to DAM settlement, but any CRR may be specified for RT settlement (The network element flows and counterflows represented by RT CRRs will be used to adjust the available DAM network capacity)
Daily transmission constrained energy and CRR buy/sell/reconfiguration auction for all CRRs | Daily transmission constrained energy auction; reconfiguration auction for PTP Obligations through DAM scheduling (including “up to” congestion bids for transactions); CRR Options only have the alternative of settling in DAM or RT as price takers
3-part supply offers not accommodated in DAM | 3-part supply offers accommodated in DAM

## Slide 2: E-HDAM Proposal Details (1 of 3)
CRRs that are held by a Market Participant may be specified prior to the DAM to be settled based upon real-time nodal settlement prices. Any CRRs held by a Market Participant that are not specified to be settled in real-time and all other CRRs will be settled based upon day-ahead nodal settlement prices.
The CRR auction and/or PCRR allocation process will remain unchanged.
The network element flows (and counterflows) represented by CRRs that are specified to be settled in real-time will be accounted for in the determination of available transmission capacity in the DAM.
The Day Ahead market will use three-part supply offers.

## Slide 3: E-HDAM Proposal Details (2 of 3)
All participation by Market Participants in the Day Ahead market will be financially binding.
Residual costs or credits incurred in the DAM will be allocated to participants in the DAM.
Physical capacity nominations and additional inter-QSE bilateral schedules may be submitted after the DAM and prior to the RUC.
DAM energy sales will reduce gross capacity nominations submitted by QSEs after the DAM; DAM energy purchases will increase gross capacity nominations submitted by QSEs after the DAM.
Post-DAM, pre-RUC inter-QSE bilateral energy sale schedules will reduce gross capacity nominations submitted by QSEs after the DAM; post-DAM, pre-RUC inter-QSE bilateral energy purchase schedules will increase gross capacity nominations submitted by QSEs after the DAM.

## Slide 4: E-HDAM Proposal Details (3 of 3)
RUC cost allocation will be subject to the same mechanism, regardless of the level of participation in the DAM.
Energy imbalances from DAM schedules will be settled based upon real-time energy settlement prices.
Energy imbalances and/or congestion associated with bilateral schedules submitted after the DAM will be settled based upon real-time energy settlement prices.

## Slide 5: DAM Models Comparison
E-HDAM | IDAM
All CRRs default to DAM settlement, but any CRR may be specified for RT settlement | All CRRs settle in DAM
Daily transmission constrained energy auction; reconfiguration auction for PTP Obligations through DAM scheduling (including “up to” congestion bids for transactions); CRR Options only have the alternative of settling in DAM or RT as price takers | Daily transmission constrained energy auction; reconfiguration auction for PTP Obligations through DAM scheduling (including “up to” congestion bids for transactions); CRR Options only have the alternative of settling in DAM as price takers
3-part supply offers accommodated in DAM | 3-part supply offers accommodated in DAM

## Slide 6: E-HDAM vs. IDAM
Only difference is the alternative to specify CRRs to settle in RT
  For PTP Obligations, the RT CRR alternative effectively exists in IDAM by scheduling a transaction in the IDAM that matches the PTP Obligation (see example next slide)
  For PTP Options and/or Flowgates, the RT CRR alternative is unique to E-HDAM and cannot be replicated with DA schedules in the IDAM

## Slide 7: IDAM and E-HDAM Example for Dynamic Schedule with PTP Obligations
Assumptions
QSE A has 100 MW PTP Obligation from A (source) to B (sink)
DAM Price at A is $20, B is $30
RT Price at A is $22, B is $31
QSE A RT Supply at A = 95 MW, RT Demand at B = 95 MW
IDAM
QSE A Schedules 100 MW from A to B in DAM
DAM Congestion Charge = $1,000 [100 MW x $10]
DAM CRR Payment = ($1,000)
RT Supply Imbalance = $110 [5MW x $22]
RT Demand Imbalance = ($155) [5MW x $31]
RT CRR Payment = $0
Net ERCOT Position for QSE A = ($45)
E-HDAM
QSE A Schedules nothing in DAM
DAM Congestion Charge = $0
DAM CRR Payment = $0
RT Supply Imbalance = ($2,090) [95MW x $22]
RT Demand Imbalance = $2,945 [95MW x $31]
RT CRR Payment = ($900) [100MW x $9]
Net ERCOT Position for QSE A = ($45)
Notes: The Net ERCOT Position for QSE A will be identical for IDAM and E-HDAM under any combination of DAM and RT prices
at A or B as long as the 100 MW PTP Obligation is scheduled in the IDAM. Observe that, like in E-HDAM, the 100 MW
PTP OBL is effectively settled in RT even in the IDAM, with the capacity represented by the 100 MW PTP OBL
being “reserved” network capacity in the IDAM (like in the E-HDAM). In the E-HDAM example, it is assumed that the
dynamic schedule is not represented as an ERCOT financial schedule; however, if it were, the supply/demand imbalance
would both be zero, and a RT congestion charge of $855 would be added, thereby still producing the ($45) net position
under the E-HDAM.