## Slide 1: Texas Nodal Market: Settlement of PtP CRR Options
Shams Siddiqi, PhD
TNT General Meeting
February 18, 2004

## Slide 2: Definition
Point-to-Point CRR Option is a Misnomer
  It’s almost impossible to model a true PtP CRR Option (one that pays positive LMP differences between sink and source) in the auction software (see Hogan’s paper)
  The CRR (which we’re calling “PtP CRR Option”) modeled in the auction software is actually a portfolio of rights on transmission elements that are positively impacted by a transaction from the CRR source to sink
  This portfolio of transmission rights ensures that an equivalent transaction from source to sink is hedged against congestion charges but is not exposed to payments if the congestion reverses

## Slide 3: Settlement Issues
LMP differences between sink and source reflects not only positively impacted transmission elements but also any negatively impacted elements
Portfolio of positively impacted elements will never pay less than the LMP differences (absent deration)
Thus, if “PtP CRR Options” are settled on LMP differences, there will never be price convergence between the auction clearing prices and expected payoffs at settlement
If Flowgate Rights are offered, no one would buy “PtP CRR Options” since buying the same portfolio of FGRs would cost the same and yet result in much greater payoff in most cases

## Slide 4: Example
Shadow Prices: T2=$10/MWh and T3=$70/MWh
“PtP CRR Option from 2 to 1” = $23.33/MWh
FGR portfolio from 2 to 1 =$23.33/MWh
“PtP CRR Option from 2 to 1” payoff = $20/MWh
FGR portfolio from 2 to 1 payoff = $23.33/MWh
T1:100 MW
T3:100 MW
T2:60 MW
G1:500 MW@$10/MWh
G2:200 MW@$30/MWh
L3:165 MW G:$60/MWh
LMP1:$10/MWh
LMP2:$30/MWh
LMP3:$60/MWh
Flow3:100 MW
Flow2:60 MW
Flow1:40 MW

## Slide 5: Reasons for Proper Settlement
“PtP CRR Option” should be correctly settled as a portfolio of FGRs consistent with how it’s evaluated in the auction
  PtP CRR Option likely to clear in the auction close to its expected value (Price Convergence)
  Provides greater transparency by publishing LMPs and Shadow Prices and ensuring consistency between them
Settling “PtP CRR Options” on LMP differences is WRONG and would make these rights obsolete if FGRs are offered (see JETRA paper by O’Neill et al)
  Result in paying more for the PtP CRR Option than its expected value (Price Divergence)