## Slide 1: Market Mitigation for the Texas Nodal Design
Shmuel Oren
University of California at Berkeley and Senior Adviser to the PUCT MOD
Presented at the PUCT Technical Workshop on Market Mitigation
Austin, Texas February, 26, 2004

## Slide 2: Why Mitigate
Economic perspective
  Competitive forces work in ideal commodity markets
  Electricity markets have structural flaws that necessitate market power mitigation
Engineering perspective
  Electricity markets represent decentralized/distributed control mechanisms integrated into the traditional command and control power system operations
  Market mitigation can be viewed as corrective actions based on security states of the market

## Slide 3: Why Mitigate The SMD Rationalization
“The development of structurally competitive markets is the Commission's long-term goal. However, at this stage of the industry's evolution, wholesale electric markets are not yet structurally competitive in all respects.”
“The two significant structural flaws are the lack of price-responsive demand and generation concentration in transmission-constrained load pockets. Even in regions where markets are generally competitive, transmission constraints may create non-competitive conditions during certain hours.”
“Given these structural defects, the Commission cannot rely on the interaction of supply and demand in all instances to ensure that prices are competitive and thus just and reasonable.”

## Slide 4: Dealing with Market Imperfection (per SMD)
“When markets do not produce competitive outcomes, the Commission must use new regulatory tools to produce just and reasonable results.”
“We propose new market power mitigation measures to deal with the consequences of major structural defects in wholesale electric markets, by approximating the outcomes that a competitive market would produce.”
“Market mechanisms can be used to approximate the outcomes that a competitive market would produce to provide the price signals for efficient investment and demand response.”

## Slide 5: What is Market Power and What is the Role of Mitigation ( per SMD)
“Market power is the ability to raise price above the competitive level. This can be accomplished if the generator can withhold physical power (physical withholding) or cause physical power to be withheld through inflated bids (economic withholding).”
“Market power can also be exercised by creating barriers to entry so other suppliers cannot reach the market or by causing other supplier's production costs to increase.”
“Market power mitigation needs to mitigate local market power, whether it arises because of a load pocket, transmission constraints, or ownership concentration.”
“To be effective, market power mitigation measures must be applied before the fact, since remedies after the withholding has occurred are disruptive to the market and increase regulatory risk to its participants, which increases costs to customers.”

## Slide 6: Mitigation Mechanisms (per SMD)
Market monitoring and intervention by independent market monitor: “The market monitor will identify certain conditions in which certain generators are in concentrated geographic markets created by transmission congestion or reliability needs of the grid. These would include units needed to run to support the reliable operation of the grid or a set of units owned by a small number of companies. At those times, those units will have localized market power so that when they are required to provide their energy or ancillary services to the grid their bids into the market should be capped”
Safety-net bid cap such as the $1000 per megawatt-hour
Resource adequacy requirement
Automatic Market Mitigation (AMP): “Examining and possibly limiting bids from individual suppliers into the day-ahead and real-time spot markets if those bids are high due to withholding rather than scarcity. Exercise of this mitigation could be triggered by predetermined conditions or triggers (such as a sustained period of prices significantly above competitive levels), or by significant infrastructure problems in the market (e.g., sustained tight reserve conditions, as might be due to drought).”

## Slide 7: DyLiacco System Security States
Normal and Secure State: All load supplied, no operating limits violated, and in the event of a single contingency, there will be no violations or transition from the normal state.
Normal Correctively Secure State: All load supplied; no operating limits violated; any violations caused by a contingency can be corrected by appropriate post-contingency control actions without loss of load.
Alert Insecure State: loads are met; no operating limits violated; some violations caused by a contingency cannot be resolved without loss of load.
Correctable Emergency State: All load supplied; some operating limits are violated that can be corrected by appropriate control actions without loss of load.
Non-Correctable Emergency State: all load supplied; operating limits are violated; but cannot be corrected without loss of load.
Restorative State: No operating limits are violated, but loss of load has occurred.

## Slide 8
State Transition Diagram

## Slide 9: Market Security States
Normal & efficient: Supply offers are greater or equal to demand; Market clears economically without violating physical operating limits; No spikes in prices for energy, A/S, and congestion charges; Market results are posted within market time-lines.
Normal Correctively efficient: Supply offers are greater or equal to demand, Market clears with some appropriate market corrective control actions (uneconomic adjustment, AMP, Residual Unit Commitment, or simply etc.); No spikes in prices for energy, A/S, and congestion charges; Market results are posted within market time-lines.
Alert Inefficient: Supply offers are greater or equal to demand; Market clears with some appropriate market corrective control actions; Spikes in prices for either energy, reserves, or congestion.
Correctable Emergency: Supply offers are insufficient to meet demand; Bids are at very high levels; Under-scheduling of load in DA market; Market clears; Administrative rules are used to clear the market or market results are not posted within market time-lines.
Non-Correctable Emergency: Supply offers are insufficient to meet demand; Bids are at very high prices; Abuses of market power that can NOT be corrected or detected in time; Excessive real-time deviation from DA schedules; Excessive costs incurred to make corrective actions; Frequent violations
Market Collapse: Suspend market; Encourage long terms contracts to reduce the excessive real time deviations; Give right incentives to market participant to add physical resources which will make market more competitive; Market rules re-design

## Slide 10: Market Mitigation Approaches
Structural and Preventative Remedies
  Long Term
    Forced divestiture or mandatory capacity auctions
    Entry and new investment
    Facilitate demand response
    RMR contracts and bid caps on specific generators
    Limits on CRR ownership
  Short term
    Exclusion of noncompetitive constraints from LMP calculation
    Exclusion of generators with local market power from setting prices

## Slide 11: Market Mitigation Approaches
Market Intervention
  Long Term
    Reserves or hedging requirement
    Mandatory vesting contracts
    Offer caps (generator specific and global safety-net caps)
  Short term
    Direct monitoring of market behavior
    Automatic market mitigation
      Setting locational offer caps based on economic dispatch excluding non-competitive constraints (ZEN)
      Directed mitigation based on conduct and impact test applied to individual entities (e.g. NY AMP)
      General mitigation activated by market condition test (e.g. CSM and MCSM)

## Slide 12: Competitive Solution Method (CSM)
Competitive Sufficiency Test
Offer cap when test fails
What it addresses
  Mitigates the price effect of system-wide market power and hockey stick pricing
  Does not affect the mitigation of local market power by other means
  Addresses problems beyond the reach of local market power mitigation

## Slide 13: Competitive Sufficiency Test
Quantity test
  Supply is at least 105% of demand (reduced from 115%)
Pivotal supplier test
  No supplier is pivotal
  Easier to trigger than originally proposed; pivotal supplier need not set the price

## Slide 14: Scenarios and outcomes
 | Sufficient quantity | Insufficient quantity
No pivotal suppler | CSM not activated | Global offer cap imposed (may be overridden by tighter local caps)
Pivotal supplier |  | 

## Slide 15: Determination of offer cap
Price corresponding to 95% of the competitive portion of the offer stack, multiplied by 1.5
  Competitive portion excludes pivotal suppliers who account for more than 5% of total supply
  MCSM is a special case where every offer is pivotal

## Slide 16: Scarcity proxy under CSM
95% of offer stack
cap
cap

## Slide 17: Scarcity proxy under CSM
95% of offer stack
Cap: $257

## Slide 18: Conclusions
Market power mitigation is a necessary evil that is required in order to achieve market credibility and stability
Structural remedies may not be sufficiently responsive to temporary market failure conditions that may have devastating impact over short time periods
Market intervention must strike a fine balance between suppressing scarcity rents that are needed to stimulate investment and entry and preventing price gauging
Market mitigation must be addressed in conjunctions with mechanisms that will allow prices to reflect legitimate scarcity rents and with mechanisms for generation adequacy assurance