## Slide 1: Texas Nodal Market: Market Mitigation Policies
Shams Siddiqi, PhD
shams@crescentpower.net
PUCT Market Mitigation Workshop
February 26, 2004

## Slide 2: Outline
Mitigation Needs Identified so far:
  Real-time Market: Locational Market Power Mitigation
  Day-ahead Reliability Unit Commitment related Mitigation
  CRR Market related Mitigation
  Day-ahead Energy Market related Mitigation
Market Monitoring at ERCOT

## Slide 3: R-T: Locational Market Power Mitigation
Constraints that can’t be competitively resolved lead to locational market power
Market power can be exercised through either price gouging (economic or physical withholding) or predatory pricing (dumping)
Locational market power mitigation must tradeoff between price signal and unjustified transfer of wealth from customers

## Slide 4: Proposed R-T Mitigation for Texas
Competitive Constraints are annually determined based on Competitive Test but may become Non-competitive any time they fail the following Competitive Test:
  HHI < limit - test based on “Effective Capacity” ownership percentages
  No Pivotal Player in resolving the constraint
Not submitting an offer is treated as offering at infinity for up and negative infinity for down and is subject to the same mitigation treatment as all other offers
Competitive Constraints: No mitigation (except $1000/MWh cap and -$1000/MWh floor)
Non-Competitive Constraints: Offer cap (say 16*Nat. Gas price) for all units and technology-specific offer floors (e.g. -$20/MWh for Coal units) for the units’ energy above their minimum loading amount plus capacity providing Regulation Down

## Slide 5: Proposed R-T Mitigation for Texas
Step 1: System is optimally dispatched with Competitive Constraints modeled with no mitigation: this run provides nodal “Reference Prices” that are used to possibly enlarge the mitigation cap and floors
Step 2: System is then optimally dispatched with mitigated bids and all Constraints modeled (SCED) to determine LMPs and dispatch instructions
Note: If no Non-competitive Constraint is binding, then results of 2nd Step is the same as that of 1st Step. Thus, any change in 2nd Step from 1st Step is due to need to resolve Non-competitive Constraints and so is resolved using mitigated offer curves. [No need to identify specific resources that need to be mitigated for particular Non-competitive Constraints under this method.]

## Slide 6: Proposed Texas Bid Mitigation - 1
Price ($/MWh)
Bid Cap
Bid Floor
Nodal Price from 1st Run
Bid Curve
Quantity (MWh)
Mitigated Bid Curve

## Slide 7: Proposed Texas Bid Mitigation - 2
Price ($/MWh)
Bid Cap
Bid Floor
Nodal Price from 1st Run
Bid Curve
Quantity (MWh)
Mitigated Bid Curve

## Slide 8: Proposed Texas Bid Mitigation - 3
Price ($/MWh)
Bid Cap
Bid Floor
Nodal Price from 1st Run
Bid Curve
Quantity (MWh)
Mitigated Bid Curve

## Slide 9: Proposed Texas Bid Mitigation - 4
Price ($/MWh)
Bid Cap
Bid Floor
Nodal Price from 1st Run
Bid Curve
Quantity (MWh)
Mitigated Bid Curve

## Slide 10: R-T MM: Allows for Scarcity Prices
SCED with Competitive Constraints only (Step 1) to determine nodal Reference Prices that are used to possibly enlarge the mitigation caps and floors so as to not mitigate against true scarcity
Thus, Proposed Mitigation policy distinguishes between high prices due to true scarcity (not mitigated) and high prices due to manipulation (mitigated) and between low prices due to market glut (not mitigated) and low prices due to intentional or unintentional dumping (mitigated)
Offer floors also mitigate against the “Dec Game” arising from oversold CRRs on Non-competitive Constraints

## Slide 11: Proposed Texas R-T Mitigation: Pros
Ex ante structural locational market power mitigation with clearly defined Competitive (Unmitigated) & Non-Competitive (Mitigated) Constraints
Does not mitigate high prices due to true scarcity
Does not allow ERCOT to Arbitrarily mitigate prices based on changes in bidding behavior
Does not require explicit identification of “Out-of-merit” Resources that are required to resolve Non-competitive Constraints

## Slide 12: Day-Ahead RUC: Need for Mitigation
Mitigation of D-A RUC needed for:
  Minimizing the “Uplift Game”
    By having ERCOT commit the Resource through D-A RUC instead of self-committing, the uplifted start-up and no-load costs are paid for by all short load instead of being reflected in higher local LMPs
  Controlling Locational Market Power Abuse
    Similar to R-T energy market, Resources with locational market power can offer high (economic withholding) or not offer (physical withholding) for exorbitant returns

## Slide 13: Proposed RUC Mitigation for Texas
RUC Start-up Cost and Minimum-energy Cost offers are capped
  Technology-specific offer caps or verifiable cost plus 10%
RUC Resources’ energy bids are capped for “make-whole” payment determination purposes only
  If LMP at Resource node is greater than Resource’s capped energy bid, this difference multiplied by Resource’s output is applied towards reducing uplifted “make-whole” payments
RUC Resources are guarantied full cost recovery plus at least 10% profit but have limited potential for greater profits (no risk, minimal gain)
Self-committed Resources are not guarantied any cost recovery but have greater potential for profits
Thus, Proposed Mitigation provides incentive to self-commit thereby having the potential to reduce uplifted costs

## Slide 14: CRR Market: Need for Mitigation
CRR ownership exacerbate locational market power
  Refer to Joskow and Tirole (2000) for detailed explanation of this problem
  Market power can be exercised in two ways:
    Withholding (economic or physical) to increase profits
    Dumping or predatory pricing to eliminate competition
Oversold CRRs (due to unexpected outages) can lead to the “Dec Game”
  Concerns about the “Dec Game” in the current market design is what has led us to re-design this market

## Slide 15: Local Mitigation: Need in Load Pocket
G2’s income greatly increased due to CRR ownership
  G2’s energy revenue = $1000/MWh x 50MWh = $50,000
  G2’s FTR revenue = $980/MWh x 100MWh = $98,000
CRRs ownership enhances incentives to exercise market power (see Joskow and Tirole (2000))
T:100 MW
G1:500 MW@$20/MWh
G2:200MW@$50/MWh
L2:150 MW
CRR:100 MW
G2: If I bid $1000/MWh, not only do I make money on energy but also get paid more for my CRRs!

## Slide 16: Local Mitigation: Need in Gen. Pocket
If G1 bids its marginal cost of $20/MWh (=LMP1)
  G1’s revenue = $20/MWh x 50MWh (for energy) + $30/MWh x 100MWh (for CRRs) = $4,000: Some uplift
If G1 bids -$1000/MWh (=LMP1) [“Dec Game”]
  G1’s revenue= -$1000/MWh x 50MWh (for energy)+ $1050/MWh x 100MWh (for CRRs) = $55,000: Outrageous profits & uplift!
T:50 MW
G1:110 MW@$20/MWh
G2:200MW@$50/MWh
L2:150 MW
CRR:100 MW
G1: Local line is derated to 50MW and ISO doesn’t derate CRRs, time to make serious money!

## Slide 17: TNT Decisions Regarding CRRs
No ownership limits on CRRs held at any given time. However, this condition is subject to development of market monitoring and business rules that govern the use of CRRs.
Uplift any shortfall of CRR revenues to CRR holders on a pro-rata basis. (Surpluses and shortfalls will be held in a balancing account to balance out over a calendar period.)

## Slide 18: CRR Market Mitigation for Texas
With uplifting of CRR revenue shortfall due to oversold CRRs, the “Dec Game” must be mitigated
Applying offer floors can mitigate the “Dec Game” – essentially CRR holders would be insuring each other against network deration and reasonable costs incurred but not allowing exorbitant profits from offering at very low prices
Mitigation caps and floors applied to offers needed to resolve all Non-competitive Constraints also serve the purpose of mitigating the exacerbated market power situation for these Non-competitive Constraints

## Slide 19: Example of Offer Floors
Technology | Offer Floor | Avg. Marg. Cost
Nuclear, Hydro | -$1000/MWh | $0 to $5/MWh
Coal | -$20MWh | $15/MWh
Combined Cycle | 1HR*FIP=$5 | 7HR*FIP=$35
Gas Steam | 6HR*FIP=$30 | 11HR*FIP=$55
QF, Wind | -$250/MWh | -$30 to $30/MWh

## Slide 20: Day-Ahead Energy Market
No Mitigation Required for the Auction DAM
  Willing buyers and sellers cleared at each Settlement Point; thus bidding at a Load Zone does not result in local market power issues
  All CRRs cleared in real-time: No interaction between CRRs and virtual bids
  No need to place limitations (from a mitigation perspective – credit issues remain) on virtual bidding
Mitigation for E-HDAM needs to be developed
  Local market power issues – can Resources that do not bid be forced into DAM and mitigated?
  Start-up and Min-energy capped as in RUC?
  Energy offers mitigated similar to real-time market?
  Mitigation of virtual bidding to influence CRR values?

## Slide 21: Other Mitigation Needs
Ancillary Services Market
Tight unconstrained market: Scarcity or Market Failure requiring mitigation?
Resource Adequacy Market
Others

## Slide 22: Market Monitoring at ERCOT
Independent market monitoring function within ERCOT
PUCT MOD would work with Independent Market Monitor (IMM)
  MOD would continue to initiate complaints, investigations, or take appropriate enforcement action
  IMM would provide periodic reports to MOD on activity the warrants further investigation
Director of IMM will report to a three member Board of Directors Subcommittee comprised of the independent Board members which will have administrative authority over the Director
The Market Monitoring Group will rigorously review market participants for items such as:
  Operations significantly inconsistent with ERCOT dispatch instructions
  Outages of transmission or generation that appear excessive or unusual
  Prohibited behaviors
  Deviations from TDSP construction, maintenance and outage scheduling practices
  Other unusual behavior

## Slide 23: Market Monitoring at ERCOT
IMM will contact respective market participants to get their perspective on detected unusual bids or operational behaviors
IMM will review the performance of ERCOT operations to ensure that ERCOT practices and produces are consistent with the Protocols
IMM will also perform the function of verifying the behavior of TDSPs in setting transmission limits (parameters) and requests for outages of lines, transformers and busses that have major impacts on LMPs. When significant changes in LMPs are observed, IMM shall investigate them to make sure such changes were consistent with good utility practices.
Any unresolved market participant bidding or operational behavior or ERCOT non-compliance will be referred to the PUC Market Oversight Division for enforcement or correction
The Market Monitor will publish an annual “State of the Market Report” assessing the competitiveness of the market and suggested changes