| OGRR Number | 142OGRR | OGRR Title | DOE and NERC Reporting |
| --- | --- | --- | --- |
| Operating Guide Section Requiring Revision | 3.1.3.4, QSE Responsibility for Department of Energy (DOE) and NERC Reportable Events [new] 3.1.5.1, Disturbance Reporting 2.1, Operational Duties |
| Protocol Section Revised | N/A |
| Proposed Effective Date | April 1, 2004 |
| Revision Description | Changes the reporting processes by having TDSPs and QSEs provide required disturbance data for DOE/NERC reportable events to the ERCOT Control Area Authority, who will distribute the report to the DOE and NERC. |
| Benefit | Clarification of the Operating Guide’s DOE / NERC reporting requirements. Adds QSE reporting requirement. ERCOT, as the Control Area Authority, should be the reporting Entity for DOE/NERC events. |
| OWG Recommendation | OWG recommends approval of OGRR142 as revised by OGRTF comments. |
| ROS Recommendation | ROS recommends approval of OGRR142 as recommended by OWG. |
| TAC Action | TAC approved OGRR142 as recommended by ROS. |

| Sponsor |
| --- |
| Name | Rick Keetch, on behalf of the OWG |
| E-mail Address | rkeetch@reliant.com |
| Company | Reliant Energy |
| Company Address | P.O. Box 1700, Houston, TX 77251 |
| Phone Number | (713) 497-2526 |
| Fax Number | (713) 497-9720 |

Proposed Operating Guides Revision

      - QSE Responsibility for Department of Energy (DOE) and NERC Reportable Events

QSEs shall provide ERCOT with the DOE Form EIA-417 report for each DOE reportable event that happens in areas they represent.  ERCOT, as the Control Area Authority, will forward these reports to the DOE and NERC as required.

#### 3.1.5.1	 Transmission Operator Responsibility for Department of Energy (DOE) and NERC Reportable Events

TOs shall provide ERCOT with the DOE Form EIA-417 report for each DOE reportable event that happens in areas they represent.  ERCOT, as the Control Area Authority, will forward these reports to the DOE and NERC as required.

## 2.1	Operational Duties

| CONTROL AREA AUTHORITY RESPONSIBILITY | CONTROL AREA AUTHORITY ACTION |
| --- | --- |
| Ensure the reliability of the ERCOT Transmission Grid in accordance with North American Electric Reliability Council/ERCOT reliability guidelines. | Evaluate ERCOT Transmission Grid conditions on a continuous basis. Oversee operation of the ERCOT Transmission Grid and act as the ERCOT Control Area Authority. Serve as the point of contact for initiation of generation interconnection to the transmission system. Implement Congestion Management of the ERCOT Transmission Grid on a nondiscriminatory basis. Coordinate all planned outages of transmission system facilities. Schedule ERCOT Interchange transactions across the DC Ties. Deploy Ancillary Services Compile a detailed operations plan to ensure that sufficient resources and required Ancillary Services have been provided for all expected load and transactions within the ERCOT Region. Forecast the actual load, generation dispatch and transmission system operations for the next seven days and update available transmission capacity (TTC), as necessary. Adjust resources in accordance with the ERCOT Protocols as needed to maintain ERCOT in a secure operating condition and meet NERC control performance requirements. |
| Supervise the ERCOT System operational transmission planning | Perform operational transmission system security studies, including those related to generation and load interconnection responsibilities. Review outages of generating units and major transmission lines to identify constraints that may affect transfers. Perform load flows and security analyses of planned outages submitted by TDSPs as a basis for approval or rejection. Withdraw approval of a scheduled Transmission Facility Maintenance Outage if unable to meet the applicable reliability standards even if all other reasonable options are exercised. |
| Collect and disseminate information | Provide appropriate operational information to individual QSEs and TDSPs. Provide relevant operational information to Market Participants over the ERCOT Market Information System. Collect and maintain Control Area Authority operational data required by the PUCT. Receive reports from TOs and QSEs and forward them to DOE and/or NERC as required. Submit Reliability Coordinator reports to DOE and/or NERC as required. Record and report accumulated time error. |

| OGRR Evaluation |
| --- |
| Non-ERCOT Market Comparison | No Comparison conducted. |
| Comments Author | Comments Summary |
| OGRTF | Revised language. |

| Sponsor's Revision Description | Changes the reporting processes by having TDSPs and QSEs provide required disturbance data for DOE/NERC reportable events to the ERCOT Control Area Authority, who will distribute the report to the DOE and NERC. |
| --- | --- |
| Sponsor's Reason for Revision | Clarification of the Operating Guide’s DOE / NERC reporting requirements. Adds QSE reporting requirement. ERCOT, as the Control Area Authority, should be the reporting Entity for DOE/NERC events. |