## Slide 1: Update of the IDR Threshold Analysis with UFE Impact
Presented by:
Carl Raish
Lindsey Turns

## Slide 2: Introduction
This is a report of Ercot’s Phase 2 analysis of the IDR requirement
The purpose of the analysis was to include the impact of UFE allocation in the calculation of error associated with the use of profiles vs. use of IDRs

## Slide 3
METHODOLOGY

## Slide 4: Methodology Profiling Error
Profiling Error illustrates whether the profile overestimates or underestimates the true usage. The formula is:
where PE = Profiling Error (kWh) for a premise,
Eiactual= Actual Energy (kWh) for a 15-minute interval, and
Eiprofiled = Profiled Energy (kWh) for a
15-minute interval.

## Slide 5: Methodology UFE Adjustment
UFE (unaccounted for energy) is computed as follows:
UFE = Generation – (Load at Meter + Losses)
Allocation of UFE varies by interval
  ~ 85% to profiled load
  ~ 15% to IDR load
  None is allocated to NOIE load
Shifting load from a profile to an IDR eliminates Profiling Error for those ESI IDs
Shifting load from an IDR to a profile creates Profiling Error for those ESI IDs
In either case UFE in total or as a percent may increase or decrease

## Slide 6: Methodology UFE Adjustment Factor
Each interval of profiled load is multiplied by an adjustment factor to account for UFE:
If IDRs are shifted to profiles or vice versa, both profiled load and UFE are affected:

## Slide 7: Methodology UFE Adjustment Factor
Based on the incremental load and UFE a new adjustment factor is computed:
The New Adjustment factor is a function of the IDR threshold since the Incremental UFE is the net profiling error for all ESI IDs meeting the IDR threshold

## Slide 8: Methodology Adjusted Profiling Error
The profiled version of the IDR load is multiplied by this
factor to replicate the data aggregation process. The
adjusted load is compared to the actual interval data to
determine adjusted profiling error.
where Adj PE = Adjusted Profiling Error (kWh) for a premise,
Eiactual= Actual Energy (kWh) for a 15-minute interval
New Adj Factor = New UFE Adjustment Factor
Eiprofiled = Profiled Energy (kWh) for a
15-minute interval.

## Slide 9: Estimates for IDR Costs
  ERCOT estimated the annualized
  incremental cost of IDR metering using
  the following assumptions:
  IDR Purchase/Installation $1000
  Annual Reading Cost $72
  Amortization Period 15 years
  Interest Rate 5.0%
  Annualized IDR Cost $168

## Slide 10
RESULTS

## Slide 11: Voluntary Removal Threshold
ERCOT analyzed the impact of establishing a demand threshold below which IDRs could be voluntarily removed

## Slide 12: Voluntary Removal Net Profiling Error Cost

## Slide 13: Voluntary Removal Net Profiling Error Cost Adjusted for UFE

## Slide 14: Voluntary Removal Net Profiling Error Adjusted for UFE All IDRs 0 kW to 500 kW

## Slide 15: Distribution of Net Profiling Error Adjusted for UFE

## Slide 16: Voluntary Removal Cross Customer Error

## Slide 17: Voluntary Removal Cross Customer Error Adjusted for UFE All IDRs 0 kW to 500 kW

## Slide 18: Tariff Savings for Premises which Benefit by Removing IDR Meter

## Slide 19: Voluntary Removal Profiling Error Summary of IDRs with Lower Tariff Charges

## Slide 20: Voluntary Removal Cumulative Cross Customer Error of IDRs with Lower Tariff Charges

## Slide 21: Mandatory Installation Threshold
ERCOT considered lowering the threshold required for installation

## Slide 22: Mandatory Installation Cross Customer Error Per IDR

## Slide 23: Mandatory Installation Cross Customer Error

## Slide 24: Mandatory Installation Number of IDRs that would be Required

## Slide 25: Mandatory Installation Cross Customer Error Adjusted for UFE All NIDRs 100 kW to 1000 kW

## Slide 26: Mandatory Installation Cumulative Cross Customer Error Adjusted for UFE - All NIDRs 100 kW to 1000 kW

## Slide 27: ERCOT Recommendations
Initially set IDR threshold at 700 kW
  988 IDRs would need installation
  Cross Customer Error reduction ~ $2 million per year
Optional removal below 150 kW
  615 premises impacted however likely that only 271 would experience tariff reductions
  TDSP tariff reductions ~ $646/premise
  ~ $229 Cross Customer Error introduced

## Slide 28: ERCOT Recommendations Additional Research
Analyze benefits of a mandatory TOU provision
Analyze load research data to refine estimates particularly in 100 kW to 700 kW range

## Slide 29: CR Impact with IDR Removal All IDRs 0 kW to 500 kW

## Slide 30: CR Impact with IDR Installation All IDRs 100 kW to 1000 kW
*NPEC not extrapolated to the population level