## Slide 1: May 2004 Resource Plan Pilot Metrics Report For QSE Project Managers ERCOT Compliance June 8, 2004 Scores Calculated Using Common Measures Developed With ERCOT Market Operations and QSE Project Managers. Contact ERCOT Client Reps for further information, data behind any of the scores, and/or comments. This is a work in progress and information is subject to change upon further review.

## Slide 2: Resource Plan Pilot Metrics Report: PRR520
PRR was posted on Monday, May 24, 2004.
Several Comments Have Been Received
  Treatment of Combined Cycle Plants as a Single Unit for the Resource LSL As a % of HSL Measure.
  Reasoning for exclusion of LAARs and Renewable Generation Resources for the Resource Status Measure.
  Possibility of HOLs being used to determine Regulation Up and Responsive Reserve Availability instead of HSLs.
In the meantime, continue identifying issues for QSEs less than 90%. A majority of the issues with the Metrics have been resolved in the past few months. Other issues are still being worked on.

## Slide 3
The Zonal approach is being abandoned because of Down Regulation, which cannot be assessed Zonally. We are going with an ERCOT-wide approach. The negative impact is that failure to bid enough in one Zone could cause a failure for the entire hour.
PRR501 addresses concerns about including Down Regulation Scheduled in the calculation of the Mandatory Down Balancing Bid. This PRR also addresses concerns about units receiving an OOMC instruction. Should Units under Test have to bid Down Balancing? Remanded by TAC to the PRS for discussion at the June 24th PRS meeting.
Resource Plan Pilot Metrics Report: DRAFT Down Bid & Obligation Issues

## Slide 4
This hourly measure has two functions:
  Determines whether Mandatory Balancing Down-Bids are provided for the entire ERCOT grid, and
  Compares Resource Plan Aggregated Low Sustainable Limit to the Sum of the Resource Plan Aggregated Planned MW Output, Down Regulation, and Down Balancing Bid.
Based on final RP (end of AP).
Exceptions:
  Units providing RMR Service and Units receiving an OOMC instruction for a given hour are excluded from having to bid Down Balancing.
The Mandatory Down Balancing Bid is calculated ERCOT-wide as follows:
  (RP Plan MW – Down Reg Sch – RP LSL) if
    (RP Plan MW – Down Reg Sch – RP LSL) ≥ 0 AND
    (RP Plan MW – Down Reg Sch – RP LSL) < (RP Plan MW * Posted DB %)
  (RP Plan MW * Posted DB %) if
    (RP Plan MW – Down Reg Sch – RP LSL) < 0 OR
    (RP Plan MW – Down Reg Sch – RP LSL) ≥ (RP Plan MW * Posted DB %)
Resource Plan Pilot Metrics Report: DRAFT Down Bid & Obligation ERCOT

## Slide 5
An occurrence is counted when the following conditions are met:
  (RP LSL + Reg Dn Sch + Mand Down Bid – RP Plan MW) > 1 MW
  (Mandatory Down Bid - Down Balancing Bid) > 1 MW
The overall QSE score is calculated as follows:
Resource Plan Pilot Metrics Report: DRAFT Down Bid & Obligation ERCOT

## Slide 6
Resource Plan Pilot Metrics Report: DRAFT Down Bid & Obligation ERCOT

## Slide 7
This hourly measure has two functions:
  Determines whether Mandatory Balancing Down-Bids are provided for the entire ERCOT grid, and
  Compares Resource Plan Aggregated Low Sustainable Limit to the Sum of the Resource Plan Aggregated Planned MW Output, Down Regulation, and Down Balancing Bid.
Based on final RP (end of AP).
Exceptions:
  Units providing RMR Service and Units receiving an OOMC instruction for a given hour are excluded from having to bid Down Balancing.
First, Mandatory Down Balancing Bids are calculated by Zone as follows:
  DBbid Zonal = Max[0, Min(Σ RP PlanMW * Posted DB %, Σ RP PlanMW – ΣRP LSL)]
Then, the aggregate Mandatory Down Balancing Bid for all Zones is calculated as follows:
  MandDownBid = Max[0, Min(Σ(DBbid Zonal), RP PlanMW – DownRegSch – RP LSL)]
This last calculation gives us the mandatory down balancing bid required ERCOT-wide.
Resource Plan Pilot Metrics Report: DRAFT Down Bid & Obligation Revised

## Slide 8
The change in the calculation of the Mandatory Down Balancing Bid increased the score of several QSEs and did not have an effect on the other QSEs.
An occurrence is counted when the following conditions are met:
  (RP LSL + Reg Dn Sch + Mand Down Bid – RP Plan MW) > 1 MW
  (Mandatory Down Bid - Down Balancing Bid) > 1 MW
The overall QSE score is calculated as follows:
Resource Plan Pilot Metrics Report: DRAFT Down Bid & Obligation Revised

## Slide 9: Resource Plan Pilot Metrics Report: Resource Status
Compares hourly Resource Plan status to telemetry. 12 telemetry values are used, an average over 5 minutes, for each Resource in the Resource Plan.
Exceptions:
  Combined Cycle Trains approved by ERCOT are treated as if they were single units.
  LAARs, Units that do not have to provide telemetry, Non-Commercial Units, and Units of type “Renewable” are excluded.
An occurrence is counted when either of the following conditions are met:
  RP Status Flag = “Offline” AND all 12 telemetry values > 0.5 MW
  Resource Plan MW > 0 MW AND all 12 telemetry values < 0.5 MW
Each QSE’s Resource with telemetry is evaluated each hour of the month. The overall QSE score is calculated as follows:

## Slide 10: Resource Plan Pilot Metrics Report: Resource Status

## Slide 11: Resource Plan Pilot Metrics Report: Resource LSL As a % of HSL
Reviews minimum and maximum sustainable limits for each Resource listed as “online” in the Resource Plan each hour. Utilizes the Unit Type for each Resource provided on the Asset Registration Form. This measure only looks at the Resource Plan.
Cogenerators will no longer be an exception beginning with the June Scores.
Exceptions:
  Hydros, Renewables, Cogenerators, and LAARs are excluded.
An occurrence is counted when:
  RP Low Sustainable Limit > (Defined % * RP High Sustainable Limit)
  RP High Sustainable Limit > 0 MW
The overall QSE score is calculated as follows:

## Slide 12
Unit types in the Protocols, Section 6.8.2.1, item 1 are as follows with percentages used in red:
  Nuclear 70%
  Hydro N/A
  Coal and Lignite 60%
  Combined Cycle greater than 90 MW 85%
  Combined Cycle less than or equal to 90 MW 85%
  Gas-Steam Supercritical Boiler 40%
  Gas-Steam Reheat Boiler 40%
  Gas-Steam Non-reheat or boiler without air-preheater 40%
  Simple Cycle greater than 90 MW 90%
  Simple Cycle less than or equal to 90 MW 90%
  Diesel (and all other diesel or gas-fired Resources) 90%
  Renewable (i.e., non-Hydro renewable Resources) N/A
  Block Load Transfer N/A
Resource Plan Pilot Metrics Report: Resource LSL As a % of HSL

## Slide 13: Resource Plan Pilot Metrics Report: Resource LSL As a % of HSL

## Slide 14: Resource Plan Pilot Metrics Report: DA Zonal Energy Schedule (2.0%)
Compares hourly Resource Plan MW to the Schedule by Zone. This measure uses Day Ahead data. Duplicate data has been removed. Only data from the first approved Resource Plan Validation has been used.
PRR404 allows Scheduling from the Balancing Energy Market (ERCOT). This should not affect this measure.
An occurrence is counted when:
  (RP Zonal MW – Zonal Schedule) > 2% * Zonal Schedule
  (RP Zonal MW – Zonal Schedule) > 1 MW
The overall QSE score is calculated as follows:

## Slide 15: Resource Plan Pilot Metrics Report: DA Zonal Energy Schedule (2.0%)

## Slide 16: Resource Plan Pilot Metrics Report: AP Zonal Energy Schedule (2.0%)
Compares hourly Resource Plan MW of all Units to the Average Hourly Schedule by Zone.
PRR404 allows Scheduling from the Balancing Energy Market (ERCOT). This should not affect this measure.
An occurrence is counted when:
  (RP Zonal MW – Zonal Schedule) > 2% * Zonal Schedule
  (RP Zonal MW – Zonal Schedule) > 1 MW
The overall QSE score is calculated as follows:

## Slide 17
Resource Plan Pilot Metrics Report: AP Zonal Energy Schedule (2.0%)

## Slide 18: Resource Plan Pilot Metrics Report: Total Up AS Scheduled Obligation
Compares QSE Resource Plan Aggregated High Sustainable Limit for each interval to the Sum of the Schedule, Up Regulation, Responsive Reserve, Non Spin, and Up Balancing Deployed. Schedule and AS awards for increased MW output is the “obligation”.
Based on final RP (end of the AP). Uses SPD output, so telemetry at time of balancing deployment is used.
An occurrence is counted when:
  (Obligation – Aggregated HSL) > 1 MW
  Up Regulation + Responsive Reserve + Non Spin > 0 MW
The overall QSE score is calculated as follows:

## Slide 19: Resource Plan Pilot Metrics Report: Total Up AS Scheduled Obligation

## Slide 20
Proposed Appeals and Exclusions
Scores below 90% will be reviewed with the QSE to identify the cause.
The review process will begin with ERCOT providing notification of scores and the intervals with occurrences to the QSE, who will then have ten (10) business days to review the data and provide an explanation of the cause.
If ERCOT agrees that the cause is due to scheduling or operational conditions not adequately assessed by the metrics, or questionable data, then no further response from the QSE will be expected.
ERCOT will adjust the scoring to the extent possible and provide the QSE’s explanation to the PUCT.
If the QSE cannot provide such a basis for performance, ERCOT will conclude that the QSE did not make the necessary internal efforts to provide accurate resource plans during that month and send the QSE a notice of non-compliance.
An additional ten (10) business day period will be allowed for further response or supply of QSE mitigation plans before closing the matter.
Final QSE responses will be forwarded to the PUCT along with scores. Non-performance of this nature is subject to public posting and if recurrent during a rolling six (6) -month period, other enforcement actions may be applied.

## Slide 21: Resource Plan Pilot Metrics Report: Action Items
Obtain individual cogenerator minimum capability as a % of maximum capability. Letters were sent to all QSEs with cogenerators on Monday, April 26, 2004 requesting percentages by June 1, 2004. Have received responses from all QSEs but two (2).
Request justification from QSEs if 100% is sent in as the percentage to use for their cogenerators in the Resource LSL as a % of HSL Measure.