Disconnect Reconnect Process Guide

May 07, 2004

Version 1.0

Table of Contents

I. Purpose	4

II. Definitions and Acronyms	4

III. Assumptions and Market Processes	6

A. REP Certification	6

B.  Forecasts	6

C. Service Order Dispatching	6

D. Safety Nets	6

IV. Process Overview	7

A.  Disconnect Process Overview	7

B. Reconnect Process Overview	7

V. Transaction Processing	8

A. Timelines for Transaction Delivery	8

i. Disconnect	8

ii. Reconnect	8

B. Transaction Validations	9

i. REP validations prior to initiating 650_01	9

ii. TDSP validations upon receipt of 650_01	9

C. Competing Orders	10

i. Move In	10

ii. Off-cycle Switch	10

iii.  On-cycle Switch	11

D. Reconnect/Disconnect Processing Order	11

E. Disconnection at Alternate Location	12

F. Completed Unexecutable and Rejected Orders	12

G. Priority Orders	13

H. Service order cancellations	14

I. Response Transactions	14

VI. Field Service Activities	15

A. Disconnection Service Orders	15

B. Reconnection Service Orders	17

C. Requirements for reconnecting service	18

D. Customer receipting issue	19

E. Premise access issues	19

F. Door Hanger Policies	19

G.  Meter Seal Policies for Disconnection	20

VII. Exceptions	20

A. Emergency reconnects	20

B. Critical Load	21

C. Critical Care	22

D. Weather Moratoriums	22

i. Disconnection Activity During Extreme Weather	23

ii. Reconnection Activity During Extreme Weather	24

E. Force Majeure	24

F. Master Metered Premises	25

G. Unmetered Service	25

H. Multiple Metered Service (not Master Metered)	26

I. Meter Tampering Issues	26

J. Customer Threatens TDSP FSR	27

VIII. TDSP Charges for Reconnect and Disconnect Services	28

A. Discretionary Charges	28

B. Other Charges	29

C. TDSP Tariffs	29

IX. Contacts	30

A. Emergency System Outage	30

B. Disconnect Forecast Contact	30

C. Website available information	30

D. TDSP general call center phone number	31

X. List of Tables	31

Table 1. Competing Orders- Move-In	31

Table 2. Competing Orders-Off-cycle Switch	31

Table 3. Competing Orders- On-cycle Switch	31

Table 4. Transaction Processing Order	31

Table 5. TDSP Priority Codes	31

Table 6. Field Service Hours-Disconnect	31

Table 7. REP timelines for submitting reconnect request	31

Table 8. Field Service Hours-Reconnection	31

Table 9. Door Hanger Use by TDSP	31

Table 10. Extreme weather emergency due to cold	31

Table 11.  Extreme weather emergency due to heat	31

Table 12. SAC04 Codes-Discretionary Charges	31

XI. Appendices	31

Appendix 1-Weekly REP Disconnect for Non-Payment Forecast	31

Appendix 2-Emergency Reconnect Request- Data Requirements	31

Appendix 3-TNMP Weather Zone Zip Codes	31

# I. Purpose

The purpose of this Disconnect Reconnect Process Guide is to provide market participants with a document that defines market processing for disconnection and reconnection requests and for managing emergency and contingency procedures in support of disconnection for nonpayment and reconnection activities.

# II. Definitions and Acronyms

Complete   Action code on the 650_02 indicating that the service request for either disconnect or reconnect activity has been successfully completed in the field by the field service representative (FSR).

Complete Unexecutable   Action code on the 650_02 indicating that the FSR was unable to successfully complete the service request for either disconnection or reconnection due to conditions at the customer’s premise outside of the TDSP’s control.

This action code may also be used in the 650_02 for disconnection requests when the TDSP has received a reconnect service request prior to completing the disconnect request.

Pending    Any order that is received prior to the requested completion date.

Overflow   Service order requests not worked on the date wanted due to events such as outages, extreme weather, or an increased volume of higher priority service request types (Reconnects, MVIs, MVOs).  These overflow service requests will be scheduled for the next available field operational day until the order is successfully completed or completed unexecutable.

Service Order Request   The Texas SET 650_01 issued from the CR to TDSPs requesting field work.

Service Request   Same as above.

Business Day   8:00 AM to 5:00 PM CPT Monday through Friday excluding observed company holidays, as outlined on the TDSP websites.

Field Operational Day    The normal hours of operation for field services at the TDSP. Refer to section VI. Field Service Activities.

Collection Day   The hours of operation for collection and payment services at the REP.

Acronyms included in this document

ANSI		American National Standards Institute

CPT		Central Prevailing Time

CR		Competitive Retailer

DNP		Disconnect for Non-Pay

ESI ID		Electric Service Identifier

FSR		Field Service Representative

MVI		Move-In

MVO		Move-Out

PUCT		Public Utility Commission of Texas

REP		Retail Electric Provider

ROR		REP of Record

RNP		Reconnect for Non-Pay

TDSP		Transmission Distribution Service Provider

Processes for the following TDSPs are included in this document. Some of these TDSPs are identified by an acronym. These are identified below.

AEP		American Electric Power

CNP		Centerpoint

Entergy	No acronym

Oncor		No acronym

SULP		Sharyland Utilities, L.P

TNMP		Texas New Mexico Power

# III. Assumptions and Market Processes

## A. REP Certification

Prior to issuing 650_01 for disconnect/reconnect, certified CRs shall have successfully completed market certification testing and have received disconnection authority from the PUCT.

## B.  Forecasts

CRs will provide to the TDSPs on a weekly basis the number of disconnection requests that they estimate will be issued.  This will be an Excel spreadsheet reporting the total number of disconnects expected for the next week with the report showing the range of disconnects for each day of that week. Please refer to Appendix 1 for the REP forecast template. These forecast spreadsheets will be emailed to the designated TDSP contact listed in section IX. B. of this guide on the Tuesday of the week before that week’s activity would begin.  The data submitted by CRs in these forecast spreadsheets is confidential and intended to be an estimate only that will allow TDSPs to plan and allocate resources in order to complete disconnect and subsequent reconnect service orders.

## C. Service Order Dispatching

In order to efficiently manage all types of service requests, field service orders are dispatched in accordance to their respective priority by geographic area.

Below are the field execution priorities associated with each TDSP:

Priority One:  Priority and Routine Move-Ins, Priority and Routine Reconnects, Off Cycle Reads for Switches, Move-Outs (CNP only)

Priority Two:  Move-Outs (except CNP), DNP, Investigation Orders, Re-Read and Maintenance Requests

## D. Safety Nets

Disconnects received prior to safety nets will be completed as will the subsequent safety net requests.  If a safety net Move In has been received and completed by Oncor for a new REP of Record, a force Move-Out will be created for the previous REP of Record.  Any subsequent disconnect or Move Out request issued from the previous CR will be rejected upon receipt as not Rep of Record by Oncor.

For all other TDSPs, if a safety net Move-In has been received and completed for a new REP of Record, but the supporting EDI transaction has not been received, any subsequent disconnect or move-out requests received by the TDSP will be completed.

Safety Net processing will be reviewed following TX SET 2.0 implementation.  Until that time, upon notification from the REP of an inadvertent disconnect or Move-out that has been completed by the TDSP, the TDSP will restore service following the Emergency Reconnect procedures outlined in section VII. A. of this guide.

Any TDSP charges associated with re-energizing the customer’s premise will be billed to the CR initiating the safety net Move-In.  Charges associated with re-energizing a customer’s premise while completing an Emergency Reconnect as a result of an inadvertent disconnect or move-out will be billed to CR of Record. If necessary the CR of Record will need to use the dispute process to remedy any resulting billing issues.

# IV. Process Overview

## A.  Disconnect Process Overview

CR credit cycle reveals ESI ID population subject to DNP.

CR performs internal validations prior to issuing disconnection requests.

CR submits 650_01 for disconnection according to TX SET guidelines no later than one day prior to requested completion date.

TDSP receives 650_01 transaction and performs validations.

For orders that do not pass validations, 650_02 Reject with the appropriate code and reason is sent to CR.

If the transaction does not pass ANSI validation, a negative 997 reject is sent.

Upon successfully validating the 650_01, TDSP creates an internal service order which is then routed and scheduled geographically to the appropriate FSR.

For orders that can not be completed, 650_02 Completed Unexecutable is sent to CR with appropriate code and reason.

For orders that can not be completed on the requested date due to time constraints in the field, TDSP will pend the order and schedule on the next available field operational day.

TDSP completes order and responds to CR with a 650_02 transaction within one business day of completion.

## B. Reconnect Process Overview

CR confirms customer’s satisfactory correction of reasons for disconnect.

CR performs internal validations prior to issuing reconnect request.

CR submits 650_01 for reconnection according to timelines outlined in Substantive Rule 25.483 (n) 1-7.

TDSP receives 650_01 transaction and performs validations.

For orders that do not pass validations, 650_02 Reject with the appropriate code and reason is sent to CR.

If the transaction does not pass ANSI validation, a negative 997 reject is sent.

Upon successfully validating the 650_01, TDSP creates an internal service order which is then geographically routed and scheduled to the appropriate FSR to be completed according to the timelines outlined in Substantive Rule 25.483 (n) 1-7.

For orders that can not be completed, 650_02 Completed Unexecutable is sent to CR with appropriate code and reason.

TDSP completes order and responds to CR with a 650_02 transaction within one business day of completion.

# V. Transaction Processing

## A. Timelines for Transaction Delivery

Suggested timeframes for receipt of Disconnection and Reconnection service order requests:

### i. Disconnect

For routine disconnect requests to be scheduled on the next field operational day transactions must be received by all TDSPs by 5:00 PM CPT.  Disconnect orders received prior to 5:00 PM CPT with a requested date that equals the date submitted will be processed as follows:

AEP:  Will schedule order for next available field operational day.

CNP:  Will schedule order for next available field operational day.

Entergy:  Will schedule order for next available field operational day.

Oncor:  Will schedule order for next available field operational day.

SULP:  Will schedule order for next available field operational day.

TNMP:  Reject order as backdated.

Disconnect orders received after 5:00 PM CPT on the same day as the requested date will be rejected except for CNP.

Any valid Texas SET approved EDI 650_01 disconnect requests received prior to the next field operational day will be accepted and scheduled by the TDSP.

### ii. Reconnect

For routine reconnect requests to be scheduled no later than the next field operational day, transactions must be sent to the TDSPs according to the timeframes outlined in Substantive rule 25.483 (n) (1-7).

For priority or after hours reconnect requests to be scheduled on the same field operational day transactions must be sent to the TDSPs by the following times:

AEP:  3:00 PM for priority

CNP: No priority

Entergy:  7:00 PM for after hours

Oncor:  24x7

SULP:   5:00 PM for after hours

TNMP:  7:00 PM for after hours

## B. Transaction Validations

### i. REP validations prior to initiating 650_01

Prior to issuing 650_01 for disconnection, REPs shall verify that they are still the Rep of Record.  Further, verifying that a pending Disconnect or Move-Out does not exist will prevent a service request from being rejected.  REPs will also verify critical care status of residential customers prior to issuing initial disconnection request.

### ii. TDSP validations upon receipt of 650_01

Upon receipt of a disconnect or reconnect service request, TDSPs may perform the following validations on 650_01 transactions:

Verify that the REP is certified for disconnection for non-pay transaction processing.

Verify that the REP submitting a disconnect request is the Rep of Record.

Perform ANSI validations on 650_01.

Perform TX SET validations on 650_01.

Review meter indicators for ESI ID for critical load, critical care, and master metered premise.

Verify if a disconnect request is a duplicate.

Verify if a reconnect request is a duplicate.

Verify if a Move-In or Switch has been scheduled on the requested date.

Verify if a Move-Out has been received by requesting REP.

Verify if the requesting REP is available for reconnection the following day if requested date for disconnection is Friday.

Identify if reconnect request is a priority reconnect.

Verify if a reconnect request has been previously received for disconnect request within the past 24 hours. (CNP only)

Upon receipt of a reconnect, verify if original disconnect request was not rejected (CNP Only)

Verify if a weather moratorium is in effect.

C. Competing Orders
When a disconnect request is received with a requested completion date that is two business days prior to the scheduled date of a pending Switch or Move-In, the disconnect requests will be rejected by all TDSPs, with the exception of CNP, Oncor and TNMP.

CNP, Oncor and TNMP will complete unexecutable a disconnect for non-payment only when the requested date is greater than (after) or equal to the scheduled date of a pending Switch or Move-In and these transactions have been successfully completed changing either the Rep of Record and/or customer for this premise. When a disconnect request is received with a requested date that is less than (before) the scheduled date of a Switch or Move-In the disconnect requests will be worked.  Disconnect orders carried over to next business day may not be worked due to competing order and will be complete unexecutable.

### i. Move In

In order to re-energize a premise that has been disconnected, the new Rep of Record’s Move-In will energize the customer’s premise and will be subject to applicable move-in or reconnect fees per TDSP tariffs.

Table 1. Competing Orders- Move-In

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| 650_01 DNP requested date 2 days prior to MVI or Switch | Reject 650_01 | Will work 650_01 | Reject 650_01 | Will work 650_01 | Will work 650_01 | Will work 650_01 |
| 650_01 DNP requested date >/= MVI or Switch | Reject 650_01 | Reject 650_01 | Reject 650_01 | Complete unexecutable | Reject 650_01 | Complete unexecutable |
| Fee | Connect Fee | Connection Charge | Move-In Fee | Connect Charge | Service Connection Charge | Account Initiation Fee |

A Move-In submitted on a premise that has been de-energized for non-payment may still require a permit for completion in certain jurisdictions.  Regardless of the duration that a premise has been de-energized for non-payment, a permit will not be required for re-energizing a premise while completing an off-cycle switch.

### ii. Off-cycle Switch

If the new Rep of Record has submitted an off-cycle Switch the TDSP will re-energize the premise and bill applicable off-cycle switch or reconnect charges to the new Rep of Record.

Table 2. Competing Orders-Off-cycle Switch

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| TDSP Action | Re-energize premise | Re-energize premise | Re-energize premise | Re-energize premise | Re-energize premise | Re-energize premise |
| TDSP Fee | Reconnect Charge | Connection Charge | Out of Cycle Switch Charge | Connect Charge | Special Meter Read Fee | Off Cycle meter reading charge |

### iii.  On-cycle Switch

If the new Rep of Record has submitted an on-cycle Switch at a premise that has been previously de-energized, the TDSP will perform one of the following actions:

In order to re-energize the premise CNP, Entergy and TNMP would require the CR with the ability to submit a 650_01 Reconnect transaction to send the transaction with a purpose code of RC003 to the TDSP in order to restore the service.  In the event that a CR is not certified to transmit this transaction, CNP, Entergy and TNMP would expect the CR to follow the Emergency Procedures outlined in section VII.A of this guide.

Table 3. Competing Orders- On-cycle Switch

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| TDSP Action | Perform meter read | Perform meter read | Perform meter read | Perform meter read | Perform meter read | Perform meter read |
| Energize | Yes | No | No | Yes | Yes | No |
| TDSP Fee | Reconnect Charge | None | None | Connect Charge | Reconnect Charge | None |

## D. Reconnect/Disconnect Processing Order

If a reconnect request is received before a disconnect request, all TDSPs except for CNP will reject the reconnect request immediately using SET code “RWD”. Any disconnect requests received after an associated reconnect order has been rejected will be worked by the TDSP.  If inadvertent disconnection occurs, then emergency reconnection provisions will be followed.

CNP has developed a process that if a reconnect is received without a corresponding disconnect request, the reconnect request is currently held for 24 hours to wait for the corresponding disconnect for non-payment transaction (650_01).

- If no corresponding disconnect is received in the 24-hour period the reconnect requested will be Rejected- 650_02.  If CNP later receives the 650_01 Disconnect Request after the 24-hour period and the transaction reference number BGN06 refers to the Reconnect, CNP will reject that DNP request with a 650_02 'RC RECEIVED BEFORE DNP WORKED' reason description.

- If the corresponding disconnect for non-payment arrives during that period, the transactions/requests cancel each other out and produce 650_02 complete unexecutable responses with SET code 'T018' reason codes and 'RC RECEIVED BEFORE DNPWORKED' reason description.

- If inadvertent disconnection occurs, then emergency reconnection provisions will be followed.

Table 4. Transaction Processing Order

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| TDSP Action | Reject 650_01 reconnect | See text Above | Reject 650_01 reconnect | Reject 650_01 reconnect | Reject 650_01 reconnect | Reject 650_01 reconnect |
| Code | RWD | See text Above | RWD | RWD | RWD | RWD |

## E. Disconnection at Alternate Location

When necessary, service orders without a premium disconnect location indicator (i.e. pole, substation) that can not be completed by the FSR at the meter may be referred within one business day to a specialized field group that will disconnect service at the pole or transformer.  Service orders with premium disconnect location indicator will be immediately referred to specialized field personnel.

When service is disconnected at an alternate location, TDSP will notify the CR on the 650_02 with a code of ‘O” for “other than at the meter”.  For any disconnect performed the appropriate TDSP tariff charges will be applied.  When service cannot be disconnected at an alternate location, the TDSP will respond with a 650_02 complete unexecutable and the CR will need to contact the TDSP for special consideration.

## F. Completed Unexecutable and Rejected Orders

The TDSP will issue 650_02s within one business day for rejected service order requests or service orders that can not be completed in the field.

No charges will be applied to service orders that are rejected.

Service requests that are dispatched and then completed unexecutable will be subject to the following TDSP charges:

AEP:      Dispatched order fee

CNP:      Disconnect or reconnect charge based on initiating service order request with the exception  	   of cancels prior to field completion

Entergy: Disconnect or reconnect charge based on initiating service order request with the exception 	   of cancels prior to field completion.

Oncor:    Disconnect or reconnect charge based on initiating service order request with the exception            	   of cancels prior to field completion.

SULP:    Disconnect or reconnect charge based on initiating service order request with the exception  	   of cancels prior to field completion

TNMP:   Disconnect or reconnect charge based on initiating service order request with the exception            	   of cancels prior to field completion.

The most common causes for service orders that are completed un-executable are:

Access Issues

Unsafe Conditions at the Meter

Reconnect request received before Disconnect performed

Some common causes for rejected service requests are:

Account already in “active-disconnected”status

Requesting party not current Rep of Record

Pending Move-In, Switch or Move-Out (same REP of Record)

Account not active

## G. Priority Orders

When issuing a 650_01 for service reconnection, REPs may request priority service where available.  The following Texas SET codes should be used to indicate priority status on reconnect service orders:

Table 5. TDSP Priority Codes

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| Outside Normal Business Hours | 99 | Not Applicable | 02 | 03 | Not Applicable | Not Applicable |
| Holiday | Not Applicable | Not Applicable | Not Applicable | 04 | Not Applicable | Not Applicable |

All routine service orders should be submitted with an “01” priority code. Any service order received by a TDSP with a priority code other than those listed above will be processed as a routine service order.

If a CR issues a priority reconnect order after issuing a routine reconnect order and the routine reconnect order has not been completed, the priority order will be processed as follows:

AEP: Rejects priority order as a duplicate request

CNP: Not applicable

Entergy: Priority order trumps routine order

Oncor:  Rejects order as a duplicate request

SULP:  Not applicable

TNMP:  Not applicable

## H. Service order cancellations

In order to cancel a disconnect request that has not been completed, a REP must send a 650_01 reconnect request referencing the BGN02 disconnect to the TDSP.  With the exception of AEP and TNMP, no charges will apply if the reconnect is received prior to completing the disconnect request.  For orders that are already in a scheduled status after 8:00 AM CPT on the date of request the following charges will apply:

AEP: $25

CNP: No Charges will be applied

Entergy:  No Charges will be applied.

Oncor:  No Charges will be applied

SULP:  No Charges will be applied.

TNMP: $15

In order to cancel a reconnect request because the REP may have sent the reconnect in error or for the wrong ESI ID, a REP must send a 650_01 "C" Cancel, referencing the BGN02 of the initiating 650_01 Reconnect Service Order Request.  For orders that are already in a scheduled status after 8:00 AM CPT on the date of request the following charges will apply:

AEP: $25

CNP: No Charges will be applied

Entergy:  No Charges will be applied

Oncor:  No Charges will be applied

SULP:  No Charges will be applied.

TNMP: $15

## I. Response Transactions

A 650_02 response transaction will be issued by TDSPs for every 650_01 transaction within one business day upon the following:

Rejection of service order after performing initial transaction validations

Completion of the requested field service activity

Determination by field service personnel of unexecutable status

Cancellations of a requested reconnect request

After unsuccessfully completing the request two days in a row (Oncor only).

Because not all Mobile Data Systems used by TDSPs capture the date and time the FSR completed a service order, the date and time completed field of the 650_02 will be populated at the time the response transaction is generated and sent to the REP except by CNP.  CNP will populate the field completion date and time in the 650_02 transaction for successfully completed service order requests.

Due to the exceptional conditions outlined in section VII of this guide, REPs will need to follow up with the TDSP if the 650_02 for a disconnect request is not received within 3-5 business days following the requested disconnect date.  Inquiries should be submitted via email as follows:

AEP:  crrtx@aep.com

CNP:  hou-cso.operations@centerpointenergy.com

Entergy: email contact to REP Relations

Oncor: utiltxn@oncorgroup.com

SULP:  egarcia@su-power.com

TNMP: dnprelations@tnpe.com

# VI. Field Service Activities

## A. Disconnection Service Orders

The following schedule outlines the availability of field service personnel for performing disconnection requests.  Disconnect orders requesting dates beyond the next field operational day will be scheduled and performed by TDSP according to availability of field service personnel on the requested date.  Field activities for disconnection service begin at 8:00 AM CPT for all TDSPs except for Entergy, which begins its collections at 7:00 AM CPT.

Per Customer Protection Rule 25.483 (f), only REPs that have payment centers open and personnel available to submit reconnect requests on Saturdays or holidays can request disconnection of a customer’s electric service for nonpayment on a holiday or weekend or the day before a holiday or weekend.  Only TDSPs that are available to reconnect service on a holiday or weekend will disconnect a customer’s electric service for nonpayment on a day preceding a weekend or holiday.

REPs who do not want disconnection requests completed on a day that immediately precedes a weekend or holiday should notify the TDSP as follows so that these service orders will be pended until the next available field operational day:

AEP:  Not applicable

CNP: hou-cso.operations@centerpointenergy.com, 10 business days prior to effective 				         date

Entergy: Not applicable

Oncor:  contact REP Relations Manager 10 business days prior to effective date

SULP:  egarcia@su-power.com

TNMP:  dnprelations@tnpe.com, 10 business days prior to effective date

Disconnection Order Overflow

If a disconnect request can not be completed on the requested day and the next available field operational day immediately precedes a weekend or holiday, the TDSP may pend the order and reschedule the disconnect request on the next available field operational day as follows:

AEP:  No Friday disconnects processed

CNP:  Per REP specification

Entergy:  No Friday disconnects processed for Thursday requested dates.

Oncor:  Per REP specification

SULP:  No Friday disconnects processed

TNMP:  Per REP specification

REPs requesting that disconnect overflow requests will not be completed on the business day immediately preceding a weekend or holiday should notify the TDSP:

AEP:  Not applicable

CNP: hou-cso.operations@centerpointenergy.com

Entergy: Not applicable

Oncor:  contact REP Relations Manager 10 business prior to effective date

SULP:  egarcia@su-power.com

TNMP:  dnprelations@tnpe.com

Table 6. Field Service Hours-Disconnect

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| Routine | 4:00 PM | 5:00 PM | 5:00 PM | 5:00 PM | 5:00 PM | 5:00 PM |
| Priority | Not available | Not available | Not available | Not available | Not available | Not available |
| Weekend | Not available | Not available | Not available | Not available | Not available | Not available |
| Holiday | Not available | Not available | Not available | Not available | Not available | Not available |
| After hours | Not available | Not available | Not available | Not available | Not available | Not available |

## B. Reconnection Service Orders

The following schedules outline the availability of field service personnel for performing reconnection requests:

Routine Reconnects:

Per PUCT Substantive Rule 25.483, any reconnect request, including those for a Premium Disconnect Location (i.e. pole, substation), issued by a REP according to the timeframes outlined in (n) 1-7, must be completed by the TDSP no later than the next field operational day.

All reconnect requests will be completed within 48 hours from the time the

order is received. For Routine reconnect requests received by Oncor after

7:00 PM on a Friday or after 7:00 PM on any business day that precedes a

holiday followed by a non-business day, these reconnect requests will be

charged the Oncor Reconnect Tariff charge for Special Route During Regular

Hours, $28.00.

Table 7. REP timelines for submitting reconnect request

| Payments made on a Business Day: | Reconnection request must be sent by: |
| --- | --- |
| Between 8:00AM and 12:00 PM | 2:00 PM that business day |
| Between 12:00 PM and 5:00 PM | 7:00 PM that business day |
| Between 5:00 PM and 7:00 PM | 9:00 PM that business day |
| Between 7:00 PM and 8:00 AM | 2:00 PM the next business day |
| Payments made on a weekend day or holiday | 2:00 PM the first business day after the payment is made |

Emergency Reconnects:

Please refer to section VII of this guide for the 24x7 emergency reconnection process and appropriate contacts.

After Hours Reconnects:

Entergy After Hours/Holiday/Weekends Reconnects

Reconnect requests outside normal business hours must be initiated by a 650_01 reconnect transaction as well as a call to Entergy’s 24x7 Support Center 1-888-847-1211. The REP’s phone call to the Support Center is the only trigger that will initiate the after hours reconnect.

TNMP offers an after hours reconnect for an additional charge. This reconnect request should be used when submitting a reconnect to be worked outside normal business hours.  For a REP to initiate an after hours reconnect, a 650_01 reconnect transaction should be sent, as well as a  call to TNMP's  24x7 Support Center, 1-888-866-7456. The REP's phone call to the Support Center is the only current trigger that will initiate the after hours reconnect.  TNMP also requires any reconnect request to be supported by phone call on reconnect requests submitted after 2pm on Fridays or days before a holiday.

Table 8. Field Service Hours-Reconnection

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| Routine | 5:00 PM | 9:00 PM | 5:00 PM | 5:00 PM | 5:00 PM | 5:00 PM |
| Friday | 5:00 PM | 9:00 PM | 5:00 PM | 5:00 PM | 5:00 PM | 5:00 PM |
| Priority | 5:00 PM CPT Priority Code Required | Not applicable | 7:00 PM CPT Priority Code Required | 24 x 7 Priority Code Required | Not applicable | Not applicable |
| Weekend | Not applicable | Not applicable | Saturday until 7:00 PM CPT Priority Code Required | 24 x 7 Priority Code Required | Not applicable | 10:00 PM CPT Priority Code Required |
| Holiday | Not applicable | Not available | Until 7:00pm CPT Priority Code Required | 24 x 7 Priority Code Required | Not applicable | 10:00 PM CPT Priority Code Required |
| After hours | Not applicable | Not applicable | Until 7:00pm CPT Priority Code Required | 24 x 7 Priority Code Required | Not applicable | 10:00 PM CPT Priority Code Required |
| Emergency | – See Section VII.A. of this document. Priority Code Required |

## C. Requirements for reconnecting service

Safe access to the meter or premium disconnect location are required to restore service.  Evidence of tampering or damage to the meter equipment may result in delayed or completed unexecutable orders when reconnecting service.

Entergy Distribution will not reconnect a service where there is load on the meter.  If the Entergy Distribution FSR verifies with a voltmeter that there is load on the meter the reconnection request will be completed unexecutable.

With the exception of Entergy, TDSPs will not require inside or outside breakers to be off when performing a reconnection request. However, REPs are advised to inform customers whose service has been disconnected for non-pay to take appropriate safety measures such as placing all breakers in the “OFF” position and to disconnect any extension cords from a neighboring facility.

## D. Customer receipting issue

Due to the fact that the industry has not established a process for the FSR to verify a customer’s payment and/or determine if the receipt shown is valid for the outstanding amount, the disconnection request may be executed by the FSR.  Under this circumstance, the FSR will inform the customer to contact their Retailer to arrange for reconnection of their service.

## E. Premise access issues

TDSPs will make every reasonable attempt to gain access to the customer’s premise to complete the service order.  These measures may include notifying law enforcement agencies to request assistance or referring the service order to specialized field personnel for disconnection at a premium location.  Based upon determinations made in the field at the time the FSR is attempting to disconnect or reconnect, these measures are applied by TDSPs on a case by case basis.  The REP may also be requested to assist and participate with this request, as a means to successfully completing the service order.

If access is denied, no additional denial of access fees are applied to a disconnect or reconnect order.  These types of orders will be completed unexecutable with applicable TDSP tariff charges.

AEP:  Dispatched order fee.

CNP:  Disconnect or reconnect charge based on initiating service order request with the exception of cancels prior to field completion.

Entergy:   Disconnect or reconnect charge based on initiating service order request with the exception of cancels prior to field completion.

Oncor:  Disconnect or reconnect charge based on initiating service order request with the exception of cancels prior to field completion.

SULP:   Disconnect or reconnect charge based on initiating service order request with the exception of cancels prior to field completion

TNMP:  Disconnect or reconnect charge based on initiating service order request with the exception of cancels prior to field completion.

## F. Door Hanger Policies

TDSPs may   provide a Disconnect for Non-Payment (DNP) door hanger that informs the customer that at the request of their Competitive Retailer the TDSP has disconnected the electric service for nonpayment.  The language provided in the door hanger encourages the customer to contact their Competitive Retailer to arrange for reconnection of their service. This door hanger is left at the premise for Disconnects for Non-Payment, both residential and commercial.

If the FSR is unable to gain the required access to reconnect service a door hanger may be left advising the customer of the reconnection attempt and the action the customer may take to have service restored.

Door hangers are used by TDSP as follows:

Table 9. Door Hanger Use by TDSP

|  | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| --- | --- | --- | --- | --- | --- | --- |
| Disconnect | No | Yes, for completed service order | Yes, for completed unexecutable service order | No | Yes | No |
| Reconnect | Yes, when unable to access meter | Yes, when unable to access meter | Yes, when unable to access meter | Yes, when unable to access meter | Yes | No |

## G.  Meter Seal Policies for Disconnection

The following distinguishing characteristics are used at a customer premise meter to indicate the service is off for non-pay (e.g. meter seal, sticker, etc.)

AEP:  brown tag is attached to meter seal advising customer to contact REP to have service restored

CNP: meter seal is red, also this is same seal used for completed Move-Out (MVO) request.

Entergy: meter seal is yellow

Oncor: meter seal is orange

SULP:  meter seal is red

TNMP: meter seal is gold

# VII. Exceptions

## A. Emergency reconnects

There may be times when a customer has been disconnected for non-payment in error. For completed disconnection orders that result in a life threatening situation, PUCT request or are completed inadvertently, REPs will need to contact each TDSP to arrange for an emergency reconnection and identify the reason for the emergency service request.  Life threatening situations should be immediately reported to the TDSP 24x 7 contacts in order to expedite the reconnection request.

AEP:  Contact CR Relations team for process.  A phone call by only designated representatives declared by each CR can initiate an emergency restoration process via a dedicated 24x7 phone number AEP will provide.

CNP: Contact 24x7 Support Center, 713-207-2222 or 1-800-332-7143

Entergy:  Contact 24x7 Support Center, 1-888-847-1211

Oncor:  Contact 24x7 Support Center, 1-888-313-6934

SULP:  Contact 24X7 Support Center, 956-668-9551

TNMP: Contact 24x7 Support Center, 1-888-866-7456

After initiating an emergency service reconnection with the TDSP’s 24x7 support center, REPs should submit a follow up email, including a completed Emergency Reconnect Request spreadsheet to the TDSP.  Please refer to Appendix 2 for the required spreadsheet template. The TDSP email contacts are:

AEP:  email crrtx@aep.com , 650_01 reconnect not required

CNP:  	08:00 A.M. to 5:00 PM Monday – Friday, Email

spreadsheet to CustomerCare-CR@CenterPointEnergy.com

After 5:00 P.M. until 7:00 PM Monday- Friday also on Saturday 8:00 AM to 4:00 PM, Email spreadsheet to CNP.Priority@CenterPointEnergy.com , 650_01 RC001 or RC003 required. (If CR can not issue RC003 reconnects and is not the CR initiating the original disconnect, 650_01 will not be required.)

Entergy: pbc@entergy.com

Oncor: utiltxn@oncorgroup.com, 650_01 reconnect not required

SULP:  egarcia@su-power.com, 650_01 reconnect not required

TNMP: dnprelations@tnpe.com, 650_01 reconnect not required

## B. Critical Load

In the interest of public safety, disconnection requests for non-residential customers that have been identified by the TDSP as critical or sensitive load will be either rejected with an A13 code with remarks that will reflect Life Support/Critical care or completed unexecutable by TDSPs with a reason code of V002 Life Support Customer.

AEP:  FSR discretion at point of service will be exercised.  If FSR determines that completing the disconnect order would create an unsafe condition, the order will be completed un-executable with reason (e.g. sensitive load-school).

CNP: 	Disconnect request is rejected with A13 and remarks will reflect Life Support/Critical Customer if the Life Support indicator is “Y” in CNP system.

Entergy:  Disconnect request is completed unexecutable.

Oncor:     Disconnect request is completed unexecutable.

SULP:     Disconnect request is completed unexecutable.

TNMP:    Disconnect request is completed unexecutable.

In the event that a life threatening situation is discovered or the FSR determines that the premise qualifies as a Critical Load although currently not indicated as such, the disconnect request will be completed unexecutable with reason code V002-Life Support Customer.

Upon discovery of red lights or equipment associated with supporting air traffic control or other associated FAA activities, FSR will complete unexecutable the disconnect request.   REPs who have received FAA approval to perform disconnect for the premise may submit to AEP a 650_01 disconnect request with the notation “second request: FAA approval received”.  For all other TDSPs, REPs requesting to disconnect service for FAA related premises must contact the TDSP to arrange for disconnection.  REPs will need to coordinate with their REP Relations managers at each TDSP, other than Oncor, to complete disconnection requests for critical load premises. For Oncor, contact Business Support at 1-888-313-6934, or contactcenter@oncorgroup.com.

## C. Critical Care

Disconnection requests received by the TDSP for residential customers that the TDSP has identified as critical care will be processed as follows:

AEP:  Disconnect request will be processed on first trip as completed unexecutable with reference to 	life support customer.  CR can resubmit DNP request with note “second request” to 	acknowledge Critical Care situation and for AEP to perform DNP request.

CNP:	Disconnect request is rejected with A13 and remarks will reflect Life Support/Critical 	Customer.

Entergy: Disconnect request is completed unexecutable.

Oncor:    Disconnect request is completed unexecutable

SULP:    Disconnect request is completed unexecutable.

TNMP:   Disconnect request is completed unexecutable.

REPs requesting to disconnect service for critical load or care customers in CNP, Oncor, TNMP, or Entergy service territories must contact the TDSP to arrange and coordinate any special instructions in reference to the disconnection of these types of premises. REPs will need to coordinate with their REP Relations managers at each TDSP, with the exception of Oncor, to complete disconnection requests for critical care premises.  For Oncor, contact Business Support at 1-888-313-6934, or contactcenter@oncorgroup.com

## D. Weather Moratoriums

All Market Participants should monitor www.nws.noaa.gov  for the following conditions that would establish a weather moratorium. Weather moratorium may be invoked in a service territory at any time during the day when one of the following conditions exists in a county as outlined in PUCT Rule 25.483:

Table 10. Extreme weather emergency due to cold:

| The previous day's highest temperature did not exceed 32°F and the predicted temperature for the next 24 hours is at or below 32°F. (Both conditions must be met before disconnection activity is suspended in a service territory). | Saturday | Sunday | Monday | Tuesday | Wednesday | Thursday | Friday |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Example I | 28°F | 28°F | 32°F | 34°F | 34°F | 32°F | 32°F |
|  |  |  | No Disconnect | Disconnect | Disconnect | Disconnect | No Disconnect |
| Example II | 28°F | 28°F | 32°F | 32°F | 34°F | 32°F | 45°F |
|  |  |  | No Disconnect | No Disconnect | Disconnect | Disconnect | Disconnect |
| Example III | 28°F | 28°F | 32°F | 30°F | 34°F | 32°F | 25°F |
|  |  |  | No Disconnect | No Disconnect | Disconnect | Disconnect | No Disconnect |

Table 11.  Extreme weather emergency due to heat:

| The National Weather Service issues a heat advisory for that day or on any one of the preceding two calendar days. | Saturday | Sunday | Monday | Tuesday | Wednesday | Thursday | Friday |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Example I | Heat Advisory in Effect | Heat Advisory in Effect | Heat Advisory in Effect | No Heat Advisory | No Heat Advisory | No Heat Advisory | Heat Advisory in Effect |
|  |  |  | No Disconnect | No Disconnect | No Disconnect | Disconnect | No Disconnect |
| Example II | Heat Advisory in Effect | No Heat Advisory | No Heat Advisory | No Heat Advisory | Heat Advisory in Effect | No Heat Advisory | No Heat Advisory |
|  |  |  | No Disconnect | Disconnect | No Disconnect | No Disconnect | No Disconnect |

### i. Disconnection Activity During Extreme Weather

In the event that one of the above conditions exists in a county served by a TDSP, that TDSP shall notify the PUCT and REPs via email that a weather moratorium has been invoked and that disconnection activity has been suspended as follows:

AEP:  By County

CNP:  By Service Territory

Entergy: By Service Territory

Oncor:  By County

SULP:  By Service Territory

TNMP: By Service Territory Zone (please refer to Appendix 3 or TNMP website for a list of zip codes associated with each zone.)

REPs will need to provide their company contact to their REP Relations Manager at each TDSP in order to receive these weather notifications.

For the duration of the weather moratorium, REPs shall not issue disconnection request for any affected areas.  Any disconnection requests issued for premises in counties or service territories that are experiencing a weather moratorium will be processed as follows:

AEP:  Completed Unexecutable

CNP:  Pended until moratorium lifted

Entergy: Completed Unexecutable

Oncor:  Completed Unexecutable

SULP:  Completed Unexecutable

TNMP: Pended until moratorium lifted

Disconnection requests that are pending completion by the TDSP at the time a weather moratorium is established will be processed as follows:

AEP:  Completed Unexecutable

CNP:  Pended until moratorium lifted

Entergy: Completed Unexecutable

Oncor:  Completed Unexecutable

SULP:  Completed Unexecutable

TNMP: Pended until moratorium lifted

Disconnection requests that are pended by a TDSP during a weather moratorium will be processed and scheduled with all transactions at the time the moratorium is lifted.

Disconnection requests that are completed unexecutable by a TDSP during a weather moratorium should be re-issued by the REP at the time the moratorium is lifted.

In the event of a PUCT mandated weather moratorium for an extend length of time, 7-calendar days or more, the REP will cancel all pending disconnect requests with 650_01 reconnect requests until the PUCT has declared that the weather moratorium has been lifted.  This would prevent any outstanding and/or pending disconnect requests from being completed after the moratorium is lifted where customers may have made payments during that time period, also the TDSP would now be working with and scheduling more up to date DNP transactions.

### ii. Reconnection Activity During Extreme Weather

All types of reconnect request will be processed by all TDSP during a weather moratorium.

Reconnect requests received for pended disconnect orders will be processed in order to cancel the disconnect request.  Reconnect requests received for disconnect completed prior to an extreme weather event are processed and dispatched according to applicable timeframes during a weather moratorium.

## E. Force Majeure

In section 4.2.4 of Terms and Conditions of the TDSP tariffs a Force Majeure event is defined as:

Neither Company nor Competitive Retailer shall be liable in damages for any act or event 
that is beyond such party's control and which could not be reasonably anticipated and 
prevented through the use of reasonable measures, including, but not limited to, an act of 
God, act of the public enemy, war, insurrection, riot, fire, explosion, labor disturbance or 
strike, wildlife, unavoidable accident, equipment or material shortage, breakdown or 
accident to machinery or equipment, or good faith compliance with a then valid 
curtailment, order, regulation or restriction imposed by governmental, military, or lawfully established civilian authorities, including any order or directive of the Independent Organization.

AEP, Entergy, Oncor, and SULP:  Any pending service request, including disconnect or reconnect, will be completed unexecutable during a Force Majeure event.

CNP and TNMP:  REPs should  cancel all pending disconnect or reconnect service requests with 650_01 reconnect or cancel reconnect requests until the Rep Relations group notifies the CR via email and/or telephone that routine operations have been restored.

Once a Force Majeure event has concluded and the TDSP has re-established routine operations, REPs should submit any service requests for ESI IDs that still qualify for disconnection or reconnection.

## F. Master Metered Premises

Prior to issuing a disconnection request for a master metered premise, a REP must fulfill the tenant notification requirements outlined in PUCT Substantive Rule 25.483 (k).   If applicable, a REP may request that a TDSP’s field personnel post the required notices at a master metered property for a designated fee listed below:

AEP:    Notice posting available, $42 per master metered premise; contact AEP CR Relations 	account manager to arrange.

CNP:  	 Notice posting not available

Energy: Notice posting not available

Oncor:  Notice posting not available

SULP: Not applicable, SULP has no master metered premises

TNMP: Notice posting available, $35 per master metered premise

Disconnection requests received for a master metered premise will be completed unexecutable by the TDSP.  The requesting REP will need contact the TDSP to coordinate the disconnection of the master metered premise as follows:

AEP:   contact to REP Relations

CNP:  hou-cso.operations@centerpointenergy.com

Entergy: contact REP Relations manager

Oncor: contact Business Support at 1-888-313-6934, or contactcenter@oncorgroup.com

SULP:  Not applicable, SULP has no master metered premises

TNMP: contact REP Relations manager

## G. Unmetered Service

An unmetered service that is not a critical load premise or that does not present a hazardous condition if disconnected will be subject to the same processing as metered services for disconnection and reconnection.

For all other unmetered services, disconnection requests will be completed unexecutable upon receipt or following field investigation. The requesting REP will need contact the TDSP to coordinate the disconnection request as follows:

AEP:   contact to REP Relations

CNP:  hou-cso.operations@centerpointenergy.com

Entergy: contact REP Relations manager

Oncor: contact Business Support at 1-888-313-6934, or contactcenter@oncorgroup.com

SULP:  contact REP Relations manager

TNMP: contact REP Relations manager

## H. Multiple Metered Service (not Master Metered)

For TDSPs that have multiple meters associated with an ESI ID, any 650_01 service order, whether for disconnection or reconnection, will be executed for all meters associated with that premise. REPs will need to submit 650_01s for multiple meters as follows:

AEP:  		one service order per ESI ID

CNP:  		one service order per meter

Entergy:  	one service order per ESI ID

Oncor:  	one service order per ESI ID

SULP:		not applicable

TNMP: 	not applicable

If a disconnect or reconnect can not be completed for any meter associated with the ESI ID the TDSP will notify the REP via a 650_02.

Discretionary charges for disconnection or reconnection are billed by the TDSP as follows:

AEP:  		one service charge per ESI ID

CNP:  		one service charge per ESI ID

Entergy:  	one service charge per ESI ID

Oncor:  	one service charge per ESI ID

SULP:		not applicable

TNMP:  	not applicable

## I. Meter Tampering Issues

While performing a disconnection of service a FSR may discover that there has been tampering at the meter.  If the FSR determines that the degree of tampering does not present a hazardous condition, the disconnection will be completed.  If the meter tampering has created an unsafe condition, the disconnection request may be referred to specialized field personnel to attempt to complete the disconnection request at an alternate location as outlined in Disconnection at Alternate Location of this guide.  If disconnection can not be completed as a result of the tampering incident the disconnection request will be completed unexecutable and the TDSP may notify the REP of the hazardous condition and, if applicable, meter removal by issuing a 650_04.

Tampering may also be detected when a FSR is performing a reconnection request or when re-energizing a disconnected premise while performing a Switch or Move-In.  If possible, the FSR will reconnect service at the meter.  If the meter tampering has created an unsafe condition, the 650_01 reconnection request will be completed unexecutable and the TDSP may notify the REP of the hazardous condition and, if applicable, meter removal by issuing a 650_04.

Tampering fees may be assessed by the TDSP and billed to the Rep of Record at either the time of disconnection or upon reconnection of service.  Please refer to the TDSP tariffs for specific charges.

If the REP is notified of potential meter tampering at a premise, the REP may notify the TDSP via a 650_01 MM006 service order for tampering suspected if they are currently the REP of Record and are an Option 1 REP.  Any REP may report suspected tampering at any time by contacting the TDSP’s general call center phone number.

## J. Customer Threatens TDSP FSR

If threatened by the customer, the FSR will not disconnect service. However, the FSR may refer the disconnection request to another group specialized in disconnecting service at the pole, transformer (overhead and padmounted), or weatherhead.  Similar to resolving access issues the TDSP will exhaust all means available, which may include communicating with the REP to request their assistance and participation, as a means to successfully complete the service request.

# VIII. TDSP Charges for Reconnect and Disconnect Services

## A. Discretionary Charges

TDSP will use SAC04 codes for discretionary charges resulting for disconnection or reconnection service as outlined below:

Table 12. SAC04 Codes-Discretionary Charges

|  | Service Territory |
| --- | --- |
| Charge Description | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| Disconnection |  |  |  |  |  |  |
| Routine Disconnect at Meter | N/A | SER024 | SER024 | SER024 | SER024 | SER024 |
| Routine Disconnect at Pole | N/A | SER024 |  | SER026 | SER024 | SER026 |
| Priority Disconnect at Meter | SER027 | N/A | N/A | N/A | SER027 | N/A |
| Priority Disconnect at Pole | SER027 | N/A | N/A | N/A | SER027 | N/A |
| Priority Disconnect at Subsurface Box | SER027 | N/A | N/A | N/A | SER027 | N/A |
| Reconnection |  |  |  |  |  |  |
| Routine Reconnect at Meter | SER030 | SER028 | SER028 | SER030 | SER028 | SER030 |
| Routine Reconnect at Meter Special Route | N/A | N/A | N/A | SER031 | N/A | N/A |
| Routine Reconnect at Pole | SER030 | SER028 | SER028 | SER034 | SER028 | SER034 |
| Routine Reconnect at Subsurface Box | SER030 | N/A | SER028 | SER034 | SER028 | N/A |
| Routine Reconnect at CT Meter | SER030 | N/A | N/A | N/A | SER028 | N/A |
| Priority Reconnect at Meter | SER029 | N/A | N/A | SER029 | SER029 | N/A |
| Priority Reconnect at Pole | SER029 | N/A | N/A | SER035 | SER029 | N/A |
| Priority Reconnect at Subsurface Box | SER029 | N/A | N/A | SER035 | SER029 | N/A |
| Priority Reconnect at CT Meter | SER029 | N/A | N/A | SER035 | SER029 | N/A |
| Weekend Reconnect at Meter | N/A | N/A | N/A | SER032 | N/A | N/A |
| Weekend Reconnect at Pole | N/A | N/A | N/A | SER035 | N/A | N/A |
| Weekend Reconnect at Subsurface Box | N/A | N/A | N/A | SER035 | N/A | N/A |
| Weekend Reconnect at CT Meter | N/A | N/A | N/A | SER035 | N/A | N/A |
| Holiday Reconnect at Meter | N/A | N/A | N/A | SER033 | N/A | N/A |
| Holiday Reconnect at Pole | N/A | N/A | N/A | SER036 | N/A | N/A |
| Holiday Reconnect at Subsurface Box | N/A | N/A | N/A | SER036 | N/A | N/A |
| Holiday Reconnect at CT Meter | N/A | N/A | N/A | SER036 | N/A | N/A |
| After Hours Reconnect at Meter | N/A | N/A | SER029 | N/A | N/A | SER032 |
| After Hours Reconnect at Pole | N/A | N/A | SER029 | N/A | N/A | SER035 |
| Charge Description | AEP | CNP | Entergy | Oncor | SULP | TNMP |
| After Hours Reconnect at Subsurface Box | N/A | N/A | SER029 | N/A | N/A | N/A |
| After Hours Reconnect at CT Meter | N/A | N/A | SER029 | N/A | N/A | N/A |
| Denial of Access to Meter |  |  |  |  |  |  |
| For Disconnection Orders | SER133 | N/A | SER133 | N/A | SER133 | SER133 |
| For Reconnections Orders | SER133 | N/A | SER133 | N/A | SER133 | SER133 |
| Order Cancellation Fees |  |  |  |  |  |  |
| Disconnect Administration Fee | N/A | N/A | N/A | N/A | N/A | SER132 |
| Dispatched Order Fee | SER132 | N/A | N/A | N/A | SER070 | N/A |
| Tampering Charges |  |  |  |  |  |  |
| Broken Meter Seal Fee | SER130 | N/A | N/A | N/A | SER130 | SER130 |
| Meter Tampering Fee | SER072 | SER072 | SER072 | SER072 | SER072 | SER072 |
| Connection Fees |  |  |  |  |  |  |
| Connect Fee/Connection Charge at Meter/Account Activation Fee | SER019 | SER019 | SER019 | SER030 | SER019 | SER009 |

## B. Other Charges

Non-usage based charges will continue to be assessed by the TDSP and billed to the Rep of Record until service at the disconnected premise has been terminated upon completion of a Move-Out Request.  Non-usage based charges are:

Customer Charge:

All TDSPs use BAS001

Customer Metering Charge:

All TDSPs use BAS003

In order to avoid ongoing liability, a REP must submit a Move-Out request to terminate service no earlier than 5 calendar days after receipt of 650_02 indicating successful completion of disconnect for nonpayment. Competitive Retailers receiving reliable information indicating premise is vacant may submit Move-Out earlier. Upon completion of the Move-Out order the TDSP will discontinue billing any non-usage based charges outlined above to the REP.

## C. TDSP Tariffs

Please refer to the appropriate rate class in each TDSP tariff for rates.  TDSP tariffs are located on the following links:

AEP: http://aepcustomer.com/tariffs/default.htm

CNP: www.centerpointenergy.com/houston/retail/1,2668,,00.html?sub=Tariff&stype=FCRTRF

Entergy: http://uat.exotran.com/entergy/indexMainMenu.jsp?mainmenu_id=2

Oncor: www.oncorgroup.com/electricity/tariffs/distrates

SULP:  www.su-power.com/Tariff.pdf

TNMP: www.tnpe.com/affiliatetransactions/tdutariffs.doc

# IX. Contacts

## A. Emergency System Outage

In the event of a system outage during business hours and a REP can not submit EDI transactions, REPs should contact their REP Relations manager at the TDSP(s) to arrange for a workaround in order to submit reconnect service order requests.  For system outages that occur outside business hours REPs should contact the TDSPs as follows:

AEP:  For system outage contact your REP Relations Manager, 1-877-373-4858

CNP: For system outages contact your REP Relations Manager. Contact information can be found on CNP Website at:

http://www.centerpointenergy.com/files/104289_CR_Support_Contacts&PUCT2-2-04.pdf, for after hours contact 1-800-332-7143

Entergy: 936-525-2034, Rep Relations, after hours contact 1-888-847-1211

Oncor:  For system outage contact Business Support at 1-888-313-6934, or contactcenter@oncorgroup.com

SULP:  For system outage contact your REP Relations Manager during business hours,  after hours contact (956) 668-9551

TNMP: For system outage contact your REP Relations Manager during business hours, after hours contact 1-888-866-7456

## B. Disconnect Forecast Contact

AEP:  crrtx@aep.com

CNP: hou-cso.operations@centerpointenergy.com

Entergy:  pbc@entergy.com

Oncor: utiltxn@oncorgroup.com

SULP: egarcia@su-power.com

TNMP: dnprelations@tnpe.com

## C. Website available information

AEP: 		www.aepcustomer.com

CNP: 		www.centerpointenergy.com/houston/retail/

Entergy: 	http://uat.exotran.com/entergy/index.jsp

Oncor: 	www.oncorgroup.com

SULP:		www.su-power.com

TNMP: 	www.tnpe.com/affiliatetransactions/aboutaffiliatetransrepindex.asp

## D. TDSP general call center phone number

AEP: 		1-877-373-4858

CNP: 		713-207-2222 (Houston area local)

1-800-332-7143 (Long Distance- Toll free)

Entergy: 	1-888-847-1211-- REPs only, not end-use customer

Oncor: 	1-888-313-6934 – REPs only, not end-use customer

SULP:		(956) 687-5600 during normal business hours, (956) 668-9551

TNMP:	1-888-866-7456

# X. List of Tables

## Table 1. Competing Orders- Move-In

## Table 2. Competing Orders-Off-cycle Switch

## Table 3. Competing Orders- On-cycle Switch

## Table 4. Transaction Processing Order

## Table 5. TDSP Priority Codes

## Table 6. Field Service Hours-Disconnect

## Table 7. REP timelines for submitting reconnect request

## Table 8. Field Service Hours-Reconnection

## Table 9. Door Hanger Use by TDSP

## Table 10. Extreme weather emergency due to cold

## Table 11.  Extreme weather emergency due to heat

## Table 12. SAC04 Codes-Discretionary Charges

# XI. Appendices

## Appendix 1-Weekly REP Disconnect for Non-Payment Forecast

## Appendix 2-Emergency Reconnect Request- Data Requirements

## Appendix 3-TNMP Weather Zone Zip Codes