## Slide 1: A Non-Transmission Alternative to the Bates RMR Contract
Greg Ramon & Juan Villa
TECO Energy, Inc (Frontera)
WMS Meeting
June 17, 2004

## Slide 2: “The Concept” A Non-Transmission Alternative to Bates
Currently J.L. Bates is under RMR Status at a projected cost of $26 Million for 2005 (after BENA)
Frontera is a 450 MW modern Combine Cycle facility that already dispatches efficiently under present ERCOT market conditions as an intermediate plant (Typically 16 hr/day); located immediately adjacent to the J.L. Bates Plant
Under this proposed Non-Transmission Alternative, Frontera would receive OOM deployments only as needed when it’s not running to replace the existing Bates RMR; implementation should yield significant savings

## Slide 3: “The Situation” A Non-Transmission Alternative to Bates
Frontera has a 138 kV tie with Mexico that allows 150 MW of transfer (either CT at Frontera could go to Mexico)
Reliability criteria dictates ERCOT to plan for an N-1 contingency – Due to the Mexican tie, ERCOT cannot count on either of Frontera’s units for OOM deployment during an emergency
As a result, ERCOT Pays Bates $Millions yearly for RMR to maintain reliability in case of a potential emergency
Frontera has taken the initiative and approached ERCOT after identifying the situation
ERCOT has confirmed through studies that Frontera is a technically and economically viable alternative to the Bates RMR

## Slide 4: “The Alternative” A Non-Transmission Alternative to Bates
Frontera agrees to Lock-out its tie with Mexico, to forego all sales into Mexico for an agreed upon term, and thus would make the entire plant available to ERCOT
Frontera agrees to meet certain ERCOT operational and notification requirements
In return, ERCOT and Frontera agree to a sharing of the savings from continuing on with a Bates RMR
  The sharing plan would represent savings net of the Frontera OOM payments

## Slide 5: “The Benefits” A Non-Transmission Alternative to Bates
Timing: Frontera can be implemented January 2005, pending expediting of AEP’s 69 kV upgrades.
Savings: A potentially significant amount of savings in uplifted charges to loads has been confirmed by ERCOT modeling
Reduction in Environmental Impacts: Significant Reduction of NOx and SO2 emission levels (on the order of 70 to 85% reductions according calculations performed based on information provided on EPA filings)
Reduction in Capital Expense:
  Postponement or cancellation of capital expenditures on DC Tie with Mexico (Estimated at $35 to $40 Million)
  Potential postponement of bulk transmission upgrades in the Rio Grand Valley (345 KV Valley Loop)

## Slide 6: “The Challenges” A Non-Transmission Alternative to Bates
New Non-Transmission Alternative PRR Must be Approved by Board this August to allow ERCOT implementation for 2005
  ERCOT Evaluation of 2005 RMR Contracts begins this September
What needs to be done
  Expedite “Frontera Specific” Protocol Revisions for ERCOT Authorization, Funding, and Implementation.
  Develop “Frontera Specific” RMR Alternative Contract
  Move through WMS, RMR TF, PRS,TAC, and Board
Expediting Transmission Upgrades
  Likely; Needed for end of 2004
  Weigh expedited construction and cost savings of implementing Frontera solution

## Slide 7: “Specific Request” A Non-Transmission Alternative to Bates
TAC is looking to WMS for recommendation on how to proceed
At least 4 Types of Policy Directions & Protocol Changes associated with the Frontera Proposal
  (1) Do not develop a non-transmission alternative to the Bates RMR contract
  (2) Market Design Change (e.g. locational ICAP)
  (3) Creation of an RFP process, standard contracts, etc
  (4) Evaluation of non-transmission alternatives within the regional planning processes with minimal protocol changes (e.g. billing & settlement)

## Slide 8: “Specific Request” A Non-Transmission Alternative to Bates
Frontera suggests that the WMS consider that our proposal fits in the 4th category
Uniqueness of proposal
  Limited non-transmission alternatives
  Existing Frontera generation alternative is unique in ERCOT for RMR Exit Strategies
    One 150 MW CT is essentially new capacity to ERCOT for planning purposes

## Slide 9: QUESTIONS?