## Slide 1: Instructed Deviation and Portfolio Balancing Energy Bids

## Slide 2
Objectives
Educate participants on EMMS Release 3 implementation
Answer FAQs
Address any remaining issues
Agenda
Brief review of EMMS Release 3.0
FAQs
Additional Questions?

## Slide 3: EMMS Release 3.0 Review
Implement protocol revisions
  PRR 332 – Resource on Test Mode
  PRR 349 – Ramp Rate adherence in portfolio deployments
  PRR 359 – Resource Plan Improvements
  PRR 373 – OOME As Instructed Deviation (ID)
  PRR 424 – Elimination of Commercial Category 4
Model new 3-step market clearing
  Step 1: Estimate portfolio deployments for power balance and zonal congestion
  Step 2: Resolve local congestion
  Step 3: Final portfolio deployments considering unit-specific instructions from Step 2
AND still consider…
  Reliability (power balance and congestion management)
  QSE’s portfolio bid and capacity
  Scheduling & Bidding opportunities (ramp rate recall and price taker mw)

## Slide 4: Questions
“My Category 1 deployment violates my portfolio ramp rate. Is this right?”
“I got struck for Balancing Energy outside of my bid curve. Is your system working?”
“I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”

## Slide 5: Question 1
“My Category 1 deployment violates my portfolio ramp rate. Is this right?”

## Slide 6: Question 1: Cat 1 violates portfolio ramp rate
Why It Happens
Manual (OOME) deployment
  OOME ID is included in Category 1
  Not based on portfolio bid
Different if unit not operating at planned level
Cleared MW v. Instructed Deviation (ID)
  Local Balancing Energy in Step 2 cleared based on Adjusted SCADA
  LBES ID calculated based on Resource Plan
  LBES ID included in Portfolio Deployment
Violate ramp rate to manage congestion or power balance

## Slide 7: Pre-R3 Portfolio Deployment
Portfolio deployment includes:
  1) Step 1 cleared BES from bids
  2) Step 2 cleared BES from bids (ID for Local Balancing Energy instructions)
Portfolio deployment constrained by Bid Ramp Rate
Portfolio Deployment
Step 1 Cleared BES bids
Step 2 Cleared BES bids

## Slide 8: Post-R3 Portfolio Deployment
Portfolio deployment includes:
  1) Cleared BES from bids
  2) ID for Local Balancing Energy instructions (LBES ID)
  3) ID for OOME instructions (OOME ID)
Portfolio deployment (and recall) constrained by Bid Ramp Rate
Portfolio Deployment
LBES ID
OOME ID
Step 3 Cleared BES bids

## Slide 9: Question 1: Cat 1 violates portfolio ramp rate
Example
  QSE A in North Zone
    No deployment in previous interval
    UBES bid: 100 MW @ $40 Ramp: 5 MW/min
    DBES bid: 100 MW @ $20 Ramp: 5 MW/min
    Unit A1
      Planned Level: 45 MW
      Adjusted SCADA: 65 MW
  Market Clearing
    To resolve constraint, cleared 50 MW UBES in Step 2 to Unit A1
    Instructed Output Level = 65 MW + 50 MW = 115 MW
    Instructed Deviation = 115 MW – 45 MW = 70 MW
    Category 1 Deployment: 70 MW UBES
    Category 3 Unit-Specific Deployment to Unit A1: 115 MW
Max UBES based on Ramp Rate = 50 MW

## Slide 10: Question 1: Cat 1 violates portfolio ramp rate
Software Solution
Includes instructed deviation in portfolio deployment, even if outside ramp rate limit
Does not clear BES to offset instructed deviation beyond ramp rate limit

## Slide 11: Question 1: Cat 1 violates portfolio ramp rate
IF BES cleared to offset instructed deviation…
  Assume MCPE = $45
  QSE A in North Zone
    UBES bid: 100 MW @ $40 Ramp: 5 MW/min
    DBES bid: 100 MW @ $20 Ramp: 5 MW/min
    Category 1 Portfolio Deployment: 70 MW UBES
    Category 3 Unit-Specific Deployment to Unit A1: 115 MW
  To meet ramp rate limit, software would clear 20 MW DBES from QSE in Step 3 as “price taker”
  Final Results
    Category 1 Portfolio Deployment: 50 MW UBES
    Category 3 Unit-Specific Deployment to Unit A1: 115 MW

## Slide 12: Question 2
“I got struck for Balancing Energy outside of my bid curve. Is your system working?”

## Slide 13: Question 2: I got struck for Balancing Energy outside of my bid curve. Is your system working?
Why It Happens
Instructed Deviation (ID)
  ID calculated for Local Balancing Energy (LBE) and OOME deployments
  LBE and OOME deployments not based on portfolio bid ($) curve
Previous deployment cannot be entirely recalled
  Previous deployment cannot be entirely recalled due to bid ramp rate
  MW amount that can’t be recalled is cleared as “price taker”

## Slide 14: Question 2: I got struck for Balancing Energy outside of my bid curve. Is your system working?
Example
  QSE B in South Zone
    Deployment in previous interval: 70 MW UBES
    UBES bid
      100 MW Ramp Rate: 5 MW/min
60
100
60
120
MW
$/MWh
80
MW
T0
T1
70
120
20

## Slide 15: Question 2: I got struck for Balancing Energy outside of my bid curve. Is your system working?
Example
  QSE B in South Zone
    Deployment in previous interval: 70 MW UBES
    UBES bid
      100 MW Ramp Rate: 5 MW/min
MW
T0
T1
70
120
20
60
100
60
120
MW
$/MWh
80
Can recall 50 MW of previous deployment
(5 MW/min * 10 min = 50 MW)
Leaves 20 MW UBES that must be deployed

## Slide 16: Question 2: I got struck for Balancing Energy outside of my bid curve. Is your system working?
Example
  QSE B in South Zone
    Deployment in previous interval: 70 MW UBES
    UBES bid
      100 MW Ramp Rate: 5 MW/min
  Market Clearing
    Assume MCPE = $30
    20 MW UBES issued as “price taker” to QSE B
60
100
60
120
MW
$/MWh
80
    Category 1 deployment: 20 MW UBES

## Slide 17: Question 2: I got struck for Balancing Energy outside of my bid curve. Is your system working?
Software Solution
MW Amount that must be issued due to ramp rate cannot set price (“price taker”)

## Slide 18: Question 3
“I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”

## Slide 19: Question 3: “I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”
Why It Happens
Instructed Deviation
  ID calculated for Local Balancing Energy (LBE) and OOME deployments
AND
Previous deployment cannot be entirely recalled
  MW amount that can’t be recalled is cleared as “price taker”

## Slide 20: Question 3: “I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”
Example
  QSE B in South Zone
    Deployment in previous interval: 70 MW UBES
    UBES bid
      100 MW Ramp Rate: 5 MW/min
    OOME ID: 30 MW
60
100
60
120
MW
$/MWh
80
MW
T0
T1
70
120
20

## Slide 21: Question 3: “I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”
Example
  QSE B in South Zone
    Deployment in previous interval: 70 MW UBES
    UBES bid
      100 MW Ramp Rate: 5 MW/min
    OOME ID: 30 MW
60
100
60
120
MW
$/MWh
80
Can recall 50 MW of previous deployment
(5 MW/min * 10 min = 50 MW)
Leaves 20 MW that must be deployed
MW
T0
T1
70
120
20

## Slide 22: Question 3: “I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”
Example
  QSE B in South Zone
    Deployment in previous interval: 70 MW UBES
    UBES bid
      100 MW Ramp Rate: 5 MW/min
    OOME ID: 30 MW
  Market Clearing
    Assume MCPE = $80
    20 MW UBES issued as “price taker” to QSE B
    40 MW UBES cleared based on bid
60
100
60
120
MW
$/MWh
80
    Category 1 deployment: 70 MW UBES
    Category 3 OOME deployment
Price Taker
30 MW of OOME ID
+ 40 MW of Cleared Bid
20
40
Cleared from Bid

## Slide 23: Question 3: “I didn’t get struck for the amount of Balancing Energy I expected. What’s wrong?”
Software Solution
MW Amount that must be issued due to ramp rate cannot set price (“price taker”)
Any additional amount cleared from bid can set price
Final Deployment includes Instructed Deviation + Any Cleared BES from bid

## Slide 24: Summary
Instructed deviation and portfolio ramp rate relate in 14 different ways
  Scenarios depend on:
    Previous deployment (UBES or DBES)
    Previous deployment can/cannot be entirely recalled
    ID’s relation to deployment range based on ramp rate
14 scenarios detailed in Market Bulletin # 19