## Slide 1: Summary of BES Market Activity September 7 – September 20

## Slide 2: Data
Data Points
  Load Forecast Difference
    Difference between mid-term load forecast (end of Day-Ahead) and short-term load forecast (Balancing Energy Market)
  BES Deployed
    Net Balancing Energy Service deployment
  UBES Bids
    Aggregated UBES Bid MW
  MCPE
    Market Clearing Price (without price correction)
Time Period
  Weekdays of September 7 – September 20
  HE 14:00 – HE 18:00
Summary
  Data points averaged by day

## Slide 3
Summary

## Slide 4
 | September 9th | September 10th
Average Load Forecast Difference | 1594 MW | 1665 MW
Average BES Deployed | 2949 MW | 3269 MW
Average UBES Bid MW | 4275 MW | 5320 MW
Average MCPE | $166.96 | $81.92
320 MW
1045 MW
Sept 9 v. Sept 10 Peak

## Slide 5
 | September 9th | September 15th
Average Load Forecast Difference | 1594 MW | 409 MW
Average Difference in Load Forecast & Gen Sched | 2949 MW | 4119 MW
Average UBES Bid MW | 4275 MW | 5247 MW
Average MCPE | $166.96 | $130.08
1170 MW
Sept 9 v. Sept 15 Peak

## Slide 6
September 9th
  Big difference between mid-term and short-term load forecast
  Less UBES bid
September 15th
  Big difference in scheduled generation and load forecast
Summary

## Slide 7
September 9th Interval |  | 14:15 | 14:30 | 14:45 | 15:00
Load Forecast |  | 42,700 | 43,200 | 43,600 | 43,800
Scheduled Generation |  | 40,670 | 40,724 | 40,751 | 40,836
UBES Bid |  | 4,296 | 4,296 | 4,296 | 4,296
Available Capacity Not Bid |  | 1,700 | 1,646 | 1,619 | 1,534
Step 1 | UBES | 2,169 | 2,723 | 2,934 | 3,049
 | DBES | 139 | 247 | 85 | 85
 | MCPE | $59.59 | $72.08 | $90.60 | $119.54
Step 3 | UBES | 2,848 | 3,042 | 3,209 | 3,385
 | DBES | 816 | 566 | 360 | 421
 | MCPE | $79.29 | $290.01* | $290.01* | $152.54
Step 1 MCPE is result of simulation
MCPE for 14:30 and 14:45 were later corrected per Protocol 6.9.5.1
Available Capacity Not Bid = Total Max Online Capacity - Energy Schedules –
AS Requirement – UBES Bid
Sept 9 Details

## Slide 8
September 9th Interval |  | 14:15 | 14:30 | 14:45 | 15:00
Load Forecast |  | 42,700 | 43,200 | 43,600 | 43,800
Scheduled Generation |  | 40,670 | 40,724 | 40,751 | 40,836
UBES Bid |  | 4,296 | 4,296 | 4,296 | 4,296
Available Capacity Not Bid |  | 1,700 | 1,646 | 1,619 | 1,534
Step 1 | UBES | 2,169 | 2,723 | 2,934 | 3,049
 | DBES | 139 | 247 | 85 | 85
 | MCPE | $59.59 | $72.08 | $90.60 | $119.54
Step 3 | UBES | 2,848 | 3,042 | 3,209 | 3,385
 | DBES | 816 | 566 | 360 | 421
 | MCPE | $79.29 | $290.01* | $290.01* | $152.54
Sept 9 Details
500 MW
108 MW
Between 14:15 and 14:30
Load Forecast increased by 500 MW
Increase in UBES cleared
Exhausted available (ramp rate) UBES bids in 14:30 interval

## Slide 9
September 9th Interval |  | 14:15 | 14:30 | 14:45 | 15:00
Load Forecast |  | 42,700 | 43,200 | 43,600 | 43,800
Scheduled Generation |  | 40,670 | 40,724 | 40,751 | 40,836
UBES Bid |  | 4,296 | 4,296 | 4,296 | 4,296
Available Capacity Not Bid |  | 1,700 | 1,646 | 1,619 | 1,534
Step 1 | UBES | 2,169 | 2,723 | 2,934 | 3,049
 | DBES | 139 | 247 | 85 | 85
 | MCPE | $59.59 | $72.08 | $90.60 | $119.54
Step 3 | UBES | 2,848 | 3,042 | 3,209 | 3,385
 | DBES | 816 | 566 | 360 | 421
 | MCPE | $79.29 | $290.01* | $290.01* | $152.54
Sept 9 Details
200 MW
Between 14:45 and 15:00
Load Forecast increased by 200 MW
Increase in UBES cleared
Same amount of UBES bids, BUT more available UBES due to ramp rate