## Slide 1: Special WMS Meeting PRR 525
December 3, 2004
Austin Energy Proposal
Leonard Stanfield

## Slide 2: Statement of Problem
ERCOT is challenged by NERC frequency control standards.
  Frequency problems during ON PEAK / OFF PEAK transitions (0600 and 2200)
ERCOT monitors SCE performance of RGS providers only
  Nearly all RGS providers are meeting existing performance metric.
Having a Performance Metric for all participants will help ERCOT identify the cause of the problem.

## Slide 3: Possible Solutions
Double RGS procurement (ERCOT)
PRR 525 – Establish SCE Performance Criteria for all Market Participants
  3 Proposals (TXU, ERCOT, Austin Energy)
  All 3 Proposals assign a performance metric to ALL participants representing resources.
  All 3 proposals affect the ENE and AS markets differently.

## Slide 4: Current Performance Measure: RGS Ratio Share
Bases performance bandwidth on ratio of QSE’s RGS service to the total ERCOT RGS service.
RGS service is the amount of change on SCE. It has nothing to do with the absolute value of the schedule or generation.

## Slide 5: TXU PROPOSAL: Generation Ratio Share
Assigns a performance metric to all participants representing resources.
Larger bandwidth for larger generators could require more RGS service
Reduces Performance bandwidth for RGS providers with smaller generation ratio shares who are active in the regulation market.
Less RGS providers = Higher RGS prices

## Slide 6: ERCOT Proposal: Generation Obligation Ratio Share
Assigns a performance metric to all participants representing resources.
Bases Performance bandwidth on Ratio Shares of % of Scheduled Generation
Reduces performance bandwidth for current RGS Providers
Discourages participation of smaller RGS providers
Less RGS providers = Higher RGS prices

## Slide 7: Austin Energy Proposal: Generation Change Ratio Share
Bases performance bandwidth on QSE’s ratio share of both RGS & scheduled ENE changes to the total ERCOT RGS & scheduled ENE change.
Recognizes positive impact of RGS, BES and Bilateral ENE providers.

## Slide 8: AGC Response to Schedule Changes
Request for change can happen stepwise. Response
will not. It is SCE that drives AGC.
Following instructions ON SCHEDULE incurs some SCE…

## Slide 9: SCE is about ‘Change’… Controlling to Changes from one interval to another
1000
1100
5000
5100
Increase 100 MW, not 5100 MW
Increase 100 MW, not 1100 MW
  Both QSE’s are identical from AGC point of view.
  QSE B is NOT 5X more difficult to increase than QSE A.
  SCE is about schedule change, not total schedule.
QSE A
QSE B

## Slide 10: Two QSE Comparison
QSE A
Total Gen 500 MW
  500 MW GAS/STEAM
500 MW Controllable Units.
QSE B
Total Gen 1000 MW
  500 MW NUCLEAR
  500 MW GAS/STEAM
500 MW Controllable units identical to QSE A.
Controllable units of QSE A and B are identical.
Allowing QSE B twice the bandwidth is NOT justified.

## Slide 14: Conclusion
ERCOT Control depends on RGS. RGS providers need to be held responsible based on the amount of RGS they provide.
RGS service is free up to per Generation/Schedule ratio share and is prohibitive beyond it. This is OK only if we have no ERCOT market.
ERCOT needs a metric to measure all resource performance.