## Slide 1: Real Time Balancing (RTB) & Resource Plan Statuses
Change to the QSE practice of showing offline units as online and available
ERCOT Presentation to ROS 2/10/05

## Slide 2: Overview
Current RTB Process
Role of the Resource Plan
History of the RTB
Reasons for changing the RTB process
Market Impacts

## Slide 3: Current RTB Process
Executes14 minutes before the start of the interval
Calculates MCPE and amount of zonal deployment per QSE based on the aggregated Zonal Bid Stacks of QSEs
Validates volume of MWs bid by QSEs against their latest Resource Plan submission
Sends out QSE deployments 5-7 minutes before the start of the interval ramp

## Slide 4: Utilization of the Resource Plan
RTB verifies that the bid capacity is available by checking the resource plan
  Checks unit online status
  Checks unit availability
  Compares the calculated output of units derived from QSE base power schedule and compares output to Capability

## Slide 5: RTB History
RTB execution time moved from approximately 30 minutes before the start of the interval ramp to 5 -7 minutes before the start of the ramp
  Closer to real time execution benefited load forecasting accuracy to reduce the amount of procured/deployed regulation capacity
  Improved response time to local congestion through unit specific deployment instructions – meets NERC 30 minute requirement
Offline combustion turbine units were allowed to be shown as on-line and available because of the 30 minute lead time

## Slide 6: Reasons for changing the practice of allowing offline units to be shown online
PUC rules state that a market participant’s bids of energy and ancillary services shall be from resources that are available and capable of performing… 25.503(f)(2)(6)
PUC Rules state a market entity has an obligation to provide accurate and factual information and shall not submit false or misleading information. 25.503(f)(2)(8)

## Slide 7: Reasons for changing the practice of allowing offline units to be shown online
Lowers risk of failing NERC DCS Compliance
  Deployment of balancing energy from resources that are physically offline and unable to respond in 5 minutes could cause low frequency or depletion of RRS which could result in an ERCOT exposure if a large unit were to trip during this time period. Currently ERCOT observes this risk numerous times each day placing ERCOT at risk for these intervals.
Required for proper performance of the Replacement Market in Release 4
  Replacement utilizes the status in the Resource plan to order units on as needed and incorrect statuses will prevent proper commitment of resources necessary for reliable operations.

## Slide 8: Reasons for changing the practice of allowing offline units to be shown online
Compliance with Protocols and Operating Guides
  Protocol section 4.10.3 states: “The hourly Resource Plan status for a particular Generation Resource is compared to the corresponding real power telemetry values delivered to ERCOT’s SCADA by the QSE for the same Resource. “
  Operating Guide section 3.1.3.2 references Protocol Section 4.4.15 which states: “QSEs shall use best efforts, consistent with Good Utility Practice, to continually update their Resource Plans to reflect the current and anticipated operating conditions of the Resources.”

## Slide 9: Market Impacts
Removes offline GT capacity from the bid stack
Current analysis indicates approximately 2900 MW of capacity in December that wasn’t bid into the balancing market
Average deployed UBES per interval for the month of December was approximately 1090 MW
Average deployed DBES per interval for the month of December was approximately 645 MW
Average scheduled RMR per interval equaled 280 MW
Estimated average short load schedule per interval was 725 MW for the month of December

## Slide 10: Implementation Plan
Communicate change to the ROS & WMS
Market Notification
Begin monitoring adherence to the change on Thursday March 10th