## Slide 1: Impact of Profile Code Changes on Settlement Runs

## Slide 2: Annual Profile Validation Timing
Process begins in June of each year
Analysis conducted throughout the summer by ERCOT and TDSPs
ESIIDs requiring Profile ID change are identified by end of September
TDSPs update the Load Profile IDs in ERCOT system via Texas SET transactions such that the updated Profile IDs are effective on the first meter read date on or after October 1
TDSPs and ERCOT work together to have EDI transactions successfully completed by mid-November

## Slide 3: Timing of Settlements
Initial Settlement
  17 days after operating day
  Aggregation – 15 days after operating day
Final Settlement
  59 days after operating day
  Aggregation – 57 days after operating day
True-Up Settlement
  6 months after operating day (~180 days)
  Aggregation – 178 days after operating day

## Slide 4: Timing of Profile Changes and Settlement
Profile ID changes are effective on the first scheduled meter read date on or after Oct 1
Initial settlement aggregation is 15 days after operating day
TDSPs typically provide Profile ID changes in batches toward the end of October – not immediately after the October read occurs
Potential exists to have different profiles used between Initial and Final settlements
Occurs whenever the Profile ID change is not submitted and/or fully processed within the 15 day window between the operating day and the day the aggregation occurs
Shortening the time for initial settlement may increase this potential
Most likely to occur for operating days in first half of October

## Slide 5: Impact of Profile Changes and Settlement
Most likely to occur between initial and final
Changes between final and true-up are not common and generally occur as a result of a DEV resolution
Impact depends on the old and new assignments and the usage used to scale the profiles during aggregation
Aggregation uses the assignment in the production system for the operating day when that operating day is being settled

## Slide 6: Question:
Suppose ERCOT must use historical usage to estimate load because actual meter read is not available. If the ESIID was one load profile at the time of the historical usage and is another for the operating day being settled, which load profile should be used to calculate the usage factor?
Which load profile should then be multiplied by the usage factor to get the estimated load?

## Slide 7: Answer:
ERCOT always uses the assignment for the operating day being settled to calculate the usage factor and to scale the profile