## Slide 1: RTCA, CAM, and SFT Update
Presented by: John Adams
March 1, 2005

## Slide 2: Real-Time Contingency Analysis
Contingency Analysis that runs at regular 5-minute intervals, or upon demand, using the State Estimator Solution and Network Topology.
The RTCA Solution provides accurate and reliable information to the ERCOT Operators for Congestion Management purposes.

## Slide 3: Real Time Contingency Analysis

## Slide 4: Uses of RTCA
Identify areas of congestion, both local and zonal in post-contingency situations.
  This allows operators to mediate potential problems before a given contingency occurs (N-1 secure).
  Minimizes the potential for load loss or equipment damage when a contingency does occur.

## Slide 5: Simultaneous Feasibility Test
Prevents physical operating limits from being exceeded by constraining the optimized SPD solution during:
  Realtime Redispatch 14 min before start of each Interval (9 minutes before ramp starts)
Constraint Examples:
Lines at rated normal MVA loading with no contingencies
Lines at rated emergency limits during contingency outages

## Slide 6: SFT Overview
Inputs:
Network topology including all outages (SE or Outage Scheduler)
All MW injections including load and generation (SE & Loadflow)
Contingency Definitions for performing powerflow analysis
Processing:
Powerflow Analysis for normal and contingency outage conditions
Unit Shift Factors calculated for all overloads of normal and contingency emergency ratings in the network model.
Outputs:
Unit specific constraints fed back to SPD for the interval and limited to units with most significant shift factor impact (< threshold; currently 2%).

## Slide 7: The Problem with SFT
SFT Basic Flaw Encountered:
Constrains For ANY Overload Detected
Provides No User Interface Except On/Off
Unsuccessful implementation – required further development

## Slide 8: Constraint Activity Manager
SFT Gets An Overhaul
  SFT Chain Extends
  SE -> RTCA -> RTCAM -> SFT -> SPD -> QSE
  Display Customization Very Flexible

## Slide 9: Constraint Activity Manager
Greatly improved pro-active CM
Much more accurate “Shift Factors”
  Used in congestion management
Less OOM deployments

## Slide 10
Local Constraint Flowchart For Each Interval
State Estimator Solution With Current Network Topology / Loads
Power Flow Case with Network Topology and MW Injections
SPD
SFT Loadflow with
Contingency Analysis
Generates Limited Unit Specific Constraints
Optimized
Constrained
Dispatch for the Interval
Current System
Manually Entered Constraints (oc2)
QSE/CMZ Res. Plan & Real-Time Outputs
QSE Schedules and Bid (inc. BES)
Addition of CAM/SFT to Process
Iterate Once
RTCA
Basecase/Cont Overload Detect
CAM
Basecase/Contingency Overloads Selectable for Deploy
Old

## Slide 11: Constraint Activity Manager

## Slide 12: Market Operator Interface

## Slide 13: Impact on SPD
Only units online in the State Estimator are considered available to SPD in real-time balancing deployment
This means that the present practice of bidding off-line Gas Turbines into the balancing market will be rejected in the validation phase of the SPD analysis. (i.e. it cannot find sufficient generators to allocate the step 1 solution in order to analyze local congestion.
Current CAM design cannot be implemented if offline GT’s are allowed to bid into the Balancing Market.