## Slide 1: Facts About Local Congestion Costs
Congestion Management Working Group
Jerry Ward
February 24, 2005

## Slide 2: What Are Local Congestion Costs?
OOMC – ERCOT pays a generator that did not plan to be on-line to start and run at minimum.
OOME Up – ERCOT pays a generator to operate at a higher output than planned.
OOME Down - ERCOT pays a generator to operate at a lower output than planned.
RMR – Reliability Must Run – ERCOT pays a generator to be available and operate as directed when the owner would have otherwise suspended operation for an extended period of time.

## Slide 3: Local Congestion Costs ($ Millions)
 | 2003 | 2004
OOMC | $ 135.2 | $ 76.8
OOME Up | 52.2 | 19.0
OOME Down | 78.9 | 55.4
RMR | 138.8 | 119.5
TOTAL | $ 405.1 | $ 270.7

## Slide 4: Local Congestion Costs

## Slide 5: 2004 Congestion Cost $ Per MWh
 | $ Million | $/MWh
OOMC | 76.8 | 0.27
OOME Up | 19.0 | 0.07
OOME Down | 55.4 | 0.19
RMR | 119.5 | 0.41
TOTAL | 270.7 | 0.94

## Slide 6: Causes of Local Congestion
Congestion is caused by a mismatch of load and generation in a local area of the transmission system (sometimes referred to as a “load pocket” or a “generation pocket”).
ERCOT gathers congestion data based on which generator was paid.

## Slide 7: 2004 Local Congestion Cost Paid to Generators by Zone
Average = $0.94

## Slide 8: 2004 Local Congestion Costs Paid to Generators by Local Security Area
South Zone
North Zone
West Zone
Average = $0.94

## Slide 9: 2004 Local Congestion Costs Paid to Generators by Local Security Area
South Zone
North Zone
West Zone
Average = $0.94
$7.03
$0.98
$0.76
$0.04
$1.96
$1.06
$040
$15.87
$0.30
$0.37
$7.41

## Slide 10
The following is a backup slide in case a question about 2003 Local Congestion Cost/MWh is asked

## Slide 11: 2003 Congestion Cost $ Per MWh
 | $ Million | $/MWh
OOMC | 135.2 | 0.48
OOME Up | 52.2 | 0.18
OOME Down | 78.9 | 0.28
RMR | 138.8 | 0.49
TOTAL | 405.1 | 1.42