## Slide 1: PRR 485 Heat Adder
Wholesale Market Subcommittee
24 February, 2005
Brandon Whittle
Market Operations Support

## Slide 2: Objectives
WMS to recommend Heat Rate Adders.
Heat Rate Adder must be Approved by ERCOT Board before Release 4 implementation

## Slide 3: Agenda
Background of PRR 485
  Protocol Language
  Formulae for Bid Limit Calculations
Example of Bid Limit Calculations
  Discussion
Vote
  Heat Rate Adder Up Value
  Heat Rate Adder Down Value

## Slide 4: Background
Market Solution Suspended
WMS endorses Generic Cost Method plus Heat Rate Adder method (January 2004)
No decision made on what Adders to use
PRR 485 Passes with the Adders left for an appropriate TAC subcommittee to decide (April 2004)

## Slide 5: Protocols 4.4.20
(1) The Resource Category Generic bid limits for Balancing Energy Up for all gas-fired units will be calculated by multiplying the most recent FIP by the sum of a constant heat rate adder and the Resource Category heat rate, as used in the Resource Category Generic Fuel Cost calculation for upward instructions specified in Section 6.8.2.1, Resource Category Generic Cost.
(2) The Resource Category Generic bid limits for Balancing Energy Down for all gas-fired units will be calculated by multiplying the most recent FIP by the difference of a constant heat rate adder and the Resource Category heat rate, as used in the Resource Category Generic Fuel Cost calculation for downward instructions specified in Section 6.8.2.1, Resource Category Generic Cost.
(3) For all other Resource Categories, the Resource Category Generic bid limit for Balancing Energy Up and the Resource Category Generic bid limit for Balancing Energy Down will be calculated using the appropriate Resource Category Generic Fuel Cost calculation using the most recent FIP, if necessary, as specified in Section 6.8.2.1, Resource Category Generic Cost.
(4) The proposed value of the heat rate adder will be recommended by the appropriate TAC subcommittee and will be re-evaluated on a quarterly basis. The value of the heat rate adder must be approved by the ERCOT Board.
The Resource Category Generic bid limits for Balancing Energy Up for all gas-fired units will be calculated by multiplying the most recent FIP by the sum of a constant heat rate adder and the Resource Category heat rate…

## Slide 6: Formulae
Gas Fired Resource Categories (Combined Cycle, Simple Cycle, Gas-Steam, Diesel)
  Up Limit = (Heat Rate + Adder) * Fuel Index
  Down Limit = (Heat Rate – Adder) * Fuel Index
Other Categories
  Up and Down Limits = Heat Rate * Fuel Index
      or
    = Constant

## Slide 7: Example
Example Spreadsheet

## Slide 8: Discussion
Discussion
Vote
  Value of Heat Rate Adder Up
  Value of Heat Rate Adder Down