## Slide 1: EMMS Release 4
QSE PMWG
14 March, 2005
Brandon Whittle

## Slide 2: Agenda
Action Items from February meeting
Replacement Reserve Service (RPRS)
  Description of Testing
  Questions Received
Simultaneous Selection of Ancillary Services (AS)
  Description of Testing
Other Release 4 Questions
Notes: OOM – Out of Merit Order – The OOM tool is a generic term used to refer to the ERCOT operator mechanism to deploy OOME, OOMC, and now with R4 VDI and Fleet OOME.

## Slide 3: Action Items
Provide briefer version of XML Specification.
  In progress, should be available by end of the month.
Investigate feasibility of running User Acceptance Testing with Current RPRS model.
  No Mock Market Feasible in current Timeline
  Will provide some results of ERCOT testing

## Slide 4: Action Items
Investigate extent of RPRS results to be posted to MIS.
  6.6.3.2.1 (14) Quantity, MCPC, Shadow Prices
  6.5.10 PRR 515 information on OOMC
Report possible options for accessing daily resource specific bid premiums.
  Portal
  XML is scheduled for the next Release. It is not feasible for R4.
  QSE’s should be able to shadow the limits.

## Slide 5: RPRS
Three Step Clearing Process
  Local Congestion
  Zonal Congestion & System Balance
  MCPC Calculation
When?
  Day Ahead between 1600 and 1800
  Anytime During the Adjustment Period
Notes: MCPC – Market Clearing Price for Capacity - The highest price associated with a Congestion Zone for a Settlement Interval for Ancillary Service capacity awarded in each Ancillary Services capacity procurement run by ERCOT. There will be a separate Market Clearing Price for Capacity for each Ancillary Services capacity market. (Protocols 2)
Adjustment Period- The Adjustment Period for any given Operating Hour is the time period following the close of the Day-Ahead market and extending up to each Operating Period. (Protocols 2)
Timeline from ERCOT Protocols 4.1.1

## Slide 6: RPRS
Improvements?
  Temporal (Time) Constraints
    Startup Time
    Minimum Run Time
    Minimum Down Time
  24 Hour Optimization
    Opposed to 24 1 Hour Optimizations
    Proper treatment of Start Up Costs
  Suggestion Plan
    Operator intervention to (de-) select resources
    Information on non selected resources

## Slide 7: RPRS
Which Resources are Eligible for RPRS?
  Local Congestion – any generator resource offline and available will be eligible
  Zonal Congestion, Capacity – any offline and available generator or online, available, active LaaR resource with a RPRS bid.

## Slide 8: RPRS
What makes up an RPRS Bid?
  DAY – The Operating day for which the bid is submitted
  FIRSTHOUR – The first hour the bid is active
  LASTHOUR – The last hour the bid is active
  CAPACITY – The capacity in MW for the RPRS bid
  RSRC_ID – ID of Resource
  RSRC_TY – Type of Resource (GEN, UFR, CLD)
  CMZONE – Zone where the Resource is located
  STARTUP_PRICE – Capacity Price per MW
  PERHOUR_PRICE – Operational price per MW
  EXPIRATION_DATE – Date which bid expires
  EXPIRATION_TIME – Time which bid expires
  BES_BIDPOINT – Procured RPRS MW will be bid under this price
Notes: Startup cost will be calculated by RPRS. Startup cost will equal the Capacity Price per MW multiplied by the Capacity MW in the bid.

## Slide 9: RPRS Testing
Daily FAT (Factory Acceptance Test) Analysis
Daily SAT (Site Acceptance Test) Analysis
Planned ability to run R4 RPRS Market on current data.

## Slide 10: RPRS Questions I
What will be included in R4 MP training?
  What ERCOT expects as far as QSE communication, an overview of clearing engines, and any process changes.
What will the Congestion flag be used for in RPRS deployments?
  The congestion flag will be set if the RPRS deployment was for local congestion
What is the difference in Lead Time (RPRS Bid) and Startup Time (RP)?
  Lead time will not exist in the bids, per protocol

## Slide 11: Simultaneous A/S
Simultaneous Selection of Ancillary Services is equal to or less expensive than Sequential Selection.
New bidding rules for linked bids –
  RRS bid cannot exceed the URS bid by more than X%
    RRS bid <= URS bid + ( X/100 * URS bid)
  NSRS bid cannot exceed the RRS bid by more than X%
    NSRS bid <= RRS bid + (X/100 * RRS Bid)
Notes: Simultaneous Selection – All Ancillary Services are selected at the same time, based on QSE bids and ERCOT requirements. Cost is minimized using a linear program to perform the simultaneous selection.
Sequential Selection – Ancillary Services are procured in order – Up Regulation, Responsive Reserve, Non Spinning Reserve.

## Slide 12: Simultaneous A/S
Given: ERCOT needs 10 MW URS and RRS, X = 25
QSE A bids 10 MW; $9 URS, $5 RRS
QSE B bids 10 MW; $10 URS, $8 RRS
QSE C bids 10 MW; $15 URS, $30 RRS
Sequential (old) – $9 URS (QSE A), $8 RRS (QSE B)
$170 Total
Simultaneous (new) – $10 URS (QSE B), $5 RRS (QSE A)
$150 Total
 REJECTED
30 <= 15 + 25/100 * 15 = 18.75

## Slide 13: AS Testing
Extensive Testing performed on Market Clearing Engine
Starting this week we will be running the R4 AS Market concurrently with the production market.
  Results planned to be reported to WMS in April and May meetings.

## Slide 14: AS Testing
Sample Results 3/8/2005 Total Savings $13,980
 | DRS | URS | RRS
Production | 15.10 | 15.42 | 9.53
Release 4 | 15.10 | 15.55 | 8.95
Cost Savings | 0 | ($1,216.57) | $15,196.57

## Slide 15: Other Release 4 Questions
What resources can be specified as Non-Bid in the resource plan?
  RMR (Mandatory), QF, LaaR, Block Load Transfer, Nuclear, Renewable, and Hydro.
Must a unit which is classified as bid submit premium bids?
  No – System will consider the bid limit for a null bid.

## Slide 16: Other Release 4 Questions
Will ERCOT use the Reason field with Release 4?
  No.
Could ERCOT explain the scenarios that will require the use of the following OOME types? OOME, OOMC, OOMEVDI, OOMCVDI, etc?
  Please see XML documentation.

## Slide 17: References
Release 4 Functional Design Documents
  Available through your ERCOT Account Manager
Protocol Revisions
  PRR 342 A/S Simultaneous Selection
  PRR 413/491 Replacement Reserve Service

## Slide 18: Questions?