## Slide 1: Generation Adequacy Task Force Report to TAC
March 3, 2005

## Slide 2: Background
In February, TAC requested that a joint WMS/ROS Task Force be assembled to address issues surrounding the ERCOT reserve margin (e.g., treatment of “mothballed” generating units) and report back to TAC at the March meeting.
The scope of the group will be to “reexamine the reserve margin calculation and make recommendations on how to make calculations more representative of the actual situation.”
Steve Madden of StarTex Power was appointed chair of this group.

## Slide 3: Progress to Date
The GATF has held two meetings (Feb. 21 and Feb. 28) with at least one more meeting scheduled on March 11
Examined each of the following components of the ERCOT Reserve Margin calculation:
  Load Forecast
  Installed Capacity
  Load Participation
  Wind Generating Capacity
  “Mothballed” Capacity
  DC Tie Capacity
  “Switchable” Capacity
  Retired Capacity

## Slide 4: Current ERCOT Reserve Margin Calculation Methodology
Firm Load = Forecasted total summer peak demand – LaaRs – BULs
Resources = Installed Capacity (excluding wind generation)
+ 100% of DC Ties
+ 100% of “Switchable” Capacity
+ 10% of Wind Generation
+ 100% of Planned Generation (with signed Interconnect Agreement)
+ 10% of Planned Wind Generation (with signed Interconnection Agreement)
- 100% of “Mothballed” Units (first year of forecast only)
- 100% of Retiring Units (all forecast years)
Reserve Margin = (Resources – Firm Load)/Firm Load

## Slide 5: Load
ERCOT intends to use an econometric load forecast beginning with the next CDR calculation
LaaRs = 1,150 MW (no change, although some parties are advocating use of all registered LaaRs = 1,650 MW)
BULs = 0 MW (no change)

## Slide 6: Installed Capacity
Currently use capacity as shown in resource registration, as updated through a questionnaire last fall
Proposal:
  To use Net Summer Dependable Capability pursuant to ERCOT testing requirements instead of values based on resource registration
Impact: Reduces installed capacity by approximately 1,488 MW (<2%)

## Slide 7: Wind Generation
Currently use 10% of installed capacity
Proposal:
  Use actual historical hourly production data for the hours 16:00 – 18:00 for the months of July and August;
  weighted by installed capacity;
  apply a confidence level (to be determined – 80% to 95%) to account for intermittency; and
  use up to 10-years of actual data (currently, 3 years of data is available).
Impact: Likely to lower the 10% capacity value currently applied to wind (perhaps to as low as 2%)

## Slide 8: “Mothballed” Capacity
Currently assume that 100% of “mothballed” capacity is not available in the first year of the forecast and that 100% is available in the second through fifth years of the forecast
Issues Discussed:
  Decision to “mothball” or return a “mothballed” unit is primarily economic.
  Many drivers, including condition of unit, staffing, future market prices for energy, environmental permits, cost to return the unit to service, etc.

## Slide 9: “Mothballed Capacity”
Proposed methodology needs to address:
Technology differences
Amount of time mothballed
Amount of time needed to return to service (PRR 573)
Proposed Solution:
Develop a “probability” matrix taking into account the above attributes

## Slide 10: “Mothballed Capacity”
 | No. of Years Mothballed |  |  |  |  | 
Technology | 1 | 2 | 3 | 4 | 5 | 6
Steam Non-Reheat | 40% | 40% | 20% | 0% | 0% | 0%
Steam Reheat | 50% | 50% | 30% | 10% | 0% | 0%
CCCT | 75% | 75% | 55% | 35% | 15% | 0%
CT | 80% | 80% | 60% | 40% | 20% | 0%

## Slide 11: Example
Assume: A 120 MW steam reheat unit has been “mothballed” for 2 years. The lead-time to return the unit to service is 6 months. ERCOT is preparing this forecast in October, looking at the next calendar year as Forecast Year 1.
What “mothballed” capacity will be included in the ERCOT reserve margin calculation for this unit?

## Slide 12
In forecast year 1, the unit will have been mothballed for 3 years, thus, from the Mothball matrix 30% is selected. The lead-time to return the unit to service is 6 months which could occur in April, well ahead of the June to September peak load season and therefore, would have no impact.
Answer: Use 120 MW x 30% = 36 MW for each year of the forecast period for this unit.
Forecast Year 1