## Slide 1: Two DRS Scheduling Issues
Are these considered over-scheduling issues?
Should the “Down Bid & Obligation Measure” be changed in the Protocols?

## Slide 2: Two Issues:
DRS Scheduling Issue #1:
  The Scheduling of DRS to a Specific Plant/Unit
DRS Scheduling Issue #2:
  A Conflict Between Morning Ramp Scheduled in 15-Minutes Intervals and Passing the Hourly “Down Bid & Obligation Measure”

## Slide 3: DRS Scheduling Issue #1: Example Data
A | B | C | D | E | F | G | H | I | J | K
HE | Zone | EneSch | LSL | DB% | MandBid | ActBid | DRS | C-D-F-H | C-D-G-H=0 | G ≥ F
13:00 | A | 325 | 275 | 0.12 | 39 | 40 | 10 | 9 | True | True
 | B | 725 | 625 | 0.12 | 87 | 95 | 5 |  | True | True
 | must meet zonal DBES requirement |  |  |  |  |  |  |  |  | 
14:00 | A | 325 | 275 | 0.12 | 39 | 40 | 10 | -1 | True | True
 | B | 725 | 625 | 0.12 | 87 | 85 | 15 |  | True | False
 | bid all available into DBES |  |  |  |  |  |  |  |  | 
15:00 | A | 320 | 275 | 0.12 | 38.4 | 35 | 10 | 4.6 | True | False
 | B | 725 | 625 | 0.12 | 87 | 95 | 5 |  | True | True
 | must meet zonal DBES requirement |  |  |  |  |  |  |  |  | 
16:00 | A | 320 | 275 | 0.12 | 38.4 | 35 | 10 | -5.4 | True | False
 | B | 725 | 625 | 0.12 | 87 | 85 | 15 |  | True | False
 | bid all available into DBES |  |  |  |  |  |  |  |  | 

## Slide 4: DRS Scheduling Issue #1: Background Information
This QSE has 1 plant in each zone
The QSE assigned 10 MWs of DRS to the Plant in Zone A
The QSE assigned 5 MWs of DRS to the Plant in Zone B (plus a 10 MW DRS award for HE 14:00 & 16:00)

## Slide 5: DRS Scheduling Issue #1: Calculation of the Down Bid & Obligation Measure
The Column I Calculation (C-D-F-H) is uses by ERCOT to score the Down Bid & Obligation Measure
  If the score is positive, then the DBES requirement is scored at the Zonal Level (13:00 & 15:00)
  If the score is negative, then the DBES requirement is scored at the ERCOT-wide Level (14:00 & 16:00)

## Slide 6: DRS Scheduling Issue #1: Did this QSE pass?
Column J shows that this QSE committed all of its Down Capability into either the DRS Market or the DBES Market.
Column K shows a comparison between the Mandatory Bid Amount and the Actual Bid Amount
This QSE failed Hour Ending 15:00

## Slide 7: DRS Scheduling Issue #1: Should the Protocol be Changed?
What if a QSE automatically passed the “Down Bid & Obligation Measure” if it committed all its “Down” Capacity into either the DRS or the DBES Market?
  Would this put an unfair strain on Zonal DEBS needs in ERCOT?
  Should the QSE be allowed to make a commercial decision to schedule DRS in a specific zone (even though ERCOT looks at DRS ERCOT-wide)?

## Slide 8: DRS Scheduling Issue #2: Example Schedule Data for HE 6:00
Zonal Energy Schedule for the QSE
  5:15 – 120 MWs
  5:30 – 140 MWs
  5:45 – 160 MWs
  6:00 – 180 MWs
DRS Obligation for the QSE = 20 MWs

## Slide 9: DRS Scheduling Issue #2: Example Resource Plan for HE 6:00
Unit A:
  Energy = 100 MWs (each interval)
5:15 = 100, 5:30 = 100, 5:45 = 100, 6:00 = 100
  LSL = 80 MWs (actual value & DRS)
Unit B:
  Energy = 50 MWs (average value due to ramp)
5:15 = 20, 5:30 = 40, 5:45 = 60, 6:00 = 80
  LSL = 50 MWs (average value due to ramp)

## Slide 10: DRS Scheduling Issue #2: ERCOT Resource Plan Adjustment for 5:15
Zonal Schedule = 120 MWs
Unit A:
  Original Schedule = 100 MWs
  Adjusted Schedule = 80 MWs
  LSL = 80 MWs
Unit B:
  Original Schedule = 50 MWs
  LSL = 50 MWs
QSE cannot meet its DRS Obligations

## Slide 11: DRS Scheduling Issue #2: ERCOT Resource Plan Adjustment for 5:30
Zonal Schedule = 140 MWs
Unit A:
  Original Schedule = 100 MWs
  Adjusted Schedule = 90 MWs
  LSL = 80 MWs
Unit B:
  Original Schedule = 50 MWs
  LSL = 50 MWs
QSE cannot meet its DRS Obligations

## Slide 12: DRS Scheduling Issue #2: ERCOT Resource Plan Adjustment for 5:45
Zonal Schedule = 160 MWs
Unit A:
  Original Schedule = 100 MWs
  Adjusted Schedule = 105 MWs
  LSL = 80 MWs
Unit B:
  Original Schedule = 50 MWs
  Adjusted Schedule = 55 MWs
  LSL = 50 MWs
QSE can meet its DRS Obligations

## Slide 13: DRS Scheduling Issue #2: ERCOT Resource Plan Adjustment for 6:00
Zonal Schedule = 180 MWs
Unit A:
  Original Schedule = 100 MWs
  Adjusted Schedule = 115 MWs
  LSL = 80 MWs
Unit B:
  Original Schedule = 50 MWs
  Adjusted Schedule = 65 MWs
  LSL = 50 MWs
QSE can meet its DRS Obligations

## Slide 14: DRS Scheduling Issue #2: Resolving the Conflict
If the QSE schedules its LSL lower on Unit B, then it fails the “Down Bid & Obligation Measure.”
If the QSE does not adjust it LSL on Unit B and ERCOT needs DRS, then ERCOT Operations calls to say “DRS Obligations cannot be meet.”
EMMS Release 4 can help, but it will mean many Resource Plan submittals during the ramp hour.