## Slide 1: Shadow Price Cap Study
Market Operations Support
ERCOT
April, 2005

## Slide 2
Contents
Background
  Issue - Inefficient Deployment of BES
  Proposed Methods
Study
  “Selected” Cases
  One Month Cases
Study Results
Implementation

## Slide 3
Background
Issue: Inefficient BES deployments when resolving zonal congestion
2 proposed methods to reduce inefficient deployments :
  Averaging of similar shift factors
  Shadow Price Cap
History:
  Averaging Shift Factor method: Oct 2004 WMS
  2 proposals: Nov 2004 ORG
  Shadow Price Cap method: Jan 2005 WMS
  Presenting results in detail : March 1, 2005 ORG
    After discussion in ORG, proposal of Shadow Price Cap was recommended;
    Further study with Shadow Price cap was suggested.
ERCOT
  To continue to study Shadow Price Cap proposals;
  To present results in detail at WMS.

## Slide 4
Shadow Price Cap
Determine value of Shadow Price (SP) cap
Set penalty factor of constraint violation = shadow price cap
  For CSC, the SP cap acts as system’s stopping point
Shadow price cap (penalty factor) | Current ($/MW) | SP cap 1 ($/MW) | SP cap 2 ($/MW)
Portfolio Ramp Rate | 75,000 | 1,001 | 1,001
OC3 (contingency) | 250,000 | 3,000 | 3,000
OC2 | 500,000 | 3,000 | 3,000
OC1 (CSC) | 750,000 | 4,500 | 2,500
OC3 (base case) | 1,000,000 | 100,000 | 100,000
Power Balance | 5,000,000 | 5,000,000 | 5,000,000

## Slide 5: Lowering the CSC SP Cap
CSC SP cap 4500 $/MW:
  Goal is to deploy all bids from zones which have the most effect on the congested CSC.
  It was observed that bid stacks in the most effective zones are frequently exhausted (either UBES or DBES) leading to use of bids from less effective zones.
CSC SP cap 2500 $/MW:
  2500 cap is large enough to deploy all bid pairs from most effective zones;
  Benefit:
    Decreases amount of inefficient deployment for zonal congestion (MW and cost);
    (Potentially could help to eliminate Price Admin).

## Slide 6
ERCOT Study
Run production cases using proposed Shadow Price Caps;
  “Selected” cases
    All intervals with violation (price administration) and CSC Congestion (after R3)
      46 Cases from June 2, 2004 to Dec 31, 2004
    All intervals with CSC shadow price > $1000 (after R3)
      10 Cases from June 2, 2004 to Dec 31, 2004
  All intervals of one month (Sept. 2004)
    2879 Cases of September 2004
Compare study results with production results
  Two different caps of Shadow Price (WMS)

## Slide 7: Selected Case Results – 1: BES MW Deployment
Selected cases | # Intervals | Original BES (MW) | SP Cap 1 |  | Sp Cap 2 | 
 |  |  | BES (MW) | Diff. (%) | BES (MW) | Diff. (%)
Violation & CSC congestion | 46 | 3746 | 3339 | 11.1 | 3327 | 11.4
SP > $1000 | 10 | 2680 | 2577 | 3.8 | 2548 | 4.9
Average change of BES Deployment

## Slide 8
Selected Case Results – 2: CSC Shadow Price
Average change of CSC Shadow Price
Selected cases | # Intervals | Original CSC SP ($/MW) | SP cap 1 |  | SP cap 2 | 
 |  |  | SP ($/MW) | Diff. (%) | SP ($/MW) | Diff. (%)
Violation & CSC congestion | 46 | 622.0 | 475.1 | 23.6 | 469.1 | 25.6
SP > $1000 | 10 | 1480.3 | 991.7 | 33.0 | 989.7 | 33.1

## Slide 9
Selected Case Results – 3: BES Deployment Cost
Average change of BES deployment Cost
Selected cases | # Intervals | Original Cost | SP cap 1 |  | SP cap 2 | 
 |  |  | Cost | Diff. (%) | Cost | Diff. (%)
Violation & CSC congestion | 46 | 43.0 | 26.9 | 39.5 | 25.8 | 40.2
SP > $1000 | 10 | 205.6 | 177.6 | 13.6 | 177.0 | 13.9
Note: the costs are in thousands dollars.

## Slide 10: Sep 2004 cases
# of intervals | description
226 | CSC congestion
1073 | Local congestion
14 | *09/06 Local Congestion (deploy very small shift factor units for local congestion)
1721 | No congestion

## Slide 11: BES Deployment decrease
 | # Intervals | Original BES (MW) | SP cap 1 |  | SP cap 2 | 
 |  |  | BES (MW) | Diff. (%) | BES (MW) | Diff. (%)
CSC cong. | 226 | 2972.2 | 2972.4 | 0.0 | 2973.3 | 0.0
Local cong. | 1159 | 3031.6 | 3010.9 | 0.7 | 3011.1 | 0.7
09/06 | 14 | 5168.5 | 3677.5 | 28.8 | 3677.5 | 28.8
No cong. | 1646 | 1859.4 | 1859.4 | 0.0 | 1859.4 | 0.0
Sep. 2004 | 2879 | 2340.4 | 2332.2 | 0.4 | 2332.2 | 0.4

## Slide 12
Study Conclusions
With both proposed SP Caps, there is a great decrease in BES deployment for those intervals with inefficient BES deployment for CSC congestion.
Both proposed methods have small impact on all other intervals.

## Slide 13
Implementation – Shadow Price Cap
ERCOT will issue a market notice describing the new Shadow Price Cap;
The BES deployment will stop at a set point;
This proposed method does not require a system change (no implementation cost).

## Slide 14: Example
Interval: 04/01/2005 21:15
CSC Congestion: North-West
CSC limit: 430 MW;
Shadow Price: 5797.6 $/MW
Local Congestion: No
Price Admin: No

## Slide 15: BES Deployment
Zone | SF* | Original |  | Shadow Price Cap1 (2500) |  | Shadow Price Cap 2 (2500) | 
 |  | UBES (MW) | DBES (MW) | UBES (MW) | DBES (MW) | UBES (MW) | DBES (MW)
Houston | -0.0183 | 552 | 0 | 375 | 0 | 193 | 0
North | -0.0111 | 33 | 483 | 33 | 296 | 33 | 278
Northeast | -0.0032 | 0 | 554 | 0 | 554 | 0 | 304
South | -0.0303 | 532 | 61 | 520 | 61 | 434 | 61
West | -0.3969 | 0 | 0 | 0 | 0 | 0 | 0
Total |  | 1117 | 1098 | 928 | 911 | 660 | 643
*Subject to N-W congestion

## Slide 16: MCPE & Shadow Price (SP)
 | Original | Shadow Price Cap 1 (4500) |  | Shadow Price Cap 2 (2500) | 
Zone | MCPE ($/MWh) | MCPE ($/MWh) |  | MCPE ($/MWh) | 
 |  | With PA | No PA | With PA | No PA
Houston | 68.89 | 68.35 | 68.35 | 53.98 | 53.99
North | 27.15 | 35.99 | 35.95 | 35.99 | 35.99
Northeast | -18.65 | 10 | 0.40 | 40.21 | 16.24
South | 138.46 | 122.22 | 122.35 | 83.82 | 83.99
West | 2263.85 | 59.14 | 1772.1 | 53.5 | 1000.5
CSC | SP ($/MWh) | SP ($/MWh) |  | SP ($/MWh) | 
 |  | With PA | No PA | With PA | No PA
N-W | 5797.6 | 61.2 | 4500 | 46.3 | 2500

## Slide 17: BES & Flow
04/01/05 21:15 | BES Deployment |  |  | Calculated Flow Violation (N-W) |  | 
 | MW | Decrease |  | MW | Increase | 
 |  | MW | % |  | MW | %
Original | 2215 |  |  | 430 |  | 
SP Cap 1 (4500) | 1839 | 376 | 17.0 | 431 | 1 | 0.2
SP Cap 2 (2500) | 1303 | 912 | 41.2 | 436 | 6 | 1.4

## Slide 18
Questions