## Slide 1: SCE performance and Regulation Cost Reallocation
PUC Wholesale Market Oversight
WMS Meeting
April 23, 2004

## Slide 2: Issues PRR 586 aims to address
Morning and Evening Ramps cause dramatic frequency fluctuations, forcing ERCOT to deploy large amounts of REG DOWN and REG UP to maintain power balance and system reliability
QSEs submit schedules that don’t match increases and decreases in loads, resulting in large balancing energy deployments
However, these schedules are often infeasible: QSEs cannot ramp to their schedules, forcing ERCOT to deploy regulation during the interval to restore frequency

## Slide 3: The Issue
5:45 6:00 6:15 6:30 6:45 7:00
Targeted Output Level
MW
Time
Hourly Schedule
Actual Output Level
Regulation-Up Deployment
Balancing-down

## Slide 4: Percent of Intervals with Large Need for Regulation Jan-Sep 2004

## Slide 5: Potomac’s Recommendation 11
Implement uninstructed deviation charges that allocate a portion of the regulation costs to the QSEs exhibiting large SCEs in the periods during each hour with the largest regulation needs. In particular, we propose specific changes to PRR 356 that have been pending for more than two years. (pp. 28, 126)

## Slide 6: Uninstructed Deviation Charge (URC)
“The current URC primarily addresses “price chasing” but does not provide meaningful disincentives for QSEs to minimize SCE that increase regulation needs and costs”
During August 18, 2004 DCS event, ERCOT-wide URC charges totalled around $4,690 for the whole day
On February 13, 2005, ERCOT System Frequency dropped below 60 Hz for nearly thirty minutes, the ERCOT-wide URC charges was only $2,234 for that day

## Slide 7: URCs in March 2005

## Slide 8: PRR 525 Measures
CPS1: The one (1) minute averages of the QSE’s SCE
CPS2: The ten (10) minute averages of the QSEs’ SCEs
This PRR introduces a SCE measurement for all scheduling QSEs and establishes a standard. QSEs that do not meet the standard would be informed of such, and if they fail 3 out of 6 months, ERCOT could suspend their right to provide A/S.

## Slide 9: Shortcomings of PRR 525
CSP1 may always be met because negative SCEs and positive SCEs will tend to cancel each other out when averaged out
Cannot solve the 6:00 and 22:00 issues
  Some QSEs exhibit SCEs that are small for most of the day but exhibit an upward spike around 6:00 and a downward spike around 22:00, therefore could pass the 90% test
  No financial penalty

## Slide 10: PRR 586 Mechanism (1)
  Calculates an Ancillary Service Demand Factor for each QSE based on the system need for regulation (reg deployment – ACE) and the QSE’s SCE on a one minute basis
  ASDFqi = Sum [(-1) (ISCEqm) (REGNm)]
  Provided that if in any minute, (ISCEqm*REGNm) for a QSE is less than zero, then (ISCEqm*REGNm) is set to zero for that QSE for that minute; and
  Provided that if in any minute, total aggregated ISCEqm of all QSEs is less than 100 MW and greater than -100 MW, then REGNm is set to zero for that minute.

## Slide 11: PRR 586 Mechanism (2)
Sum all ASDFqi to obtain the total A/S demand factor TASDFi, and calculate the ratio:
Allocation factor = ASDFqi/TASDFi
Calculate A/S Cost Reallocation (ASCR) for each QSE for each interval based on the Interval Equivalent Cost of A/S (IECAS)
ASCRqi = IECASi * Allocation factor
Where IECAS is 50% of the cost of regulation for the interval, based on MCPC times REG MW procured during the hour containing the interval

## Slide 12: PRR 586 Fairness Provisions
  If a QSE’s SCE helps frequency in any minute, the ASDF for that QSE for that minute is set to zero
  Tolerance band: if ERCOT wide SCE is between 100 MW and -100 MW, ASDFqm are set to zero for that minute
  Appropriate adjustments in case of ERCOT instructions

## Slide 13: PRR 586 Next step:
We requested that ERCOT do a back cast analysis. Based on results, we may
  Refine the formula
  Consider QSE specific tolerance band
  Adjust ERCOT-wide dead-band
  Make other adjustments if necessary to ensure fairness

## Slide 14: Time line for PRR 586
To meet Commission’s expectations:
April-May: Back cast analysis results and modifications as necessary
May: PRS Vote, TAC vote
June: Board Vote