## Slide 1: Revised Approach to A/S Block Bidding
Simplified 3 Part Bidding

## Slide 2
Why We’re Here
Understand the problem
Understand the solutions
Help define a preferred solution

## Slide 3
Definition of the problem
Current AS bidding structure is one dimensional: Capacity bid price
Doesn’t acknowledge other costs that may be required to provide capacity
  Startup
  Minimum running costs
  Other
Offers must be boosted up to account for these costs
Due to the risk, sellers guess high or don’t bid

## Slide 4
Two solutions investigated
Block bidding
  Original PRR structure
  Improves bidding, but problems still exist
“Simplified” 3-part bidding
  Allows bidders to discreetly capture other costs
  Uses mechanism similar to that of the SCUC in PJM’s current DAM and TNT’s future DAM

## Slide 5: How a Block Approach Would Work
Bidders would be able to define:
  minimum block size
  minimum hours of operation
To determine how to divide costs into an appropriate bid, the equation is:
  Startup cost/MW/hr + Min. Run cost/MW (in each hour) + variable costs including margin
  For example:
    Startup = $5000
    Min. Run = $1000/hr.
    Variable cost = $10/MW
    Bid for 100MW of A/S for a 5 hour block =
    5000/100/5 + 1000/100 + 10 = $30/MW

## Slide 6: Variable Problems
The variables in the previous equation are:
  Size of the block in MWs
  Duration of the block in hrs
  Selection of which hrs in the day to target
Missing on any of the above variables puts your capacity out of the market
Can’t provide multiple bids with the same capacity (may get struck more than once) without ability to link bids
There is a better solution

## Slide 7: “Simplified” Three Part Bidding for A/S
QSE would be able to submit offers defining:
  Startup cost
  Min. run hours
  Min. down hours
  Min. loading cost
  Var. cost offer curve for capacity
  Max. capacity
Then allows the systems to determine the best mix of hours and volumes
Optimization algorithms far simpler than SCUC
  No transmission analysis
  No contingency analysis
  Only capacity level required with offers provided

## Slide 8
QSE Requirement
Input all Self Provided A/S capacity (same as today)
Input Offer Curve for capacity: $/MW (same as today)
  Same method used today
Input Start Cost: $/Day (new)
  No verification of actual start (could be related to call option execution)
  Default of $0 will be used if QSE doesn’t provide specific offer
Input Min. Run Time: Hrs (new)
  Prevents a unit from being started for a single hour
Input Min. Down Time: Hrs (new)
  Prevents a unit from being double cycled faster than is physically possible
Input Min. Loading Cost: $/Hr (new)
  Applies to each hour the bid is struck
  Allows QSE make whole if small amount of A/S struck (running at 100MW minimum for a 10MW award)
  Default of $0 will be used if QSE doesn’t provide specific offer
Input Max. Capacity: MW (new)
  Allows entity to set maximum size of block bid of each A/S product (max. 400 MW)
Min Capacity: hardwired to 0 MW

## Slide 9
Bidding Requirements
Any bids using new features must be separated out as individual bids
Bids using the current bid curve only, may continue to be bid as one large portfolio

## Slide 10
ERCOT’s Responsibility
Determine the lowest cost alternative for A/S capacity among the offers provided
Evaluate any Make Whole requirements
Determine allocation amount
Settle market

## Slide 11
Example 1 – Steam Turbine 3 Part Bid (Bringing in a single additional unit)
3 Part Bids are specified by a set of daily parameters and a set of hourly parameters.
Will only be struck by ERCOT when it lowers the over all system cost of the A/S market.

## Slide 12
Example 2 – CCCT 3 Part Bid (Bringing in a single additional unit)
3 Part Bids are specified by a set of daily parameters and a set of hourly parameters.
Will only be struck by ERCOT when it lowers the over all system cost of the A/S market.

## Slide 13
Ex. 1 & 2 – RegUp Clearing Price Impact (Each Example Was Cleared Separately)

## Slide 14
Ex. 1 & 2 – RegUp Deployment Chart (Each Example Was Cleared Separately)

## Slide 15
Ex. 1 & 2 – RegUp System Cost (Each Example Was Cleared Separately)

## Slide 16
Make Whole Allocation
Propose all make whole amounts be divided among all PURCHASED MWs in A/S market
  Self provided MWs not affected
  Most if not all purchasers in A/S market are in market full day
Example:
  $8200 make whole
  1000MW market over 24 hours
  Results in a 34 cent charge on every MW purchased in the A/S market

## Slide 17
Take-aways from meeting
Allocation of Make-whole
Benefits are apparent
Cost – need more study
Feasibility – doable but not simple

## Slide 18
Recommended Motion
PRS direct ERCOT to prepare a more detailed analysis of costs to implement PRR567 and a development time estimate.