## Slide 1: 2005 ERCOT Annual Seminar Resource Plans
Keith E. Emery
Tenaska Power Services Co.

## Slide 2
1. Identify the method used by ERCOT to derive the QSEs Compliance Score for each of the following metrics.
a. Resource Status
b. Resource LSL as a Percent of High Sustainable Limit
c. Day Ahead Zonal Schedule
d. Adjustment Period Zonal Schedule
e. Down Bid and Obligation
f. Total A/S Scheduled Obligation
2. Explain the benefit to ERCOT Inc. intended by Resource Status.
Objectives
Resource Plans

## Slide 3
Objectives
Resource Plans
3. Explain the benefit to ERCOT Inc. intended by Resource LSL as a Percent of HSL.
4. Explain the benefit to ERCOT Inc. intended by Day Ahead Zonal Schedule.
5. Explain the benefit to ERCOT Inc. intended by Adjustment Period Zonal Schedule.
6. Explain the benefit to ERCOT Inc. intended by Down Bid and Obligation.

## Slide 4
Objectives
Resource Plans
7. Explain the benefit to ERCOT Inc. intended by Total Up A/S Scheduled Obligation.
8. Identify the benefit to the ERCOT market intended by Resource Status.
9. Identify the benefit to the ERCOT market intended by Resource LSL as Percent of HSL.
10. Identify the benefit to the ERCOT market intended by Day Ahead Zonal Schedule.

## Slide 5
Objectives
Resource Plans
11. Identify the benefit to the ERCOT market intended by Adjustment Period Zonal Schedule.
12. Identify the benefit to the ERCOT market intended by Down Bid and Obligation.
13. Identify the benefit to the ERCOT market intended by Total Up A/S Scheduled Obligation.

## Slide 6
Resource Plan Definition
  “A plan provided by a QSE to ERCOT indicating the forecast state of Generation Resources or individual Loads each acting as a Resource, including information on availability, limits, and forecast generation or Load of each Resource.” (Protocols 2.1)
  “The Resource Plan capacity should be sufficient to accommodate … energy and Ancillary Services scheduled by that QSE from the Resources that the QSE represents … shall indicate the availability of the Resources represented by the QSE, including a lead-time status code, and the planned operating level of each Resource, for each hour of the Operating Day.” (Protocols 4.4.15)
Resource Plans
Definition

## Slide 7
Cold weather event - February 2003
  During February 24-26, 2003, an extreme cold weather event affected the ERCOT region
  Discrepancies between Resource Plans and Balancing Energy bids may have been a factor
  Generation Resources which were de-rated due to fuel curtailments may not have been accurately reflected in the Resource Plan
Resource Plans
Reason for Metrics

## Slide 8
Protocol Revision Implemented on 9/1/2004 (PRR 520)
  Initiated by findings of PUCT investigation into February 2003 freeze event
  Set specific criteria to measure Resource Plan accuracy
  Increased ERCOT’s confidence in RP data
Resource Plans
Reason for Metrics

## Slide 9
Protocol 4.10 Defines RP Metrics
  Minimum acceptable performance – 90% monthly score per measure
    More than 3 consecutive months below 90% = failure
    ERCOT will work with individual QSEs to improve performance
  ERCOT considers exceptions on a case-by-case basis, but are only applied (manually) if measure is below 90%
  Scores are available through Client Representative (by 10th of each month)
Resource Plans
Compliance

## Slide 10
ERCOT calculates a monthly score for each measure:
  QSE Measure Score = 1 –
Resource Plans
Scoring
# of Occurrences
Total # of Monthly Samples

## Slide 11
Resource Plans
Inputs
Resource Plan Input | Units | Description
Planned Net MW | MW | The Resource's Planned MW Level
Ramp Rate | MW / Minute | Resource's 10-minute ramp rate, expressed in MW per minute
Resource Type | GEN | Generation Resources
 | UFR | Underfrequency Relay (LaaR qualified to provide RRS)
 | CLD | Controllable Load (LaaR qualified to provide BES)
 | ILD | Interruptible Load (LaaR qualified to provide NSRS)
Resource ID | ERCOTGEN_G1 | The unique Resource ID code for each registered Resource represented by the QSE
Resource On | Yes / No | Denotes whether Resource is on-line

## Slide 12
Resource Plans
Inputs (cont)
Resource Plan Input | Units | Description
Resource Available | Yes / No | Denotes whether Resource is available
Resource Active | Yes / No | Only applies to LaaR - Yes means LaaR providing BES or A/S. No means LaaR available for RPRS
Non Spin | Yes / No | Denotes whether Resource is providing Non-Spinning Reserve Service
LSL (Low Sustainable Limit) | MW | The minimum net dependable capability of a resource that may be delivered for an indefinite period
HSL (High Sustainable Limit) | MW | The maximum net dependable capacity of a Resource that may be delivered for an indefinite period
Inc Premium | $/MW | Resource Category Generic Up Price ($/MW)
Dec Premium | $/MW | Resource Category Generic Down Price ($/MW)

## Slide 13
Resource Plans
Inputs (cont)
Resource Plan Input | Units | Description
LOL (Low Operating Limit) | MW | The minimum net dependable capability of a resource that may be delivered for a period of up to one hour
HOL (High Operating Limit) | MW | The maximum net dependable capability of a Resource that may be delivered for a period of up to one hour
Resource Condition | U | Unrestricted
 | M | Maintenance
 | RE | Restricted Emission
 | RF | Restricted Fuel
 | RP | Restricted Physical Limit
 | RO | Restricted Other
 | NR | Not Released
 | T | Testing
Cycle Time | Starts | Number of annual starts (365 means 1 start a day, 52 means 1 start a week, 12 means 1 start a month)
Startup Time | Hours | Number of hours prior to start (5 means 5 hours, 0.5 means 30 minutes, 0 means already on-line)

## Slide 14
Resource HSL
Total
UBES
Bids
Avail.
UBES
Bids
Energy Schedule
Available UBES Bid Based on Resource Plan
Resource Plans
Resource LSL
Up Ancillary Service Schedule
Resource HOL
Resource LOL
OOME Range
Avail BES Range

## Slide 15
Resource LSL
Total
DBES
Bids
Avail.
DBES
Bids
Energy Schedule
Resource Plans
Available DBES Bid Based on Resource Plan

## Slide 16
Total
UP AS
Schedule
Avail.
UP AS
Schedule
Energy Schedule
UBES Deployment
Resource Plans
Available Up-AS Schedule Based on Resource Plan
Resource HSL
Resource LSL
Resource LOL
Resource HOL
OOME Range
Avail BES Range

## Slide 17
Total
DRS
Schedule
Avail. DRS
Schedule
Energy Schedule
DBES Deployment
Resource Plans
Available DRS Schedule Based on Resource Plan
Resource LSL

## Slide 18: Resource Plans
Compares Resource Plan status to the telemetered Resources status.
Inputs:
  Last Resource Plan submitted before the Operating Hour
  MW telemetry transmitted to ERCOT by the Resource’s QSE (12 5-minute averages in 1 hour)
  Combined Cycle Units that are ERCOT-approved Aggregated Units are treated as a single unit in this measure.
Resource Status Measure
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Resource Plans
Exclusions:
  Non-telemetered Resources
  Loads Acting as a Resource (LaaR)
  Generation Resources under test
  Renewable Resources
  Units with “Online” Status in RP and Planned MW of Zero (0)
Results:
  QSE score calculated for each Resource, by hour, summed monthly.
Resource Status Measure (cont)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Resource Plans
ERCOT Benefit
  ERCOT relies on accurate Resource Status to know where and when Resources are online throughout the system to reliably operate
Market Benefit
  Helps avoid inaccurate Balancing Energy clearing prices
  Increased efficiency of ERCOT operations (lower costs) is achieved through consistency between planned and actual resource behavior
Resource Status - Benefits
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Resource Plans
Compares the LSL/HSL range in the Resource Plan with pre-defined ranges.
Inputs:
  Last Resource Plan submitted before the Operating Hour
  Hours with HSL greater than zero (0) MW
  Hours with “On-Line” Resource Status
Exclusions:
  Loads Acting as a Resource (LaaR)
  Generation Resources under test
  Renewable or Hydro Resources
Results:
  QSE score calculated for each Resource, by hour, summed monthly
Resource LSL/HSL Percent Measure

## Slide 22: Resource Plans
Resource types (Section 6.8.2.1(1)) LSL % of HSL
  Qualifying Facilities As approved
  Nuclear 70
  Hydro N/A
  Coal and Lignite 60
  Combined Cycle greater than 90 MW 85
  Combined Cycle less than or equal to 90 MW 85
  Gas-Steam Supercritical Boiler 40
  Gas-Steam Reheat Boiler 40
  Gas-Steam Non-reheat or boiler w/o air-preheater 40
  Simple Cycle greater than 90 MW 90
  Simple Cycle less than or equal to 90 MW 90
  Diesel (and all other diesel or gas-fired Resources) 90
  Renewable (i.e., non-Hydro renewable Resources) N/A
  Block Load Transfer N/A
Resource LSL/HSL Percent Measure

## Slide 23: Resource Plans
ERCOT Benefit
  ERCOT relies on realistic and accurate Resource LSL/HSL information to be able to manage load forecast uncertainty
  ERCOT System needs accurate operating range in order to perform least cost dispatch when resolving congestion
  ERCOT Operators need to be confident of the operating range shown in the Resource Plan in order to OOM or VDI Resources as necessary in case of an emergency
Market Benefit
  Overall market costs are lowered since ERCOT is able to procure and utilize Resources more efficiently with accurate Resource LSL/HSL information – can help to minimize cost / quantity of OOM instructions
Resource LSL/HSL Percent - Benefits

## Slide 24
Compares zonal energy schedule with planned Resource operating level
Inputs:
  Uses the first validated day ahead Resource Plan
  Hours with zonal energy schedule greater than zero (0) MW
  Hours with a difference of the greater of 2% or one (1) MW
Results:
  QSE score calculated by hour, by zone, summed monthly
Day Ahead Zonal Schedule Measure
Resource Plans

## Slide 25
ERCOT Benefits
  ERCOT needs an accurate estimate of the output of Resources in order to predict capacity deficiencies as far in advance as possible
  Accurate zonal energy schedules assist ERCOT in predicting transmission congestion and ensure adequate resources are available
Market Benefits
  Costs to the market are lowered when ERCOT is able to make more efficient decisions to utilize capacity procurement measures (OOM, Replacement Capacity, RMR, etc.)
Day Ahead Zonal Schedule Measure
Resource Plans

## Slide 26
Compares zonal energy schedule with planned Resource operating level
Inputs:
  Last Resource Plan submitted prior to each Operating Hour
  Hours when the zonal energy schedule is greater than zero (0) MW
  Hours when the comparison differs by the greater of 2% or one (1) MW
Results:
  QSE score calculated by hour, by zone, summed monthly
Resource Plans
Adjustment Period Zonal Schedule Measure

## Slide 27
ERCOT Benefit
  ERCOT needs an accurate estimate of the output of generators in order to predict transmission congestion and assure adequate resources to resolve.
  Accurate AP schedule enables more accurate and efficient use of OOM instructions
Market Benefit
  Assists in more reliable operation of the ERCOT grid
  Helps to minimize use of OOM instructions
Resource Plans
Adjustment Period Zonal Schedule Measure

## Slide 28
Down Bid & Obligation Measure
Resource Plans
Checks adequacy of Resource Plan sustainable limits to accommodate mandatory Balancing Energy Service Down bids and Regulation Service Down schedule.
Inputs:
  Last Resource Plan submitted prior to each Operating Hour
  Hours with energy schedule greater than zero (0) MW
Results:
  Hours with more than one (1) MW of mandatory DBES deficiency
  Hours with aggregated LSL exceeding the sum of (a) energy schedule, (b) RGS Down schedule, and (c) mandatory DBES bids by more than one (1) MW
  QSE score calculated by hour, summed monthly

## Slide 29
ERCOT Benefit
  Assures that adequate Down Balancing energy bids are available to ERCOT for managing frequency during periods where more generation is scheduled than actual load
  Increases reliability of the ERCOT grid
Market Benefit
  Adequate Down Balancing energy bids supports balancing energy price stability (lower volatility)
Down Bid & Obligation Measure
Resource Plans

## Slide 30
Compares High Sustainable Limits to the sum of the energy schedule, Balancing Energy Service Up deployed, and scheduled Ancillary Services
Inputs:
  Last Resource Plan submitted prior to each Operating Hour
Exclusions:
  Intervals during which sum of RRS, RGS-Up, and NSRS schedule is zero (0) MW
Results:
  Intervals during which QSE’s obligations exceed HSL by more than one (1) MW
  QSE score calculated by interval, summed monthly
Total Up Ancillary Service Scheduled Obligation Measure
Resource Plans

## Slide 31
ERCOT Benefit
  Accurate Up Ancillary Service capability ensures that the Resources scheduled to provide Ancillary Services are in place and available
  More reliable grid operation is achieved by knowing when true deficiencies exist
Market Benefit
  This measure helps ERCOT optimize the quantities of Ancillary Services procured – results in lower overall Ancillary Service costs
  Ensures that all Ancillary Service providers maintain their ability to meet their scheduled obligation
Total Up Ancillary Service Scheduled Obligation Measure
Resource Plans

## Slide 32
Resource Plans
REVIEW

## Slide 33
Resource Plans
Review Questions
1. What is the ERCOT benefit intended by Resource Status?
a. To be aware of scheduled outages
b. To know where and when resources are online throughout the system to reliably operate
c. To know current frequency
d. To identify standards for compliance

## Slide 34
Review Questions
Resource Plans
2. What is a MARKET benefit intended by Resource Status?
a. Helps avoid inaccurate balancing energy clearing prices
b. To identify set points for firm load shed
c. To know what loads are acting as a resource
d. To aid in balancing current load and energy scheduled

## Slide 35
Review Questions
Resource Plans
3. What is an ERCOT benefit intended by Resource LSL as a percent of HSL?
a. To validate the resource plan
b. To know what generation resources are under test
c. To provide the ERCOT System adequate operating range to resolve congestion with the least cost unit dispatch
d. To identify QSEs participating in the ancillary market

## Slide 36
Review Questions
Resource Plans
4. What is the MARKET benefit intended by Day Ahead Zonal Schedule?
a. Identifies the primary method of system frequency control
b. Identifies the sources of down balancing energy
c. Identifies the sources of up balancing energy
d. Market costs are lowered since ERCOT can make more efficient decisions on capacity procurement (OOM, RMR, etc.)

## Slide 37
Review Questions
Resource Plans
5. What are the MARKET benefits intended by Adjustment Period Zonal Schedule?
a. Assists in more reliable operation of the grid and helps minimize using OOM instructions.
b. Identifies the sources of both up regulation and down regulation
c. Identifies the sources of both up balancing and down balancing energy
d. Identifies what generation resources are under test and what loads are acting as a resource

## Slide 38
Review Questions
Resource Plans
6. What is an ERCOT benefit intended by the Adjustment Period Zonal Schedule?
a. Validates the resource plan
b. An accurate estimate of the output of generators is needed to predict transmission congestion and assure adequate resources to resolve
c. To know what generation resources are blackstart
d. To maintain frequency at 60 Hz

## Slide 39
Review Questions
Resource Plans
7. What is an ERCOT benefit intended by Down Bid and Obligation?
a. Identifies QSEs participating in the ancillary markets
b. Identifies set points for firm load shed
c. Assures adequate down balancing energy bids are available to ERCOT for managing frequency during light loads
d. Identifies the causes for OOM deployment

## Slide 40
Review Questions
Resource Plans
8. What is the MARKET benefit intended by Down Bid and Obligation?
a. Identifies sources of up balancing energy
b. Sets the market clearing price
c. Increases reliability of the ERCOT grid
d. Adequate down balancing energy bids support balancing energy price stability (lower volatility)

## Slide 41
Review Questions
Resource Plans
9. What is an ERCOT benefit intended by Total Up Ancillary Service Scheduled Obligation?
a. Ensures that the resources scheduled to provide ancillary services are in place and available
b. Identifies the primary method of system frequency control
c. To be aware of scheduled outages
d. To know what generation resources are blackstart

## Slide 42
Review Questions
Resource Plans
10. What is a MARKET benefit intended by Total Up Ancillary Service Scheduled Obligation?
a. Increases reliability of the ERCOT grid
b. Sets the market clearing price
c. To know what generation resources are under test
d. Helps ERCOT optimize the quantities of ancillary services procured, which results in lower overall ancillary service costs

## Slide 43
Resource Plans:
Questions?