## Slide 1: EMMS Release 4
ERCOT Operator’s Seminar
2005
Brandon Whittle / Mark Patterson

## Slide 2: Agenda
Replacement Reserve Service (RPRS)
Simultaneous Selection of Ancillary Services (AS)
Improvements to OOM Tools
Resource Specific Bid Limits
Resource Plan Timeline
Special Protection Schemes (SPS)
Voltage Security Assessment Tool (VSAT) and Transient Security Assessment Tool (TSAT)
Notes: OOM – Out of Merit Order – The OOM tool is a generic term used to refer to the ERCOT operator mechanism to deploy OOME, OOMC, and now with R4 VDI and Fleet OOME.

## Slide 3: Objectives - Identify
Who initiated the changes in the EMMS that are incorporated into Release 4.
The purpose of the Replacement Reserve Market.
When, in the market timeline, the Replacement Reserve Market is cleared.
The advantage of Simultaneous Selection of Ancillary Services over Sequential Selection of Ancillary Services.

## Slide 4: Objectives - Identify
The benefit associated with including fleet deployments in the SCE calculation.
The changes to notifications to QSEs of VDIs and fleet deployments.
The changes regarding Resource Plan updates.
The purpose of Special Protection Schemes.
How Special Protection Schemes will be incorporated.

## Slide 5: What is Release 4?
Package of upgrades to the EMMS (ERCOT’s computer systems)
Initiated by PUCT, ERCOT, and Market Participants
4a – Areva Projects June 2005
4b – Non-Areva Projects 2005
Notes: EMMS = Energy & Market Management System

## Slide 6: RPRS
Gen Sched
Ancillary Service for Procuring Capacity
Capacity used for
  Local Congestion
  Zonal Congestion
  System Capacity
    See Example
Gen Sched
Gen Not
Scheduled
RPRS
Notes: Ancillary Services
Those services, described in Section 6, necessary to support the transmission of energy from Resources to Loads while maintaining reliable operation of transmission provider’s transmission systems in accordance with Good Utility Practice. (Protocols 2)
Replacement Reserve Service - A service that is procured from Generation Resource units planned to be off-line and Load acting as a Resource that are available for interruption during the period of requirement. (Protocols 2)

## Slide 7: RPRS
Three Step Clearing Process
  Local Congestion
  Zonal Congestion & System Balance
  MCPC Calculation
When?
  Day Ahead between 1600 and 1800
  Anytime During the Adjustment Period
Notes: MCPC – Market Clearing Price for Capacity - The highest price associated with a Congestion Zone for a Settlement Interval for Ancillary Service capacity awarded in each Ancillary Services capacity procurement run by ERCOT. There will be a separate Market Clearing Price for Capacity for each Ancillary Services capacity market. (Protocols 2)
Adjustment Period- The Adjustment Period for any given Operating Hour is the time period following the close of the Day-Ahead market and extending up to each Operating Period. (Protocols 2)
Timeline from ERCOT Protocols 4.1.1

## Slide 8: RPRS
Improvements?
  Temporal (Time) Constraints
    Startup Time
    Minimum Run Time
    Minimum Down Time
  24 Hour Optimization
    Opposed to 24 1 Hour Optimizations
    Proper treatment of Start Up Costs

## Slide 9: RPRS
Which Resources are Eligible for RPRS?
  Local Congestion – any generator resource offline and available will be eligible
  Zonal Congestion, Capacity – any offline and available generator or online, available, inactive LaaR resource with a RPRS bid.

## Slide 10: RPRS
What makes up an RPRS Bid?
  DAY – The Operating day for which the bid is submitted
  FIRSTHOUR – The first hour the bid is active
  LASTHOUR – The last hour the bid is active
  CAPACITY – The capacity in MW for the RPRS bid
  RSRC_ID – ID of Resource
  RSRC_TY – Type of Resource (GEN, UFR, CLD)
  CMZONE – Zone where the Resource is located
  STARTUP_PRICE – Capacity Price per MW
  PERHOUR_PRICE – Operational price per MW
  EXPIRATION_DATE – Date which bid expires
  EXPIRATION_TIME – Time which bid expires
  BES_BIDPOINT – Procured RPRS MW will be bid under this price
Notes: Startup cost will be calculated by RPRS. Startup cost will equal the Capacity Price per MW multiplied by the Capacity MW in the bid.

## Slide 11: RPRS
What does the QSE do when RPRS is Procured from the QSE?
  Receives an XML message
  Updates their Resource Plan accordingly
  Adds Capacity from RPRS resource into Balancing Bids
  Brings specified resource online for specified hours
  Receives Payment based on RPRS deployment
Who Pays?
  Capacity – When QSE metered load is greater than their schedules at the time of RPRS Market execution
  Zonal Congestion – QSEs whose schedules were impacting congested CSCs when the RPRS market cleared.
  Costs that are not directly assignable will be uplifted to Loads.

## Slide 12: Simultaneous A/S
Simultaneous Selection of Ancillary Services is equal to or less expensive than Sequential Selection.
New bidding rules for linked bids –
  RRS bid cannot exceed the URS bid by more than X%
    RRS bid <= URS bid + ( X/100 * URS bid)
  NSRS bid cannot exceed the RRS bid by more than X%
    NSRS bid <= RRS bid + (X/100 * RRS Bid)
Notes: Simultaneous Selection – All Ancillary Services are selected at the same time, based on QSE bids and ERCOT requirements. Production Cost is minimized using a linear program to perform the simultaneous selection.
Sequential Selection – Ancillary Services are procured in order – Up Regulation, Responsive Reserve, Non Spinning Reserve.

## Slide 13: Simultaneous A/S
Given: ERCOT needs 10 MW URS and RRS, X = 25
QSE A bids 10 MW; $9 URS, $5 RRS
QSE B bids 10 MW; $10 URS, $8 RRS
QSE C bids 10 MW; $15 URS, $30 RRS
Sequential (old) – $9 URS (QSE A), $8 RRS (QSE B)
$170 Total
Simultaneous (new) – $10 URS (QSE B), $5 RRS (QSE A)
$150 Total
 REJECTED
30 <= 15 + 25/100 * 15 = 18.75

## Slide 14: OOME Improvements
What is the Operator OOM Tool?
  OOM Entry Tool for the Operator
Why Upgrade it?
  Does not support Verbal Dispatch Instructions (commonly referred to as VDI)
  Does not allow cancellation of OOM
  Does not allow for accurate record keeping for constraint management

## Slide 15: OOME Improvements
More Communication with QSEs
  XML messages for VDI
  XML messages for Fleet / Zonal OOME
Better SCE management
  Instructed Deviations with Some VDI
  Fleet / Zonal OOME added to SCE

## Slide 16: Resource Specific Bid Limits
Resource Specific Bids?
  Used to evaluate cost for units used for local congestion deployments
  Resources will be moved based on premiums and expected effects on the constraint (shift factors)
For Resources with Identical Shift Factors
  Lower up premium - More likely to move up
  Higher down premium - more likely to move down.

## Slide 17: Resource Specific Bid Limits
Resources currently have premium bids mandated by protocol
With Release 4, QSE’s will have flexibility with their premium bids.
QSE’s will be paid the difference in the premium and the MCPE (as it was before).
Bid Limits posted daily in ERCOT Portal

## Slide 18: Resource Plan Timeline
Allows entry of Resource Plan through the Operating Hour.
Currently (Since Release 3) Resource Plan can only be updated until 16 minutes before the beginning of the Operating Hour.

## Slide 19: Resource Plan Timeline
0800
0815
0830
0845
0830 market clears
09:00 market clears
0845 market clears
At time
: Entered Resource Plan is used for 0845 RTB clearing
A
A
0900 market clears
At time
: Entered Resource Plan does not affect 0845 but will be used for 0900
-
B
B
C
C
At time
: Resource Plan for HE 0900 is not used
After 09:00, a Resource Plan entered for 0900 will be Rejected.

## Slide 20: SPS
Special Protection Schemes (SPS) represent one or more pre-defined protective actions that are automatically taken when a given event occurs in the ERCOT network.
Currently, ERCOT Operator must study effects of an SPS offline after a violation has been identified.
With Release 4, EMS Systems will take SPS’s into account when evaluating the system. (RTCA will only show violation if violation still exists after SPS is activated.)
Notes: Special Protection Schemes (SPS)
Real Time Contingency Analysis (RTCA)

## Slide 21: SPS
NOTE – NERC SPS definition slightly different. Those who are testing for NERC certification must realize:
  SPECIAL PROTECTION SYSTEM (NERC) - A protection system designed to perform functions other than the isolation of electrical faults. Also called “remedial action scheme.”
  Name is different - Special Protection Scheme (ERCOT) vs. Special Protection System (NERC)
  NERC’s definition includes both automatic and non-automatic systems – ERCOT separates automatic (and labels those as SPS) from the non-automatic (labeled RAPs)

## Slide 22: SPS
Generation Pocket
System
2000 MW
Line A
Line B
Lines A and B identical
1500 MW Ratings,
1000 MW Initial Flows
RTCA will show post contingency violations on Lines A & B

## Slide 23: SPS
Generation Pocket
System
2000 MW
Line A
Line B
SPS implemented to trip 500 MW of Generation in the Pocket if Line A or B trips.
With Release 4, RTCA will not show post contingency violations since SPS solved the problem, but will alert the operator that the SPS was used to solve the flow.
1500 MW

## Slide 24: VSAT/TSAT
Voltage Security Assessment Tool (VSAT)
  Calculates Transfer Limits based on current state of the system
Transient Security Assessment Tool (TSAT)
  Calculates Transfer Limits based dynamics overlaid on current state of the system
With Release 4, both to be run automatically to alert operators of possible violations. Operator can then alter transfer limits to improve conditions.
Notes: The VSAT Application checks voltage range violation, voltage stability, and overload violations for current operating point and calculates transfer limit based on voltage and overload criteria.
The TSAT Application checks transient angle stability, transient voltage stability, transient frequency stability, and small signal angle stability for the current operating point. In addition, the TSAT Application calculates the transfer limit based on transient and small signal stability criteria.
Transient - Of a two-machine system is defined as the maximum power that can be transmitted from one machine to the other without loss of synchronism for a specified, sudden, severe, unrepeated shock.

## Slide 25: Summary
ERCOT, PUCT, and Stakeholders initiated the changes in the EMMS that are incorporated into Release 4.
The Replacement Reserve Market procures capacity from resources to provides solutions to anticipated congestion and capacity shortages.
The Replacement Reserve Market is cleared day ahead between 16:00 and 18:00 as well as any time in the adjustment period.
Simultaneous Selection of Ancillary Services cost is less than or equal to the cost of Sequential Selection of Ancillary Services.

## Slide 26: Summary
Including fleet deployments in the SCE calculation will allow QSE’s to better maintain their SCE during fleet deployments.
QSEs will now be notified of VDIs and fleet deployments electronically via XML.
Resource Plan updates will be allowed during the operating hour.
Special Protection Schemes are designed to detect abnormal system conditions and take corrective action.
Special Protection Schemes will defined in EMS Network Applications which will allow the applications to use the SPS’s in their power flow solutions.

## Slide 27: Review
1. Identify the entity(s) that initiated the changes in EMMS that are incorporated into Release 4.
a. PUCT
b. ERCOT
c. Market Participants
d. All of the above

## Slide 28: Review
2. Currently (Since Release 3) Resource Plan can only be updated until ____ before the beginning of the Operating Hour.
a. 6 minutes
b. 16 minutes
c. 6 hours
d. 16 hours

## Slide 29: Review
3. True/False
Release 4 allows entry of Resource Plan through the Operating Hour

## Slide 30: Review
4. The Replacement Reserve Market is cleared in the day ahead between 16:00 and 18:00 as well as any time in the _____.
a. Adjustment Period
b. Operating Period
c. Day
d. none of the above

## Slide 31: Review
5. True/False
Special Protection Schemes (SPS) represent one or more pre-defined protective actions that are automatically taken when a given event occurs in the ERCOT network.

## Slide 32: Review
6. QSEs will not be notified of ____ electronically via XML.
a. outages
b. VDI’s
c. OOME’s
d. OOMC’s

## Slide 33: Review
7. Including fleet deployments in the ________ will allow QSE’s to better maintain their SCE during fleet deployments.
a. SCE calculation
b. ICE calculation
c. 15 minute compliance factor
d. CPS1 calculation

## Slide 34: Review
8. The _____ _____ Market procures capacity from resources to provide solutions to anticipated congestion and capacity shortages
a. Real-time Balancing
b. Replacement Reserve
c. Responsive Reserve
d. none of the above

## Slide 35: Review
9. Simultaneous Selection of Ancillary Services cost is _____the cost of Sequential Selection of Ancillary Services.
a. greater than or equal to
b. greater than
c. less than or equal to
d. all of the above

## Slide 36: References
Release 4 Functional Design Documents
  Available through your Client Representative
Protocols Revisions
  PRR 359 Resource Plan improvements
  PRR 342 A/S Simultaneous Selection
  PRR 413/491 Replacement Reserve Service
  PRR 485 Resource Specific Bid Limits

## Slide 37: Questions?