## Slide 1: QSE’s ROLE IN SYSTEM RELIABILITY
Jason Sweeney
Tractebel
Notes: Optional Title slide

## Slide 2: OBJECTIVES
Upon completion of this course, you will be able to…
Identify the primary source of reactive power for
ERCOT
Identify the basic difference between voltage
management and frequency management
Identify the multiple ways QSEs contribute to System
Reliability
Identify QSE System Emergency Training
requirements
Notes: At the completion of this program, all attendee’s will be able to:
Describe the general categories of Generation Resources with regards to fuel type and service provided.
Outline the basic protocol requirements for scheduling resource outages with ERCOT.
Detail the differences between the types of resource outages as described in the ERCOT protocols.
List the required QSE outage request and response notification time frames as described in the ERCOT protocols.

## Slide 3: KEY DEFINITION #1
“Qualified Scheduling Entities”
  Market Participants that are “qualified by ERCOT in accordance with Protocol 16, ‘Registration and Qualification of Market Participants’, to submit Balanced Schedules and Ancillary Services bids, and settle payments with ERCOT”
(Protocol, pg 2-22)
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 4: QSE FUNDAMENTALS
31 QSEs own or operate the ~78,000 MWs of installed capacity in ERCOT
PUCT, August 2004, “2003 State of the Market Report for the ERCOT Wholesale Electricity Markets”
Generation capacity has increased by 47.5% since 1996; this is high-efficiency / low-emission technology that holds important side benefits for the Texas environment
PUCT, August 2004, “2003 State of the Market Report for the ERCOT Wholesale Electricity Markets”

## Slide 5: QSE FUNDAMENTALS (cont)
ERCOT currently reports resource margins of 17.4%
(ERCOT’s report to TAC, 17 January 2005)
Only last August, PUCT reported resource margins of 33%…this same study projected that load growth in Texas would half this margin; but in 4 years
PUCT, August 2004, “2003 State of the Market Report for the ERCOT Wholesale Electricity Markets”

## Slide 6: PRIMARY SOURCE of REACTIVE POWER…
As ERCOT’s primary source of dynamic reactive power, QSE’s resources are obligated to maintain reactive capability, and to make it available to grid
QSE generators are also ERCOT’s fastest, most responsive source of reactive power
As voltage changes, TDSPs deploy a variety of capacitive or inductive devices to generate or absorb reactive power, respectively; including pushing QSE generators back towards center
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 7: PRIMARY SOURCE of REACTIVE POWER (cont)…
Before ERCOT shifted from 10 CAs to a single CA, voltage stability was locally managed by the 10 different CA parties
After the shift, voltage stability became a market-wide issue, as ERCOT assumed sole accountability and oversight, but still relied on market support – by way of QSE/TDSP coordination – to actually handle the job
ERCOT now relies on QSEs to be available for voltage support; when/if the QSE cannot perform, it strains the system
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 8: VOLTAGE MANAGEMENT v. FREQUENCY MANAGEMENT…
Basic difference is…
  Voltage Management is at the local level,
  between TDSPs & QSEs
  Frequency Management is system-wide,
  between ERCOT & QSEs
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 9: VOLTAGE MANAGEMENT v. FREQUENCY MANAGEMENT (cont)…
Governor Response is the most important part of ERCOT’s ability to control frequency
All QSE generation resources have a governor response requirement
QSEs must notify ERCOT anytime they go off AGC to manual control
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 10: KEY DEFINITION #2
“Ancillary Services”
“Those services, described in Protocol 6, necessary to support the transmission of energy from Resources to Loads while maintaining reliable operation of transmission provider’s transmission systems in accordance with Good Utility Practice.”
(Protocol, pg 2-2)

## Slide 11: ANCILLARY SERVICES (ie, the QSE’s “KEY” reliability role)
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 12: BALANCING ENERGY SERVICE (UP or DOWN)
UBES/DBES balances differences between scheduled generation and forecasted load, every 15 minutes
Mitigates/minimizes Regulation Service deployments
(Protocol 6.1.1)
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 13: REGULATION SERVICE (UP or DOWN)
URS/DRS balances differences between BES deployments and actual load, every 4 seconds
Responds to System frequency changes, to maintain target System frequency (60.0 Hz)
(Protocol 6.1.2 - 6.1.3)
Notes: General Definitions and Terms
Generation Entity
Owner or controller of a Generation Resource used for generating electricity and electrically connected to the ERCOT System.
Generation Resources
Facilities that produce energy and are owned or operated by a Generation Entity.

## Slide 14: RESPONSIVE RESERVE SERVICE
RRS solves for frequency decay and/or loss-of-Resource contingencies
Auto-deploys from the following resources – and corresponding setpoints - that can respond within 15 seconds…
Unloaded/online Generation – 59.91 Hz
LaaRs controlled by high-set UFRs – 59.8 Hz
Hydro RRS – 59.91 Hz
DC Tie Response – 59.9 Hz
(Protocol 6.1.4)

## Slide 15: NON-SPINNING RESERVE SERVICE
NSRS solves for loss-of-Resource contingencies
Manually deploys from the following resources that can respond within 30 minutes…
Off-line generation
On-line generation
LaaRs
(Protocol 6.1.5, 6.7.4)

## Slide 16: REPLACEMENT RESERVE SERVICE
RPRS solves for capacity insufficiency, and/or zonal or local congestion
Deploys from among the following resources for additional BES…
Non-synchronized generation
LaaRs
(Protocol 6.1.6)

## Slide 17: VOLTAGE SUPPORT SERVICE
VSS involves scheduling voltage profiles w/ ERCOT…
Based on Resources’ power factors and output voltage levels
At specific transmission busses, to maintain acceptable voltage limits
(Protocol 6.1.7)

## Slide 18: BLACK START SERVICE
BSS governs individual, 1-year agreements between ERCOT and 3rd Parties for capacity/energy off self-starting Resources
Solves for system restoration, following a blackout
(Protocol 6.1.8)

## Slide 19: RELIABILITY MUST RUN SERVICE
RMR governs agreements for capacity/energy off financially unviable units
Solves for voltage support, grid stability, local congestion management…when no market solution exists
(Protocol 6.1.9)

## Slide 20: OUT-OF-MERIT SERVICE (UP or DOWN) (CAPACITY or ENERGY)
OOMC/OOME supplements RPRS & BES
Solves for capacity insufficiency, congestion, reliability, emergencies…when no market solution exists
(Protocol 6.1.10 - 6.1.11)

## Slide 21: RESOURCE PLAN (ie, another QSE reliability role)

## Slide 22: KEY DEFINITION #3
“Resource Plan”
  That plan - described in Protocols 2 & 4 - provided by QSEs to ERCOT “indicating the forecast state of Generation…or individual LaaRs, including information on availability, limits…forecast generation or load…”
(Protocol, pg 2-24)

## Slide 23: KEY DEFINITION #3 (cont)
“Resource Plan”
  QSEs are to use “best efforts, consistent with Good Utility Practice” to ensure “accurate Resource Plans”
(Protocol 4.4.15)

## Slide 24: EMERGENCY & SHORT SUPPLY OPERATIONS (ie, another QSE reliability role)

## Slide 25: EMERGENCY & SHORT SUPPLY OPERATIONS (cont)
Protocol 5.6.1 states that Operating Guides ensure the
following minimum standards for reliability…
Minimum operating reserve levels
Frequency control criteria
System voltage limit criteria
Transmission loading limit criteria
Cascading outage criteria

## Slide 26: EMERGENCY & SHORT SUPPLY OPERATIONS (cont)
Ascending priority of communications between ERCOT & QSEs during contingencies…
“Operating Condition Notice”
  For informational purposes only, where conditions may require additional Resources
(Protocol 5.6.3 & Operating Guide 4.2.1)

## Slide 27: EMERGENCY & SHORT SUPPLY OPERATIONS (cont)
Ascending priority of communications between
ERCOT & QSEs during contingencies…
“Advisory”
  For informational purposes only, where conditions are developing that may require ERCOT to procure additional A/S
(Protocol 5.6.4 & Operating Guide 4.2.2)

## Slide 28: EMERGENCY & SHORT SUPPLY OPERATIONS (cont)
Ascending priority of communications between
ERCOT & QSEs during contingencies…
“Alert”
  Action may be required, where A/S are needed in
  the current Operating Period (either Regulation,
  Responsive, or Non-Spin)
(Protocol 5.6.5 & Operating Guide 4.2.3)

## Slide 29: EMERGENCY & SHORT SUPPLY OPERATIONS (cont)
Ascending priority of communications between
ERCOT & QSEs during contingencies…
“Emergency Notice”
Action is required to prevent large-scale event,
where ERCOT instructs QSEs to adjust Resource output and/or TDSPs to shed load
(Protocol 5.6.6 & Operating Guide 4.2.4)

## Slide 30: ADDITIONAL QSE RESPONSIBILITIES (ie, more QSE reliability roles)

## Slide 31: ADDITIONAL QSE RESPONSIBILITIES (COMMUNICATIONS with ERCOT)
ERCOT “only interacts directly with QSEs & TDSPs to operate the ERCOT System in a reliable and secure manner” (Operating Guides, pg 1-13)
“All other entities operating in the ERCOT System interface either to the QSEs or the TDSPs (Operating Guides, pg 3-3)
“From a market operations perspective, QSEs provide the main information interface with ERCOT” for “the scheduling of energy or bidding of A/S” (Market Guide, pg 11)
Notes: …the Operating Guides, state on Page 1-13

## Slide 32: ADDITIONAL QSE RESPONSIBILITIES (SYSTEM EMERGENCY TRAINING)
QSEs now required to obtain 40hrs/yr of System Emergency Training, alongside their TO and ERCOT Operator counterparts (Operating Guide 1.8.2)
QSEs soon to be required to participate in Annual Storm Drills (in time for November/05 drill), alongside their TO and ERCOT Operator counterparts

## Slide 33: ADDITIONAL QSE RESPONSIBILITIES (PERFORMANCE REQUIREMENTS)
ERCOT-Compliance’s performance/compliance metrics measure reliability of QSEs that provide A/S
Currently measured in 5 separate metrics…
  Regulation (both CPS1 & CPS2)
  Balancing
  Responsive Reserve
  Non-Spin
  Resource Plan
In future – possibly Q3/05 – compliance will be measured in one consolidated metric…“All-Interval”
Notes: Regulation (both CPS1 & CPS2)… defined in Protocol 6.10.5.3
Balancing…defined in Prot. 6.10.5.2
Resource Plan…defined in Prot. 4.10

## Slide 34: ADDITIONAL QSE RESPONSIBILITIES (PERFORMANCE REQUIREMENTS) (cont)
Complete details on QSE metrics may be found in two
places…
1. ERCOT-Compliance’s webpage…
http://www.ercot.com/nerccompliance/compliance.htm
2. Protocol 6
Notes:     All-Interval…defined in Prot. 6.10.4-6

## Slide 35: ADDITIONAL QSE RESPONSIBILITIES (PERFORMANCE ACCOUNTABILITY)
  August 18, 2004 DCS Event…
    NERC’s Disturbance Control Standard was
    violated as ERCOT was unable to control
    frequency decay within 15 minutes
    Post-analysis revealed 12 QSEs failed to
    perform

## Slide 36: QSEs in ERCOT GOVERNANCE & MARKET RULE-MAKING
<number>
<footer>
<date/time>
Board of Directors
(BOD)
Technical Advisory
Committee (TAC)
Protocol Revision
Subcommittee (PRS)
Reliability and
Operations
Subcommittee (ROS)
Training Seminar
Oversight
Working Group
Wholesale Market
Subcommittee (WMS)
Retail Market
Subcommittee (RMS)
Commercial Ops
Subcommittee (COPS)

## Slide 37: TEXAS NODAL / IMPACT on QSEs
NODAL PRICES
LOCAL CONGESTION MANAGEMENT
+ TRANSPARENCY
= TEXAS NODAL

## Slide 38
Questions
?
?

## Slide 39
Now for MY Questions
?
?

## Slide 40: 1. A QSE’s contribution to ERCOT System Reliability can be measured by:
a. Its ability to provide needed Ancillary Services .
b. Its ability to maintain low market clearing prices.
c. Its ability to keep capacitive and reactive devices in good working order.
d. Its portfolio size.

## Slide 41: 2. The primary source of dynamic reactive power in the ERCOT system is:
a. Generators.
b. Reactive devices.
c. Capacitive devices.
d. TDSPs.

## Slide 42: 3. Frequency management in ERCOT is:
a. System-wide.
b. A local control issue.
c. Not related to governor response.
d. A TDSP responsibility.

## Slide 43: 4. Voltage management in ERCOT is:
a. System-wide.
b. A local control issue.
c. Related to governor response .
d. A QSE responsibility.

## Slide 44: 5. QSE personnel are required to participate in System Emergency Training:
a. 20 hours per year.
b. 40 hours per year.
c. 60 hours per year.
d. 80 hours per year.

## Slide 45: 6. Which of the following Minimum Reliability Criteria does a QSE play a role in?
a. Minimum operating reserve levels & Transmission loading level criteria.
b. Frequency & System Voltage control criteria.
c. Cascading outage criteria .
d. All the above.

## Slide 46: 7. If practicable, the must be allowed to work to mitigate or eliminate any possible Emergency Condition.
a. Reliability Authority.
b. Market.
c. Public.
d. Retail Electric Provider.

## Slide 47: 8. What is the purpose of the “Quick Bid” process detailed in the Emergency Communications portion of the Guides?
a. To establish the MCPE.
b. Resolve local congestion.
c. Allow QSE’s to resolve an emergency through additional ancillary services.
d. Set the price for Block Load Transfer.

## Slide 48: 9. ERCOT-Ops normally communicates just with _____ and _____.
a. REP & TDSP
b. REP & LSE
c. LSE & QSE
d. TDSP & QSE

## Slide 49: 10. The QSE will notify ERCOT of any unplanned change in resource status as soon as practicable following the change.
a. True
b. False