## Slide 1: ERCOT Update Twenty-Second Annual ERCOT Operations Training Seminar March 28 through April 28, 2005 Electric Reliability Council of Texas Thomas F. Schrader, CEO

## Slide 2: What is ERCOT?
Electric Reliability Council Of Texas
Intrastate Electric Interconnection
Public Utility Commission Of Texas (PUCT) jurisdictional
70,000 MW of active generation
37,800 circuit miles of transmission lines
  Lower-voltage local distribution lines are the responsibility of the distribution companies, and are not overseen by ERCOT
60,095 MW Peak Demand on August 7, 2003
In existence since 1941
Independent, not-for-profit organization

## Slide 3: The ERCOT System
200,000 square miles of Texas
8+ million customers (meters served)
Over 500 generating units
8,100+ circuit miles of 345 kV lines
18,200+ circuit miles of 138 kV lines
11,500 circuit miles of 69 kV lines

## Slide 4: ERCOT’s Mission
ERCOT’s Mission is to create value for Texas electric consumers through electric grid reliability, market efficiency, and fairness.

## Slide 5: ERCOT Stakeholder Process
ERCOT Board
Technical Advisory Committee (TAC)
Numerous Working Groups & Task Forces
Retail Market Subcommittee
Wholesale Market Subcommittee
Protocol Revisions Subcommittee
Reliability & Operations Subcommittee
Commercial Operations Working Group
ERCOT staff provides technical support, subject matter expertise, and impact analysis for all proceedings
158 Member companies with voting privileges

## Slide 6: ERCOT Board Structure 14-member ‘Hybrid Board’
6 stakeholder members selected by market participant segment:
  IOUs
  Municipal utilities
  Electric cooperatives
  Independent REPs
  Independent Generators
  Independent Power Marketers
3 consumer members
  Industrial
  Commercial
  Residential (OPUC)
3 unaffiliated (independent) members
ERCOT CEO
PUCT Chair (ex-officio, non-voting)
Two-thirds majority vote required for Board action
Stakeholder Board model required by SB7 due to complexity of market startup
Governance structure has been modified over the years to fit changing circumstances

## Slide 7: ERCOT’s Role in Reliability ‘Job One’
ERCOT “directs traffic” on the grid to maintain reliability
  Coordinates scheduling of power so generation matches load at all times
  Analyzes grid conditions continuously in real-time
  Solves transmission congestion problems
  Ensures adequate operating reserves are available
Coordinates emergency recovery
Ensures compliance with NERC standards

## Slide 8: ERCOT Wholesale Market
Wholesale electric market deregulated in 1996:
  All wholesale market participants provided equal access to the transmission system
  Simplified transmission rates
  Vertically-integrated utilities retained customer bases
  ERCOT ISO created to oversee these activities

## Slide 9: SB7 & ERCOT
ERCOT assigned “independent organization” role
  ‘Starts’ with 40 employees operating existing wholesale ISO
Stakeholders draft and pass Protocols
  Thousands of hours of meetings & markup sessions
  Creation & definition of several new Market Participant categories
10 control areas consolidated to 1
Massive market systems design & build-out
  Retail transactions
  Wholesale Market & Scheduling (EMMS)
  Load profiles & settlement systems
Long hours by ERCOT staff, market participants, PUC staff and commissioners

## Slide 10: The ERCOT Market Bilateral Bias
Qualified
Scheduling Entities
“QSEs”
Load
Serving
Entities
ERCOT
Resources
Sellers
Buyers
Private bilateral
contracts
~95% of
Market
Includes >80 active REPs and ~130 Munis & Co-ops
Balancing Energy
Reliability
Congestion Management
> 80 active QSEs
100% of power is scheduled with ERCOT

## Slide 11: Congestion Management
Congestion Management is a key component of ERCOT’s role in grid reliability and the wholesale market
Excluding RMR, local congestion cost uplift was reduced by $117 million (43%) from 2003-2004
  Dynamic ratings for line limits
  Transmission system additions & upgrades
  Congestion analysis
Millions

## Slide 12: Texas Retail Market
Migration from Affiliated Retailer
 | % of Load | % of Customers | 
 | Nov. ‘04 | Nov. ‘04 | Nov. ‘03
Residential | 22% | 19% | 13%
Small Non-Residential | 60% | 23% | 16%
Large Non-Residential | 67% | 63% | 54%
A total of 1.27 million customers in competitive choice areas are now receiving power from non-incumbent providers

## Slide 13: Retail Market How Does Texas Stand?
Retail market ranked #1 in North America by Center for the Advancement of Energy Markets (CAEM)
  More retail adoption than any other N. Am. market
All parties (ERCOT, TDSPs, REPs) must function well for system to work
ERCOT’s unique role as neutral registration agent has been cited as a major reason for success of this market
Major upgrade of retail transaction system implemented on schedule in 8/04 -- automates the move-in/move-out process
Transaction timeliness & accuracy rates of 98-99%

## Slide 14: ERCOT’s Role in Addressing Market Issues
ERCOT works together with market participants and policy makers
ERCOT is an independent source of facts and expertise for policymakers and stakeholders
Stakeholder process assures changes will work
Current issues:
  Reserve margins
  Fuel diversity
  Transmission planning
  Wind power
  Grid security
  Wholesale market design

## Slide 15: Reserve Margins
No immediate crisis – 2005 reserve margin is 15-17%
Recent mothball and decommissioning actions show that market forces are working
  Older, less efficient plants are less competitive
TAC Task Force developing better process for reporting status of mothballed units
  Which will likely come back online?
ERCOT will actively participate in PUC resource adequacy proceedings

## Slide 16: Fuel Diversity Electric generation fuel sources in ERCOT
Fuel Source | % Capacity (Dec. ‘04) | % Energy (Jan.-Nov. ‘04)
Natural Gas | 63% | 38%
Dual Fuel* | 10% | 
Coal | 19% | 42%
Nuclear | 6% | 18%
Renewables | 2% | 2%
* Natural Gas or Diesel Fuel; all plants currently configured for gas
TAC subcommittee is currently assessing vulnerability of electric supply to natural gas curtailments

## Slide 17: Transmission Planning
Nearly $2 billion has been invested in ERCOT transmission facilities since 1999, including:
  900 miles of new transmission line construction
  Numerous substation additions & improvements
An additional $1.8 billion will be invested by 2008 based on current projections
  Includes >500 miles of new transmission lines already being permitting or under construction
Transmission system expansion faces competing priorities:
  West Texas (wind power)
  North Texas (DFW area responsible for ~50% of local congestion costs in ERCOT)
  Rio Grande Valley
Providers & regulators must evaluate costs & benefits

## Slide 18: Wind Power
Texas is well on its way to meeting renewable mandate from SB7 (2,000 MW by 2009)
West Texas is a premium site for wind energy due to geography & weather patterns
Power from existing wind farms must be delivered hundreds of miles to population centers in the east, and is not as controllable or predictable as traditional sources
  Creates new challenges in system design & operation
Identified upgrades to transmission system could accommodate existing mandate, but not a significant increase above 2,000 MW from West Texas
1,300 MW of wind capacity is now online in West Texas (1200 MW since SB7)
550 MW more to go online in 2005

## Slide 19: Grid Security
Transmission system has continuous real-time telemetry to ERCOT
Fully redundant and staffed backup control center
Standing Emergency Operation Procedures
  Includes Emergency Electric Curtailment Plan for extreme contingencies
  Black Start
Full compliance with NERC security standards
Working with PUC to enhance and improve communication procedures

## Slide 20: Wholesale Market Design
Texas Nodal Team (TNT) stakeholders working toward consensus on details of new market design as required by PUC rule (9/03)
Cost-Benefit study filed with PUC in December
Draft protocols to be filed with PUC March 18 for review
ERCOT will be ready to develop and implement any new market design approved by PUC

## Slide 21: Texas Nodal
PUC Subst. R §25.501 (9/03) requires a significant redesign of the wholesale market. Objectives:
More efficient dispatch of electric generation
  More complete information about how each plant will operate each day (unbundle portfolio bidding)
  Ability to anticipate system conditions to reduce local congestion
Direct assignment of the costs of local congestion
“Day-ahead” energy market
  Reduce market participant exposure to volatile real-time pricing
  Enable “hedge” against direct assignment of local congestion
Expanded ERCOT role in market monitoring
  Including providing more granular information
Identifies efficient location of new transmission and generation facilities
Provide more opportunities for load participation
Notes: THESE ARE Objectives of the Nodal Rule as stated in the preamble
(not ERCOT Advocacy)

## Slide 22: Questions?
Working together with market participants & policymakers to create value for Texas consumers, ERCOT will ensure grid reliability, enable the market and serve as a catalyst for improvement.