## Slide 1
ERCOT Market Operations Support
Marguerite Wagner
TEXAS NODAL TEAM (TNT)
MARKET DEVELOPMENT

## Slide 2: Presentation Objectives
Why nodal?
Fundamental Definitions --SCUC, SCED, LMP
The Backbone of Nodal—Resource Three Part Offers
Market Building Blocks: Day Ahead
What is an Integrated Day Ahead Market?
What is Reliability Unit Commitment?
Market Building Blocks: Adjustment Period & Real Time
Security Constrained Economic Dispatch, Basepoints
Resource Compensation for Energy in Real-Time
Load Zones under the Texas Nodal
Perceived benefits of the Texas Nodal Market System

## Slide 3: Objective 1: How Did We Get Here, Why Consider Nodal?
Exploration of Nodal is a Response to Current Issues with Zonal, Including:
Congestion Costs
  Started with Wind---OOME Payments, then local commitments for OOMC (DFW)
    Ongoing example, PRR 556 by Reliant that allocates OOMC, OOME, and RMR on a zonal basis (this didn’t pass—but it is still high on the radar)
    Intrazonal congestion costs have been significant ($100 -to $150 million/ per year in 2002 and 2003). [Potomac Economics State of the Market Report 2004. p. 113.]
Operational Issues with Zonal Model
  Complexity
    Market clearing—3 steps now
    Constraint oscillation—problem under 2 step process
    Congestion management—not transparent for Market Participants
Politics
  Despite being non-FERC Regulated, TX Commissioners still sensitive to Broader Landscape
  Pat Wood supports ERCOT Nodal Efforts (meeting Dec 2004)
Notes: Parsley
Hudson
Barry Smitherman

## Slide 4: Uplifted Congestion Costs Approaching $1B, Over 3.25 Years
“The cost to solve Local Congestion will be uplifted pro rata to each QSE based on the Load Ratio Share by QSE.” (ERCOT Protocols 7.1)

## Slide 5: Sept 2003: PUCT Guidelines, Project 36376
Bidding | Resource Specific (including Loads)
Pricing | Nodal for Resources, Zonal for Loads
DA Markets | Ancillary Service, Energy (Voluntary Participation), Reliability
Hubs | For Energy Trading
Congestion Revenue Rights | Options, Obligations, Flowgates
Two-Settlement | Prices and Financial Obligations in Day Ahead & Real Time
Notes: Similar Structure to NE ISOs, But No ICAP
Rule 9/22/03 in Project 26376 Wholesale Mkt Design
Rule outlined framework for development of Texas Nodal

## Slide 6: Texas Nodal Process & Status
Spring 2004 Developed First Draft TNT Protocols
Summer-04 to Feb 2005
  Protocol Comment & Continued Development
  Economist Recommendations and TNT Response
Protocol Filing
at PUCT
Texas Nodal PUCT Required
Implementation Date
3/18/05
10/1/06
Subject to Change!

## Slide 7: Objective 1 Test Question: Why Nodal?
Which is not a reason Nodal is being considered?
Three Step Balancing Energy Market Clearing is complex
OOM costs are higher than anticipated
Other markets have concluded that Nodal works
Everything is perfect in this market

## Slide 8: Objective 2: Fundamental Definitions
Transmission Constraints: Voltage or Power Flow Limits that must be met by the (pre- or post-contingency) dispatch
Transmission Congestion: Exists when one or more transmission constraints are binding in the SCED solution. As a result, SCED dispatches higher-cost generation “out of merit” to displace lower-cost generation (contributing to line overload). This causes the prices at different nodes to be unequal.
Notes: Precontingency is base case, if contingency happens, and over limit, then post contingency limit, operate n-1 secure

## Slide 9: Fundamental Definitions
Security Constrained Unit Commitment (SCUC): Mathematical process for finding a projected dispatch that minimizes the total bid-cost of meeting demand subject to all transmission and reliability constraints (similar to Replacement now)
Security Constrained Economic Dispatch (SCED): Mathematical process for finding a dispatch (and LMPs) that minimizes the total bid-cost of meeting demand subject to all transmission constraints (similar to Real Time Balancing now)

## Slide 10: No Congestion
100MW
75MW
100MW
Generator
Load
 | Size | Offer
G1 | 150 MW | $10
G2 | 50 MW | $20
Load | 150 MW | 
All 150 MW of Load can be served with no congestion.
G1 Dispatches at 150, G2 is not dispatched.
100
50
50
G1
Cheapest Solution is G1 at 150, G2 at 0. There are no line overloads and Load is fully served.
L
G2
Notes: For Load = 150 All LMPs are 20, System Cost is $1500. With Gen 1 at 150 and Gen 2 at 0
For Load = 151 LMPs are: G1 = $10, G2=$20, L = $30 with Gen 1 at 149, Gen2 at 2

## Slide 11: Congestion
100MW
75MW
100MW
Generator
Load
G1
G2
 | Size | Offer
G1 | 150 MW | $10
G2 | 50 MW | $20
Load | 155 MW | 
Cheapest Dispatch Causes Overload of G-L. Cheapest Solution is G1 at 150, G2 at 5. This overloads line G1-L (by ~2 MW).
100
50
50
2
2
3
L

## Slide 12: Congestion Resolved
100MW
75MW
100MW
Generator
Load
G1
G2
 | Size | Offer
G1 | 150 MW | $10
G2 | 50 MW | $20
Load | 155 MW | 
All 155 MW of Load can be served. Because of congestion (from G1 to Load at the cheapest dispatch), G1 ramps back, and G2 moves higher. This is “redispatch.”
97
48
48
G1 ramps back from 150 to 145 and G2 increases output from 5 to 10. With this dispatch there are no line overloads and load is served.
3
3
7
L
Notes: Load 155 System Cost

## Slide 13: Fundamental Definitions
Locational Marginal Price (LMP, Nodal Price): Determined by SCED using Resource offers to simultaneously determine:
  A security (or contingency) constrained economic dispatch
  A price for energy at each node in the grid
LMP = MCGeneration + CCongestion + CostMargLoss
Differences in LMPs identify the presence of congestion between two points

## Slide 14: Objective 2 Test Question: Background Definitions
Security Constrained Unit Commitment means:
Resources commitments do not consider Resource constraints, system constraints and cost
Resource commitment does not honor system constraints
Resources commitments consider Resource constraints, system constraints and cost
All Resources are committed all the time

## Slide 15: Objective 3: Three Part Resource Specific Offers
BACK
3 Part Offers + SCUC + SCED =
of Nodal

## Slide 16: Three Part Resource Specific Offers
Resource Bidding Under Nodal--3 Part Offers for Each Resource
Start up Cost: Cost to bring unit on—ignition through breaker close
Minimum Energy: Energy cost for unit to stay at Low Sustainable Limit (LSL)
Energy: Multi-Part Energy “curve” (starts at zero even though applicable for energy above LSL—so need configure offer to account for some of the “Zero-LSL block” in the energy bid instead of Min Energy)
$/MW
MW
LSL
Three part bids are used in DA Energy Market (DAEM) and in the DA Reliability Market (in RUC)
The Energy component of the 3-part bid is used in RT market as the basis for SCED

## Slide 17: Objective 3 Test Question: 3-Part Bidding
The three main components of Resource specific bidding are:
A) Start up cost, minimum energy cost, and energy curve
B) Reliability, security, commitment
C) Resource name, resource cost, resource availability
D) Least cost commitment, forecast load, reliability

## Slide 18: Objective 4: Market Building Blocks
Day Ahead
  Energy Market
  Ancillary Service Capacity Market
  Reliability Commitment
Real Time
  Hour Ahead Processes
  Real-Time Dispatch
  Performance Measurement
Settlement
  Day-Ahead
  Real-Time
Congestion Revenue Rights
  Types
  Acquisition Method
Mitigation—not discussed in this presentation
Equity
Time-line
Cost
Nodal will Retain Existing QSE
Structure & Communications
Incentives
Wholesale Impact on Retail
Efficiency

## Slide 19: Anticipated DA Nodal Timeline
Notes: Most current from TNT vote 3-7-05

## Slide 20: Overview Texas Nodal Day Ahead Markets:
Co-Optimized Energy and Ancillary Service Market
Energy (part of DAEM)
  Voluntary Energy Offers
  Voluntary Demand Bids
Ancillary Service Capacity (part of DAEM)
  Regulation
  Responsive
  Nonspin
Congestion Revenue Rights
  May be Offered for sale in the DAEM
  If not offered for sale in the DAEM, CRRs settle at DAEM prices (unless indentified to settle in RT)
Reliability Market (RUC)
Capacity for System Security—Reliability Unit Commitment
Notes:   (Called DAASM = Day Ahead Ancillary Service Market)
  ADAM Objective function will be to maximize the sum of the difference between bid-based revenues and bid-based costs simultaneously over the 24-hour period: Maximize: sum over successful buy offers of (bid price) * (amount bought) minus sum over successful sell offers of (bid price)*(amount sold).
DA MCPE will be the price at which the bid curve and offer curve intersect. Or, in the case of convergent bid and offer curves that do not intersect, the price that is the mid-point between where the bid curve and offer curve are closest. Non-convergent bid and offer curves will result in a DAMCPE equal to “NC” for non-convergence

## Slide 21: Overview Texas Nodal Real-Time Markets:
Real Time
Energy Market
  Settles Energy provided in Real Time
Congestion Revenue Right Settlement for CRRs carried to Real Time

## Slide 22: Test Question Objective 4: Texas Nodal Markets Day Ahead
Identify the markets under the Texas Nodal System in Day Ahead:
A) Energy, Ancillary Services and Reliability Unit Commitment
B) Energy Only
C) Ancillary Services Only
D) Reliability Only

## Slide 23: Objective 5: Integrated Day-Ahead Market
Inputs into Integrated Energy & Ancillary Service Market (DAM)
  Bids to Purchase Energy and Ancillary Services
    Voluntary Demand Bids for Energy
    Voluntary Bids to purchase Ancillary Service Capacity
  Offers to Sell Energy and Ancillary Services
    Voluntary Resource Specific Bids: 3-part supply offers (Start Up Cost, Minimum Energy Cost, & Energy Bid Curve)
  Offers to Sell CRRs
  Self Schedules
Clear DA Energy & Ancillary Service Market using SCUC & SCED
Results of the Day Ahead Market
  Resource Commitments from Day Ahead Market
  Hourly LMPs for all Settlement Points
  Ancillary Service Capacity Market Results
    MW procured by Resource, and
    Market Clearing Price for Capacity, by Service--Regulation (Up & Down Separately), Responsive, Non-Spin
Notes:   (Called DAASM = Day Ahead Ancillary Service Market)
  ADAM Objective function will be to maximize the sum of the difference between bid-based revenues and bid-based costs simultaneously over the 24-hour period: Maximize: sum over successful buy offers of (bid price) * (amount bought) minus sum over successful sell offers of (bid price)*(amount sold).
DA MCPE will be the price at which the bid curve and offer curve intersect. Or, in the case of convergent bid and offer curves that do not intersect, the price that is the mid-point between where the bid curve and offer curve are closest. Non-convergent bid and offer curves will result in a DAMCPE equal to “NC” for non-convergence

## Slide 24: Test Question Objective 5: Integrated Day Ahead Market
One of the characteristics of the Texas Nodal Day Ahead Energy Market is:
A) Integrated Market which uses the full network model and solves for congestion in Day-Ahead
B) Same as the Balancing Energy Market ERCOT has today
C) There is no Day Ahead Energy Market in Texas Nodal
D) It is part of a larger, single, national energy market administered by NERC

## Slide 25: Objective 6: Day Ahead Reliability Unit Commitment (RUC)
Day Ahead Security Process--Reliability Market (RUC)
Day Ahead Reliability Unit Commitment (DRUC) solves with all security constraints against 100% of ERCOT Load Forecast
Results are:
  Resource Specific Commitments

## Slide 26: RUC Continued
Committing Resources Against 100% of the ERCOT Load Forecast, subject to all constraints:
Ensures sufficient Resource capacity is online to meet Forecast Load
Assists with Reliability because it solves for congestion—committing Resources as required-- using the anticipated network state for the operating day
RUC uses only the Start up and Minimum Energy components of the 3-part bids
Notes: Economist Point—self commitment not necess the same as efficient commitment. Tried to encourage self commitment to eliminate make whole costs for Start up and no load.
RUC
  Occurs After clearing of DAEM
  QSE Must Indicate Self Committed Units to ERCOT prior to RUC
  Includes constraints for Demand=Gen (power balance), A/S req & constraints, forecast load,
Results of DAEM can Impact QSEs RUC Obligation

## Slide 27: Objective 6 Test Question: RUC
Describe the basis for the Texas Nodal Day Ahead Reliability Unit Commitment Process:
A) There is no Reliability Process in Day Ahead
B) Commits units for 50% of the ERCOT Load Forecast
C) Commit units for 100% ERCOT Load Forecast, subject to all constraints
D) All units are on all the time

## Slide 28: Objective 7: Adjustment Period & RT Nodal Timeline
Preparations for Real-Time Ops
Adj Period
18:00 (D – 1)
T - 60
T- 5
Real-Time Operations
T
Respond
T + 5
T- 4 secs
Update Energy Offers &
Submit HRUC Offers
Update Output
Schedules
Communicate Instructions & Prices
Execute Load
Frequency Control approximately every 4 seconds
Execute SCED every 5 minutes
Capture Inputs & Execute HRUC
Receive Instructions
T + 60
Operating Period
Operating Hour
T = 13:00
ERCOT
Activity
QSE
Activity
Notes: Timeline is shorter than RT timeline of today

## Slide 29: ERCOT Nodal Building Blocks, Adjustment Period & Real-Time
Adjustment Period Security Market: Hour Ahead RUC (HRUC)
Similar to DRUC only closer to RT
Looks out over balance of day to next DRUC
Real Time Energy Market: Security Constrained Economic Dispatch (SCED) to Satisfy System Needs
Energy Bids used to satisfy energy demand
  Solved every 5 minutes using energy bids from Resources and state estimator system snapshot based on real time Resource and Transmission telemetry
  Honors resource & transmission constraints (e.g. resource minimum run time, minimum down time, line loading restrictions)
  Basepoints sent to QSEs for each Resource
  Dynamic Schedules—provide output schedule to ERCOT, ERCOT sends back basepoint
  CRR Settlement for Non Opt In Entities
Notes:   (Called DAASM = Day Ahead Ancillary Service Market)
  ADAM Objective function will be to maximize the sum of the difference between bid-based revenues and bid-based costs simultaneously over the 24-hour period: Maximize: sum over successful buy offers of (bid price) * (amount bought) minus sum over successful sell offers of (bid price)*(amount sold).
DA MCPE will be the price at which the bid curve and offer curve intersect. Or, in the case of convergent bid and offer curves that do not intersect, the price that is the mid-point between where the bid curve and offer curve are closest. Non-convergent bid and offer curves will result in a DAMCPE equal to “NC” for non-convergence

## Slide 30: Adjustment Period and Real Time
During Adjustment Period, QSEs can alter their QSE - QSE trades for Ancillary Service or Energy
Online Resources Must have an Output Schedule or Offer Curve at all times
Hour Ahead Reliability Unit Commitment (HRUC)
  Done Hourly
  Confirm reliability for duration of the Operating Day
Security Constrained Economic Dispatch (SCED)
  Every 5 minutes
  Base Points & Ex Ante LMPs  Settlement
Notes: Ex Ante pricing
  5 min prices are then averaged on a time and MW-weighted basis to determine the Locational Marginal Price (LMP) at the settlement point for a 15-minute settlement period.
  2-Pass SCED: first pass uses only competitive constraints to determine reference prices, second pass uses mitigated offer curves and all contraints to determine dispatch points & LMPs

## Slide 31: Objective 7 Test Question: Nodal Building Blocks, Adjustment & RT
Which of the following is not a characteristic of the Adjustment Period or Real Time?
Hour Ahead Security—HRUC Market runs in Adjustment Period
There are no processes in the Adjustment Period or Real Time
SCED Operates Every 5 Minutes and Calculates Resource Base Points which are sent to QSEs
Real Time Energy Market

## Slide 32: Objective 8: SCED & Base Points
Under Texas Nodal, ERCOT determines the output level for every online Resource in the system, in Real Time.
  Dynamically scheduled resources submit an output schedule to ERCOT for use in SCED and will receive basepoints from ERCOT every 5 minutes
Security Constrained Economic Dispatch is used to calculate basepoints for every Resource that is online in ERCOT. This is called Centralized Dispatch.
Each QSE will receive a MW level for each Resource from ERCOT every 5 minutes

## Slide 33: Objective 8 Test Question: Resource Specific Instructions
Resource specific instructions under the Texas Nodal System:
Provide a dispatch point for each online resource in the system
B) Are not affected by contingency-related constraints
C) Include all ERCOT resources
D) Are settled based on Zonal clearing prices

## Slide 34: Objective 9: Resource Compensation in Real Time
Resource Settlement
  Resources settle on 15 min basis
  MW weighted average of the 5 minute nodal prices (LMPs) for the three 5-minute periods comprising the settement interval:
Sumi (LMPi * MWi ) / (Sum MWi) = $ paid to Resource
Where i = 1 to 3 are the three 5-minute periods of a 15 minute settlement interval
Resource Performance Measures: “LMP haircut” if outside of bandwidth around their basepoint (the min of 5 MW or 5% currently)

## Slide 35: Objective 9 Test Question: Real-Time Energy Resource Settlement
Describe Resource compensation in the Real-Time Energy Market:
A) Compensation is the same for every Resource
B) Compensation is the same for every Resource in a Load Zone
C) Resources are not paid for Real Time Energy
D) Aggregate LMP * MW for each 5 min of the 15 min period summed and MW weighted.

## Slide 36: Objective 10: Load Settlement & Load Zones Under Nodal
Zones are the 2003 Congestion Zones
West
North
South
Houston

## Slide 37: Load Settlement Under Nodal
Loads settle on Zonal Price
  15 minute MW weighted bus prices (MWi * LMPi) of buses, i, in load zone

## Slide 38: Objective 10 Test Question: Load Zones
Identify the four Load Zones under the Texas Nodal Market.
A) South, North, Houston and West
B) South, North, East and West
C) South, North, Northeast, and Houston
D) North, South, Northwest, Houston

## Slide 39: Whew! What’s the Benefit?
“I’m Sweating it Out, but there is a light at the end of the tunnel!!”


## Slide 40: Objective 11: TX Nodal Biggest Changes Compared with Today’s Zonal Market
Portfolio Bidding & Dispatch  Resource Specific (3-Part) Offers & Resource Specific Dispatch
Expanded DA Processes
  DA Energy Mkt (no official one now)
  Capacity Trading (only bilateral)
  Reliability Unit Commitment
15 minute dispatch 
5 minute dispatch
Resources paid Zonal MCPE for Balancing Energy  Paid Locational Price
Load Energy Prices Calculated on Basis of Aggregated LMPs within 2003 Congestion Zone Geographic Areas
Notes: Regulation 4 sec
Moving from commitment and dispatch at discretion of QSE to commitment and dispatch by ERCOT

## Slide 41: Take Away
Attribute | Current | Texas Nodal | Benefits
D/A Reliability | Replace-ment Mkt | (Residual) Centralized Unit Commitment | More Efficient Overall
D/A Energy Market | None officially | DAEM: solving for Energy, Commitment & CRRs | Choice for all participants
Transmission Rights | Flow-gates | PTP Options, Obligations & Flowgates | More Hedging Choice
Notes: Less energy deployed to control congestion
Replacement—lots of manual intervention, optimizes hour by hour,

## Slide 42: Take Away
Attribute | Current | Texas Nodal | Benefits
Real Time Dispatch | Portfolio + Unit Specific | Resource Specific | More Efficient, More Granular Control
RT Reliability | HA Studies | HA RUC | More Efficient Overall
Conges-tion Clearing | Zonal | Nodal | More Efficient, Improved Price Signals, Improved Congestion Management

## Slide 43: Test Question Objective 11: Benefits of Texas Nodal
One of the perceived benefits of the Texas Nodal Market System is:
A) The overall dispatch of generation resources in ERCOT will be more efficient
Energy markets will disappear and ERCOT will revert to command and control operations
C) Congestion costs are expected to increase dramatically across the state
D) Consumer choice in retail providers will decrease

## Slide 44: Test Question Objective 11: Benefits of Texas Nodal
One of the perceived benefits of the Texas Nodal Market System is:
A) More granular control of generation in the ERCOT system by ERCOT
B) ERCOT will own generators
C) Consumer choice in retail providers will decrease
D) Congestion costs are expected to increase dramatically across the state

## Slide 45: Test Question Objective 11: Benefits of Texas Nodal
One of the perceived benefits of the Texas Nodal Market System is:
A) Congestion costs are expected to increase dramatically across the state
B) Consumer choice in retail providers will decrease
C) Improved price signals to generators and load
D) Energy markets will disappear and ERCOT will revert to command and control operations

## Slide 46: Test Question Objective 11: Benefits of Texas Nodal
One of the perceived benefits of the Texas Nodal Market System is:
A) Congestion costs are expected to increase dramatically across the state
B) Consumer choice in retail providers will decrease
Improved congestion management
D) Energy markets will disappear and ERCOT will revert to command and control operations

## Slide 47: THANKS!