## Slide 1: Simultaneous Selection of Ancillary Services X%
18 May, 2005
Brandon Whittle
ERCOT Market Operations Support

## Slide 2: Simultaneous Selection of Ancillary Services X%
Background
  February 24, 2004 WMS Votes X=100,000
Issue
  X=100,000 may not match the intentions of WMS
Resolution
  Clarify what X=100,000 means
  Allow WMS to recommend course of action

## Slide 3: AS - Overview
New bidding rules for linked bids –
  RRS bid cannot exceed the URS bid by more than X%
    RRS bid <= URS bid + ( X/100 * URS bid)
  NSRS bid cannot exceed the RRS bid by more than X%
    NSRS bid <= RRS bid + (X/100 * RRS Bid)
X is adjustable, Currently set at 100,000
  WMS 2/24/05 Recommended 100,000 with the intent of setting the number high enough to not have any restrictions, but restrictions exist.
  Over the past 6 months, one QSE, for one hour of one day, had one bid which would have been rejected.
  X=10,000,000 would have no restrictions

## Slide 4: AS - Example
Given: X = 100,000
QSE A bids 10 MW; $9 URS, $5 RRS
QSE B bids 10 MW; $1 URS, $1000 RRS
QSE C bids 10 MW; $.01 URS, $30 RRS
Questions?
 REJECTED
30 <= .01 + 100,000/100 * .01 = 10.01