## Slide 1: Discussion on Proposals to Improve OOME as Instructed Deviation & Portfolio Ramp Rate Recall Young Li

## Slide 2: Portfolio Balancing Deployments
Zonal portfolio schedule & bidding
Zonal balancing energy deployed by ERCOT to resolve zonal congestion and energy balance
CSC
(Commercially Significant Constraint)
West
South
Houston
Northeast
North

## Slide 3: OOME/Resource Specific Deployments
Local Congestion Management
Unit specific deployments
OOME deployments

## Slide 4: Portfolio Ramp Rate Recall
As required by PRR349, Balancing Energy Market Clearing must incorporate QSE’s portfolio bid ramp rate when:
  Issuing instructions to change QSE’s BES deployment from the previous interval to current interval
    Changes from previously deployed UBES to or DBES to zero
    Changes from UBES to DBES or vice versa

## Slide 5: OOME as Instructed Deviation
In PRR373, Resource Specific OOME instruction entered prior to start of RTB Market Clearing, Instructed Deviation will be calculated and included in portfolio BES deployment;
Manual resource specific OOME honors resource specific ramp rate

## Slide 6: Balancing Energy Market Clearing Engine

## Slide 7: When OOME and Ramp Rate Recall Interacts
When OOME Instructions and Portfolio Ramp Rate Recall occur simultaneously, the solution for the Balancing energy Market Clearing becomes very challenging;
14 scenarios in Market Bulletin #19 explain the relationship between Instructed Deviation and portfolio balancing bids;
A proposal was discussed at last QSE PM meeting to change scenario #14.

## Slide 8: An Example for the Proposed Change
Gas
500 MW
150MW
Coal
900 MW
800MW
Assume this QSE has a bilateral schedule of 950MW;
Each unit has the ramp rate of 5MW/Min;
Coal Unit Scheduled to run at 800MW and Gas Unit Scheduled to run at 150MW at its Minimum Sustainable Limit.

## Slide 9: Questions for the Proposed Change
Gas
500 MW
150MW
@$50
Coal
900 MW
800MW
@$20
When there is transmission congestion, Coal Unit is OOMEd down to 600MW;
According to the proposal as discussed at previous meeting, this QSE could get 100MW up balancing when the MCPE greater than $20;
Questions to answer before system change:
  Is this QSE capable of providing 100MW up balancing?
  What should the QSE do?
  Can the payment cover this QSEs cost in following the instruction?

## Slide 10: Proposed Changes to Improve Operations
Utilize Resource-specific scheduling, bidding and deployment,
Utilize Resource-specific ramp rates in dispatch,
Utilize Resource-specific shift factors,
Develop financial incentives for participants to follow schedules and instructions ,
Develop scheduling rules and/or market mechanisms to mitigate effects of block schedules,
Develop mechanism to ensure deliverability of Ancillary Services,
Increase observability of the transmission system,
Issue dispatch instructions every five minutes,
Assign local congestion costs directly,
Implement a more robust Day Ahead unit commitment process.

## Slide 11: Will the Proposed Changes Resolve This Issue?
The top two prioritized changes are Resource Specific scheduling, bidding, deployment and Resource specific ramp rate;
Will this proposed change resolve the issue?
  In this example, the coal unit and gas unit will have separate schedules, bids and ramp rates;
  When the coal unit is asked to go down, the gas unit will be deployed based on its bid curve and ramp rate;
  At the same time, the coal unit’s up room will not be used for up balancing deployment.

## Slide 12: Other Alternatives Available?
Bus level scheduling, bidding and dispatch

## Slide 13: Criteria for Evaluating Proposals
GOOD
CHEAP
FAST
proposal discussed at last QSE PM meeting
ERCOT
proposed changes

## Slide 14: Discussion