## Slide 1
2005-2010 ERCOT Load Forecast and Reserve Margin Update
June 2, 2005

## Slide 2: Econometric Forecast 2005 Modeling Process
Obtain weather and economic variables (historic and forecast)
Develop regression equations describing the historic actual:
  Monthly Energy
    Using a different equation for each season
  Hourly Load Shape
    Using a different equation for each season
Incorporate forecasted values of economic variables and normalized temperatures for 2005-2010 into Monthly Energy equation to produce forecasted monthly energy
Incorporate normalized temperatures for 2005-2010 into Hourly Load Shape equation to produce forecasted load shape
Produce hourly demand forecast by fitting forecasted monthly energy under projected hourly load shape

## Slide 3: Representative Variables from Selected Models
Load hour i = f {Population, Income, Hour of Day Indicators, Weekday/Weekend, Max Temps, Lagged Temps, Heat Index, Non- Linear Temp Components (square and cube), Temp Gains (diff between daily High and Low temps), Temp Build-up, Dew Point, Dark Fractions, Month*Temp Interactions}
Energy Month i = f {CDD, HDD, Income, Population, Monthly Indicators}

## Slide 4: New ERCOT Peak Forecast
1.83% Avg. Growth

## Slide 5
New ERCOT Energy Forecast
2.10% Avg. Growth

## Slide 6: Load Forecast Technical Presentation
ERCOT will host a conference call to present details of forecast modeling
  June 14, 1-3 PM
  Open to all, but will invite representative group of market participant load forecasters to provide “peer review”

## Slide 7: Reserve Margin w/GATF Changes and New Forecast

## Slide 8: Updated Calculation Assumptions
All GATF recommendations implemented
Mothballed unit capacity availability based on percentages and lead times provided by unit owners
New generating units with signed interconnection agreements updated
Peak forecast based on econometric methodology
PH Robinson 2 is RMR for 2005
B.M. Davis 2 remains on RMR and Unit 1 is included in operational capacity for 2005
Current RMR units unavailable after end of RMR need

## Slide 9: RMR Status
RMR Agreement signed with P H Robinson Unit 2
B. M. Davis Unit 1 will be kept on RMR to ensure adequate voltage control in the Corpus Christi industrial areas
  Presentation will be given to ROS on this study
No Must-Run Alternatives (MRA) proposals were accepted as alternatives to the Bates RMR Units through the Bates MRA RFP
RFP issued for MRAs to the Laredo RMR Units
  NOI to Bid extended to June 8th
  Due date for bids is July 15th

## Slide 10
Questions?