## Slide 1: -- Presentation from PWG -- Workshop on Profile ID Assignment and Annual Review Process
June 23, 2005
Notes: Ernie to open meeting

## Slide 2: Reason For Workshop
Why am I at the PWG Workshop on Profile ID Assignment Responsibility Change?
  To determine the feasibility of a proposed change to move the entire Load Profile ID assignment process, maintenance process, and annual validation to ERCOT
    Note: PWG expects at least one more workshop and several more action items prior to any decision to move forward
Notes: Ernie to present reason we are here

## Slide 3
Current AV Profile Type Assignment Process
Notes: Carl to provide current process

## Slide 4
Additional Steps to Current AV Profile Type Assignment Process
Notes: Carl to provide current process

## Slide 5
ERCOT performs the additional validations listed below & by June 1 sends each TDSP the flagged ESI IDs for review
  Business NoDemand Profile Type
  NMFlat and NMLight Profile Type
  ESIID Profile Type to Premise Type
  Service Address Zip Code
  Weather Zone Code
  Meter Data Type Code to Profile Type Code
  Weather Sensitivity Code to Meter Data Type Code
  Time of Use Code
TDSPs review and send all 814_20s to ERCOT on the first scheduled meter read date on or after October 1
Additional Annual Validations Currently Performed
Notes: Carl to explain additional validations

## Slide 6
Five Components of Profile ID
Coast
East
FWest
North
West
NCent
SCent
South
Weather Zone Code
(2)
NWS
(1)
Group
Segment
IDR
NIDR
Meter Data Type Code
(3)
(1)
Group
Segment
TOUn
NoTOU
Time-Of-Use Code
(5)
(1)
WS
Weather Sensitivity Code
(4)
BUS
RES
Profile
Group
NM
IDRRQ
HILF
NODEM
MEDLF
LOLF
HIWR
LOWR
LIGHT
FLAT
Profile Segment
Profile Type Code
(1)
Notes: Carl

## Slide 7: Five Components of Profile ID (cont.)
Example:
RESLOWR_COAST_NIDR_NWS_NOTOU
Profile Type = ‘RESLOWR’
  Profile Group = ‘RES’
  Profile Segment = ‘LOWR’
Weather Zone Code = ‘COAST’
Meter Data Type Code = ‘NIDR’
Weather Sensitivity Code = “NWS’
Time-of-Use Schedule Code = ‘NOTOU’
Notes: Carl

## Slide 8: A Brief History...
Early 2002 – Idea was introduced that annual validation could take place at ERCOT rather than jointly among all TDSPs and ERCOT
Mid 2004 – Exchange of ideas in order to craft specifics with ERCOT on a proposed PRR for Annual Validation of Load Profile IDs
08/24/04 – This issue was discussed extensively at the PWG meeting
03/03/05, 03/08/05, 05/23/05 – Ideas were formulated on feasibility of moving the Load Profile ID Assignment and Annual Validation to ERCOT, between ERCOT and sub-team
05/25/05 – Ideas presented at PWG, decision to move forward with workshop consisting of wider RMS and COPS committee membership.
06/07/05, 06/13/05 – PWG hosted two conference calls to prepare for upcoming market workshop
06/23/05 – PWG sponsored Workshop on Profile ID Assignment Responsibility Change
Notes: Zach

## Slide 9
Oct. 2001 Initial Validation
  started and was not completed until Sept. 2002
2002 Annual Validation
  not performed due to 2001 Initial Validation still in progress.
  2002 PWG sub team changed methodology from utilizing billing month to usage month
2003 Annual Validation
  Large volume of migrations (RES – 24%, BUS 17%)
2004 Annual Validation for Business Group only
  Large volume of migrations (RES – 19%, BUS 16%)
  Residential suspended due to large volumes
2005 Annual Validation (currently in progress)
  changes to methodology
    RES -- Winter Ratio Dead-bands and Winter Ratio Numerator minimums
    RES & BUS -- no changes to a default Profile Type
  Expected migrations RES 12%, BUS 15%
History of Annual Validation
Notes: Zach

## Slide 10: Goals / Assumptions for Responsibility Change
  The key to this solution is in handling TDSP Rate Class within ERCOT’s systems
  Preferable to have single entity assign Profile IDs to avoid service history conflicts/overwrites
  ERCOT will be able to create 814_20 transactions to notify CRs of Profile ID changes (ERCOT currently creates some TX SET transactions)
  Minimize changes needed for all MPs to transition to the new process
  Maintain current audit and oversight responsibilities
  Changes in Load Profile ID assignment process should be transparent to CRs
Notes: Zach

## Slide 11: Benefits of Responsibility Change
  Reduced coordination required between TDSPs and ERCOT resulting in potential market wide cost savings
  Faster implementation of changes to the Load Profile ID assignment methodology
  Potential for reduced lag between identifying the need for a Profile ID assignment change and when the change becomes effective
  Provides for more flexibility in implementing changes to the Load Profile ID assignment methodology, including more sophisticated algorithms
  Removes any TDSP limitations on the number of months of usage history that can be incorporated in calculations for Profile Type
Notes: Zach

## Slide 12: Benefits of Responsibility Change (cont.)
  Eliminates potential for inconsistent application of assignment process across the market
  Helps to minimize barriers to entry to the market
    CRs have single contact point (preferable but depends on final design)
    Muni/Co-Ops don’t have to implement complicated logic, hire outside consultants, or add personnel
  Facilitates and streamlines Mass Transition issues related to Profile Id assignment for transitioning ESIIDs
  Virtually eliminates need for TDSPs to modify their systems due to ongoing changes in the Load Profile ID assignment process and Annual Validation
Notes: Zach

## Slide 13
Texas SET changes will be necessary
  TDSP Rate Class would always be required at ERCOT
      Is a change required in 814_20?
      Do we need to add new field to 867_03??
  Load Profile ID populated in 814 transactions by ERCOT not TDSP
  Full TX SET investigation required to realize all changes
CR ad-hoc historical usage request changes
  Load Profile ID currently provided by TDSP
      Change required for retailer to get LPID from ERCOT?
      Can TDSP get LPID from 727 data for ad-hoc requests??
Impacts of Change in Profile ID Assignment Process
Notes: Zach

## Slide 14
  ERCOT and TDSP system/process changes required
  CR process changes required
  Protocol changes required
  Load Profiling Guide changes required
  ERCOT Communication Changes
    Increased level of involvement in the Load Profile ID assignment disagreement process
    Potential increase in volume of communications at the retail level
Impacts of Change in Profile ID Assignment Process (cont.)
Notes: Zach

## Slide 15
Market Considerations
  Cost Allocation
    Potential cost shifting from TDSPs to ERCOT
      Near Term: Potential TDSP savings may not be realized by entire market
      Long Term: Potential TDSP rate increase to cover expense of annual validation not currently in rate base
      TDSP resources may become available for other market priorities
  Audit and Oversight: Checks and balances considerations
    Oversight of the Profile ID assignment process by PUCT and stakeholders would continue
    Profile Decision Tree would continue to document and provide visibility for the Profile ID assignment rules … Decision Tree governance is being reviewed by PWG
    ERCOT’s business processes, including annual validation, are and would continue to be subjected to annual independent external audits (SAS 70 audits)
    CR’s would continue to have audit capability via SCR 727 extract process … all data elements used by ERCOT for profile assignment would be available
    One set of code would be used for assignment calculations rather than six independently developed sets
Notes: Zach

## Slide 16
Market Considerations (cont.)
Would a potential increase on ERCOT cost be beneficial to the market?
Assumptions for Scenario in spreadsheet risk.xls are
  2004 ERCOT MWH of 289,117,218 MWH
  $100,000 dollar increase to ERCOT cost
  Actual MCPE from 05/21/2005 to 06/02/2005
  Cost based only on intervals where MCPE greater than $70
  Cost based on only incremental MCPE above $70
  10 MWh improvement in settlement (UFE) accuracy
Conclusion:
  Payback is extremely quick assuming the market needs to buy 10 MWh from the balancing market that was not covered by $70/MWh bilateral contracts
Notes: Ernie

## Slide 17
Assign Profile ID based on:
TDSP Rate Class and 814_20 Meter Loop Detail (helps with BUSNODEM determination)
    Or
TDSP Rate Class (only)
Options to be Considered
Notes: Zach

## Slide 18
    For each option:
      ERCOT will have to make system changes to save TDSP Rate Class history at the ESI ID level
      Process would have to be set up for ERCOT to monitor PUCT approval of changes to TDSP Rate Class
    TDSP Rate Class and 814_20 Meter Loop Detail requires:
      Handles “virtual meter” issues (if rule changed to 10 kW, this wouldn’t be needed)
TDSP Rate Class Alone Vs. TDSP Rate Class and 814_20 Meter Loop Detail
Notes: Zach

## Slide 19
Initial Flowchart of Proposed Annual Validation Profile Type Assignment
Notes: Carl to show proposed method

## Slide 20
ERCOT performs the additional validations listed below & sends each TDSP the flagged ESI IDs for review
  TDSP Rate Class to usage validation
    Demands consistent with Rate Class
    Usage consistent with Rate Class
  Service Address Zip Code
  Weather Zone Code
TDSPs review and make any necessary corrections to rate class or zip code
Review frequency should be determined
Initial Proposed Additional Periodic Validations Performed
Notes: Carl

## Slide 21
Load Profile ID add/update triggers based on TDSP transactions
  Creation of new ESI ID using transaction which includes rate class
  Transaction to change rate class
  Zip code change for existing ESI ID
  Rate class change can also trigger Meter Data Type change (IDR/NIDR)
  Historical usage value changes in Annual Validation window
Initial Proposed ESI ID Assignment & Maintenance Process
Notes: Carl

## Slide 22
The key to this solution is in handling TDSP Rate Class
  ERCOT will have to make system changes to save TDSP Rate Class history at the ESI ID level, currently it is not stored
The Key to this Solution...
Notes: Carl

## Slide 23: Proposed Profile ID Component Assignment & Update
Profile Type
Assigned by ERCOT based on TDSP provided Rate Class and usage records
Changes triggered by
  TDSP Rate Class Change
  Annual Validation
  Periodic ERCOT Validation of Rate Class
  Usage change (causing the previously assigned Profile Type to be an error)
Weather Zone Code
Assigned by ERCOT based on TDSP supplied zip code
Changes triggered by
  TDSP zip code change
  TDSP originated change or Periodic ERCOT validation of zip code
Meter Data Type Code
Assigned by ERCOT based on TDSP supplied Rate Class
Changes triggered by
  TDSP Rate Class Change
  For Centerpoint, changes between IDR and NIDR are indicated by Rate Class changes (is this true for all TDSPs?)
Notes: Carl

## Slide 24: Proposed Profile ID Component Assignment & Update (cont.)
Weather Sensitivity Code
  Assigned by ERCOT based on interval data in ERCOT systems
    ‘BUSIDRRQ’ either ‘WS’ or ‘NWS’
    All NIDR premises have ‘NWS’
  Changes triggered by ERCOT running the weather sensitivity test
Time-of-Use Schedule Code
  Assigned by ERCOT based on TDSP provided Rate Class
  Changes triggered by Rate Class Change
Notes: Carl

## Slide 25
ERCOT to conceptualize at high level of how changes would be implemented
Need to review details of all TDSPs’ Rate Classes
  Establish linkage to the Load Profile ID assignment
  Final Product: Rate Class to Profile Type Matrix (example on next page)
Next Steps
Notes: Zach

## Slide 26
Example
Example of TDSP Rate Class to Profile Type Matrix
Notes: Zach

## Slide 27
Costs related to transactions and data storage?
Most efficient way to address TX SET changes?
Is it possible to have multiple meter types on 814_20 transactions, and if so, how to handle?
How to handle effective date of TDSP Rate Class change?
Matrix provided by TDSP would have to include all rate classes, including NMFLAT
The process for NOIE ESI IDs would not change from the current procedure
Options on handling BUSNODEM issues:
1. ERCOT to follow existing rules
  But how does ERCOT know if the CR uses demand for billing?
2. TDSP to submit all demand values to ERCOT
3. Assign possible new profile BUSLODEM for all demands ≤ 10 kW
4. Assign all ESIIDs with demand to a load factor profile type
Issues for PWG Workshop to consider
Notes: Ernie

## Slide 28
How to handle list based and DLC related Profile ID assignments?
Should ERCOT proactively change Profile Type based on new/modified usage records (in Profile Decision Tree window) being loaded or wait for CR dispute? If proactive, update daily, weekly, monthly?
What should be the frequency and timing of periodic validation and maintenance for remaining components (other than Profile Type) of Profile ID?
Treatment of TOU??
Does anything in this proposal cause increased CR costs?
Issues for PWG Workshop to consider (cont.)
Notes: Ernie