## Slide 1
Market Notice Regarding Off-line Units

## Slide 2: What it Did
Issued April 14, 2005
Requested to QSEs to cease showing off-line units as on line in their Resource Plans starting May 15, 2005 unless they met interim qualification test
Provided reasons for request
Established interim qualification test

## Slide 3: Development History
Presented to ROS February 10, 2005
Discussed at WMS February 28 and March 16, 2005
Discussed at QSE Project Managers Working Group
Changes made to initial proposal based on comments received
Market Notice sent out April 14, 2005 establishing interim qualification requirements
PRR 588 approved unanimously by PRS on May 19, 2005 adopting unit qualification standard consistent with interim requirements

## Slide 4: Goal
Set qualifications for off-line units that can be shown on-line in Resource Plans (typically quick-start gas turbines) and thus eligible to provide Balancing Energy
Qualification based on Balancing Energy dispatch requirements in Protocols:
  Deployment sent out by ERCOT 5-7 minutes before start of ramp (10-13 minutes before start of interval)
  Balancing Energy must be completely ramped in 10 minutes (5 minutes after start of interval)

## Slide 5: Why Needed
If off-line units are shown on-line in Resource Plan and bid into Balancing Energy, but can not respond fast enough to provide Balancing Energy according to Protocols:
  Regulation requirement is increased with risk of depletion, increasing exposure to frequency control problems, impact of unit trips and Responsive Reserve deployment
  QSE might provide Balancing out of it’s Responsive Reserve obligation to avoid SCE, making ERCOT deficient
  Incorrect unit status in Resource Plan affects procurement of Non-Spinning Reserve, OOMC, OOME now, and Replacement Reserve after Release 4

## Slide 6: Results
QSEs have complied with the request in the Market Notice and no longer show unqualified off-line units as on-line
One QSE requested interim qualification test for 312 MW
That QSE was qualified for 304 MW
As much as 2,000 MW of off-line capacity was shown on-line in past. Unknown how much was bid into Balancing