## Slide 1
Presented to
Commercial Operations Subcommittee
September 27, 2005
Settlement Impacts
of
EMMS Release 4

## Slide 2: What is Release 4?
Package of upgrades to ERCOT’s EMMS (Energy and Market Management System)
Initiated by PUCT, ERCOT, and Market Participants
Notes: EMMS = Energy & Market Management System

## Slide 3: What is Release 4?
Operational Changes
Simultaneous Selection of Ancillary Services (AS)
Resource Plan Timeline
OOM Tool Enhancements
Resource Specific Bid Limits
Replacement Reserve Service (RPRS)

## Slide 4: What is Release 4?
Settlement Impacts
Resource Plan Timeline
OOME and OOMC
Local Congestion Settlements
Replacement Reserve Service Market

## Slide 5
Resource Plan Timeline
Market Support Services
March 30, 2005

## Slide 6: Resource Plan
Operational Changes
Allows entry of Resource Plan through the Operating Hour.
Currently (Since Release 3) Resource Plan can only be updated until 16 minutes before the beginning of the Operating Hour.

## Slide 7: Resource Plan
Impacted Determinants
RP, RPAGG, HSL, LSL, OOMEUPBP, OOMEDNBP
Hourly data 15 Minute Cuts
HSL, LSL, RP, RPAGG still MW values
OOMEUPBP, OOMEDNBP in $/MWh

## Slide 8: Resource Plan
Impacted Settlement Calculations
Settlement of Capacity for Out-of-Merit Service (PCOOMAMT)
Settlement of Local Congestion with Bidding Units
Settlement of Local Congestion with non-Bidding Units
Settlement of Out of Merit Energy from a Specific Unit

## Slide 9
OOME and OOMC
Market Support Services
March 30, 2005

## Slide 10: OOME and OOMC
OOM Tool Enhancements
What is the Operator OOM Tool?
  OOM Entry Tool for the Operator
Why Upgrade it?
  Does not support Verbal Dispatch Instructions (commonly referred to as VDI)
  Does not allow cancellation of OOM
  Does not allow for accurate record keeping of constraint management

## Slide 11: OOM Tool Enhancements
New Determinants
OOMEVDI
  15 Minute interval cut
  OOME Deployment dispatched through a VDI
OOMEFLT
  15 Minute interval cut
  A Fleet OOME Deployment
OOMEZNL
  15 Minute interval cut
  A Zonal Fleet OOME Deployment

## Slide 12: OOM Tool Enhancements
New Determinants cont.
OOMCVDIFLAG
  Hourly cut
  Indicator of a VDI OOMC instruction ( 0=No Instruction, 1=OOMCVDI Instruction)
INTERVAL_HOLD
  Each hold for a day has a unique number
  Flag starts with 1 at the first interval held and continues through the end of the hold instruction.
  A subsequent hold would begin with 2

## Slide 13: OOMC
Changes to OOMC
Calculation of OOMRPQ – Awarded amount
OOMCHR – Number of hours awarded
Calculation of PO – Operating payment

## Slide 14: OOMC
Hour 8 (Intervals 29 – 32):
OOMRPQ = ( 141 + 145 + 151 + 155 ) / 4 = 148
(Used to calculate RCGSC)
OOMRPQ – OOM awarded amount

## Slide 15: OOMC
OOMCHR – Number of hours instructed
OOMCHR = 3

## Slide 16: OOMC
OOMC – Out of Merit Capacity Payment
PCOOMRPQqi = -1 * MIN[(BPRpqui * COOMRPQui),(PSui + POui)]
No change to PS
Slight change to PO
MINCAP replaced by LSL

## Slide 17
Local Congestion
Market Support Services
March 30, 2005

## Slide 18: Local Congestion
New Resource Specific Bid Limit Methodology
Resources currently have premium bids mandated by protocol
With Release 4, QSE’s will have flexibility with their premium bids.
QSE’s will be paid the difference in the premium and the MCPE (as it was before).
Bid Limits posted daily in ERCOT Portal

## Slide 19: Local Congestion
Settlement Of Local Congestion
Bidding Units Paid as Local Balancing Energy
Non-Bidding Units Paid as OOME
RP values can change every 15 Minutes

## Slide 20
RPRS
Market Support Services
March 30, 2005

## Slide 21: RPRS
New Determinants
LCFLAG
  Hourly cut
  0 = awarded Zonal RPRS
  1 = awarded Local RPRS
  2 = No award
LPS
  Hourly cut
  Start-up Payment determined in Settlements with RCGSC, LRPHR
LPO
  Hourly cut
  Operating Payment determined in settlements with RCGMEC, MCPER, GSITETOT and LSL

## Slide 22: RPRS
New Determinants cont.
LRPADJ
  Hourly cut
  Adjustment to Local RPRS Payment (LPCRPAMT)
LRPHR
  Hourly cut
  Number of hours a unit is continuously procured for Local RPRS
RPRSMW
  Hourly cut
  Minimum of average hourly HSL (at the time of procurement) or MW awarded from RPRS bid

## Slide 23: RPRS
New Determinants cont.
ZRPADJ
  Hourly cut
  Adjustment to Zonal RPRS Payment (ZPCRPAMT)
ZRPHR
  Hourly cut
  Number of hours a unit is continuously procured for Zonal RPRS
ZRPHRBP
  Hourly bid price for RPRS ($/MW)
  Only used in Zonal RPRS

## Slide 24: RPRS
New Determinants cont.
ZRPSUBP
  Hourly start up bid price ($/MW)
  Only used in Zonal RPRS
LRPQ
  Hourly cut
  MW quantity of Local RPRS awarded. Determined in Settlement using LCFLAG and HSL
ZRPQ
  Hourly cut
  MW quantity of Zonal RPRS awarded. Determined in Settlement using LCFLAG and HSL

## Slide 25: RPRS
Local Replacement Reserve (LCFLAG = 1)
Steps
LRPQ – Awarded amount
LRPHR – Number of hours awarded
LPS – Start up payment
LPO – Operation price

## Slide 26: RPRS
LRPQ – Local Replacement Quantity
Hour 5 (Intervals 17 – 20):
LRPQ = ( 141 + 145 + 151 + 155 ) / 4 = 148
(Used to calculate RCGSC)

## Slide 27: RPRS
LRPHR – number of hours instructed
LRPHR = 3

## Slide 28: RPRS
LPS – Local RPRS start up payment
Determine if “Hot” or “Cold” start (Combined Cycle only)
  Hot = Less than 5 hours from shut down to start up
  Cold = 5 hours or more from shut down to start up.

## Slide 29: RPRS
LPO – Local RPRS Operating payment
  Unit will get paid for what it generated, up to it’s LSL.

## Slide 30: RPRS
LPCRPAMT – Local Procured Capacity Replacement Amount
New Formula

## Slide 31: RPRS
ZRPQ – Zonal Replacement Quantity
Hour 5 (Intervals 29 – 32):
ZRPQ = MIN[156,( 143 + 144 + 146 + 147 )/ 4] = 145
RPRSMW = 156

## Slide 32: RPRS
ZRPHR – number of hours instructed
ZRPHR = 3

## Slide 33: RPRS
ZPCRPAMT – Zonal Procured Capacity Replacement Amount

## Slide 34
Questions and Answers
Questions ?????