## Slide 1: ERCOT Analysis of 2005 Residential Annual Validation Suspension
ERCOT Load Profiling
Presented to RMS - November 9, 2005

## Slide 2
Residential Survey Analysis
Objective: quantify the accuracy of the 2005 Annual Validation Residential Profile Assignment Changes
Approach: use survey responses together with each responder’s usage history build an accurate algorithm to predict presence and use of electric space heating
Apply the algorithm to each of the 578,572 ESI IDs with 2005 Annual Validation Profile Assignment changes
Determine the percent of changes which are correct
  RESHIWR with electric heat
  RESLOWR without electric heat
If the majority of changes are correct then AV 2005 is improving Profile Assignment Accuracy

## Slide 3
Residential Survey Analysis
Overall survey response rate was 11.4%
Response accuracy by weather zone ranges from ±3.7% - ± 4.8% at the 95% confidence level
Response accuracy at the ERCOT level ±1.5% at the 95% confidence level

## Slide 4
Responses by WZone/Profile Type
8.5% 12.6% 10.5% 9.9% 13.6% 11.3% 10.6% 14.1%
Responses / Mailed by WZone

## Slide 5
Q2 – Primary Home Heat
Electricity
Natural/Bottled Gas
Other/Not Sure

## Slide 6
Q2 – Primary Home Heat
Electricity
Natural/Bottled Gas
Other/Not Sure
By Profile Type

## Slide 7
Q3 – If Electricity, is it a Heat Pump?

## Slide 8
Q5 – Added Central Elec. Cooling/Heating

## Slide 9
Electricity
Natural/Bottled Gas
Other/Not Sure
Primary Heat/Age of Residence

## Slide 10
Electricity
Natural/Bottled Gas
Other/Not Sure
Primary Heat/Age of Residence

## Slide 11
Electricity
Natural/Bottled Gas
Other/Not Sure
Primary Heat/Age of Residence

## Slide 12
Residential Survey Analysis
Responder’s
Usage
History
Survey
Responses
Best correlation
RESLOWR or RESHIWR
Algorithm

## Slide 13
Residential Classification Algorithm
Step1: survey response validation using an initial version of the algorithm developed from the pilot survey … 85% valid heating system type responses
Step2: algorithm fine tuning to minimize miss-classification error … an iterative process
  95.4% of the final algorithm’s classifications agreed with the survey responses regarding heating system type
  The remaining 4.6% of the responses generally had usage patterns which were not clearly indicative of the heating system type
Step3: apply final algorithm to ESIIDs with Annual Validation changes to compare assignments

## Slide 14
Algorithm Basics – An Example
Actual survey respondent’s usage history plotted with scaled profiles

## Slide 15
Algorithm - Classification Rules
If number of winter readings < 3 or shoulder readings < 3 then assign “RESLOWD”
Else if the highest winter reading kWh/day is less than 15 kWh/day
then assign “RESLOWR”
Else if CorrelationRESHIWR > 0.60 and CorrelationRESHIWR > CorrelationRESLOWR
then assign “RESHIWR”
Else if the number of readings available > 9
and CorrelationRESHIWR > 0.90
and (CorrelationRESHIWR + 0.010) > CorrelationRESLOWR
and Winter Max kWh/day > 50
then assign “RESHIWR”
Else if the number of readings available > 9
and CorrelationRESHIWR > 0.95
and (CorrelationRESHIWR + 0.015) > CorrelationRESLOWR
and Winter Max kWh/day > 60
then assign “RESHIWR”
Else assign “RESLOWR”

## Slide 16: SUMMARY OF 2005 ANNUAL VALIDATION PROFILE TYPE CHANGES

## Slide 17: ACCURACY OF AV 2005 PROFILE TYPE CHANGES

## Slide 18: RESIDENTIAL POPULATION ACCURACY BEFORE & AFTER AV 2005 CHANGES

## Slide 19: Run Test Settlements to See Effects of AV
Prepare test environment to run settlements for different scenarios
Select a sample of 30 (or so) days to analyze … three strata based on differences between RESHIWR and RESLOWR
Run test settlements with currently assigned Profile IDs and capture results
In test environment, change Profile IDs as directed by the 2005 Annual Validation Process
Run test settlements with changed Profile IDs and capture results
Compare changes in UFE and Load Ratio Share

## Slide 20: Selecting Days to Analyze

## Slide 21: UFE Changes in MWh

## Slide 22: Change in Load Ratio Share for One LSE

## Slide 23: Change in Load Ratio Share and MWh

## Slide 24: Change in Load Ratio Share and MWh

## Slide 25: Change in Load Ratio Share and MWh

## Slide 26
Conclusions
62% of 2005 Annual Validation Profile Type changes are accurate
Changes to RESHIWR are significantly more accurate (78.4%) than are changes to RESLOWR (43.5%)
Accuracy of the changes by weather zone range from a low of 59.8% in the SOUTH zone to a high of 68.8% in the EAST zone
Although AV 2005 has identified 578,572 Profile Type changes, the net impact of the changes overall is to increase the number of RESHIWR ESI IDs only by 39,418 … a 2.5% increase and a corresponding 1.1% decrease for RESLOWR
The Residential population will have somewhat more accurate Profile Type assignments as a result of conducting 2005 Annual Validation (81.4% vs. 78.7%)
In spite of the small net number of Profile Type changes Settlement impacts are present both for UFE and LRS

## Slide 27
Proceed with submission of 2005 Annual Validation Profile ID changes
Continue PWG-sponsored efforts to improve the Profile Type assignment algorithm
Continue consideration of shifting Profile Type calculation responsibilities to ERCOT primarily to allow use of several years worth of data in the algorithm
Questions?
ERCOT Staff Recommendations to PWG