## Slide 1: Commercial Operations Sub-Committee Update to TAC
November 3, 2005

## Slide 2: COPS Update
  COPS voted to approve a draft PRR that “sets a lower limit to the number IDR meters within a Meter Reading Entity (MRE) that would be considered when determining whether the IDR threshold requirement is met or not for true-up settlement.” There are situations where 1 missed read was close to delaying True-Up Settlement
  Continuing the analysis of PRR 568 “Reducing Initial Settlement from 17 to 10 days.” At this time, the second review period has not completed both the Day 8 and Day 15 aggregation check points. Conference call set for Nov 9 for final data review. Progress on recommendation to implement PRR568 appears positive. Vote to be requested at the December TAC meeting.
Notes:     What entities are exposed to the uplift associated with a DAM participant’s failure to pay?
    Questions from COPS discussion:
    Is the 180 day uplift in the draft Nodal Protocols correct?

## Slide 3: COPS / PWG Review of Commercial Settlement during Hurricane Rita
  ERCOT staff presented UFE analysis for Sept 19 – 26
  UFE vacillated from -24 to +2% due to estimated usage from previous month’s avg daily use
  ERCOT Load is approximately 50% IDR and 50% non-IDR
  ERCOT processes calculate initial settlement usage from previous usage periods
    Profiled ESIIDs use previous months avg daily kWh until a meter read for the period is available
    IDR metered ESIIDs use similar day proxy data for initial settlement
  Final and True-up Settlements are expected to have estimated use replaced with “actual” meter reads
Notes:     What entities are exposed to the uplift associated with a DAM participant’s failure to pay?
    Questions from COPS discussion:
    Is the 180 day uplift in the draft Nodal Protocols correct?

## Slide 4: TDSP Activity - Hurricane Rita
  TDSPs estimated reads due to adverse conditions :
    Reported estimates for non-IDR meter reads only
    Utilized standard VEE Uniform Business Practice rules for estimating
    No unusual adjustments were applied to the estimates
    AEP estimated 8500 reads across 2 cycles
    CNP estimated 250,071 reads across 8 cycles
    TNMP estimated 15,000 reads across 3 cycles
    TXU ED estimated 100 reads – no cycles missed
Notes:     What entities are exposed to the uplift associated with a DAM participant’s failure to pay?
    Questions from COPS discussion:
    Is the 180 day uplift in the draft Nodal Protocols correct?

## Slide 5: Identified Concerns
  All solutions will create financial winners and losers
  Some MPs self adjusted schedules assuming load loss during the hurricane
  Adjusting Profiles after the fact may undermine MPs that adjusted schedules in the day ahead processes
  Concerns that a historical correction is inappropriate given the large bi-lateral ERCOT market
Notes:     What entities are exposed to the uplift associated with a DAM participant’s failure to pay?
    Questions from COPS discussion:
    Is the 180 day uplift in the draft Nodal Protocols correct?

## Slide 6: Recommendations:
  COPS voted to not adjust backcasted profiles due to events around Hurricane Rita
  COPS agreed an additional settlement was not necessary between Final and True-Up
  COPS recommends PWG identify ways to accommodate extreme events on the Settlement Process
Notes:     What entities are exposed to the uplift associated with a DAM participant’s failure to pay?
    Questions from COPS discussion:
    Is the 180 day uplift in the draft Nodal Protocols correct?