## Slide 1: TAC Potomac Recommendation Monthly Update October 6, 2005
Nieves López
ERCOT Market Rules

## Slide 2: Recommendations Related to Congestion Management
Recommendation | Sponsor | Status
1. Improve the process for designating zones to minimize the effects of the simplifying zonal assumptions. | ERCOT | PRR 589 (CSC and Zone Determination) Category B Approved by BOD on 6/21/05. Effective 7/1/05.
2. Improve process for evaluating and revising CSC definitions. | CMWG | Suggested improvements have been incorporated into the current versions of PRR587 and PRR 689. Category B
3. Modify the calculation methodology of the zonal average shift factor to exclude generation whose output is generally fixed (e.g., nuclear units). | ERCOT | PRR 592 (Modify Shift Factor Calculation to Exclude Fixed Output Generators). Category B Approved by BOD on 6/21/05. Effective 11/1/05.

## Slide 3: Recommendations Related to Congestion Management – Cont’d
Recommendation | Sponsor | Status
4. Provide ERCOT the operational flexibility to temporarily modify the definition of a CSC associated with topology changes. | ERCOT | PRR 587 (Intra-Year Modification of CREs) Approved by BOD on 6/21/05. Effective on 7/1/05.
5. ERCOT should modify its multi-step balancing energy market optimization to recognize the interactions between its local congestion management and zonal balancing energy deployments to minimize the costs of both classes of deployments. | n/a | Due to complexity and cost, the issue deferred until after the PUCT decision on the nodal market design. Category C

## Slide 4: Recommendations Related to Load Forecast
Recommendation | Sponsor | Status
6. ERCOT examine its load forecasting model to determine whether there are additional factors that could be considered or other changes to their model that would improve its accuracy. | ERCOT | Ongoing and on schedule. ERCOT has completed some items relating to load forecasting. ERCOT will continue to evaluate and make any additional changes. No PRR required for implementation. Category A.

## Slide 5: Recommendations Related to Balancing Energy Market
Recommendation | Sponsor | Status
7. Allow QSEs to submit an energy schedule for the end of the next hour that would be used by ERCOT to produce 15-minute schedule quantities by interpolating across the hour. | Tenaska – for QSE PM WG | PRR 609 (Smooth 15-Minute Resource Schedules) Category C. Rejected by TAC on 7/21/07.
8. Implement an optional capability for QSEs to automatically adjust their hourly balancing energy offers for the changes in their 15-minute schedules. This would help ensure that the participant’s portfolio energy offer is consistent with its energy schedules when the energy schedule is changing each interval. | WMS, through QSE PM WG | PRR 600 (Align BES Bids with Resource Plan Capability and Resource Schedule) Category C. Approved by BOD on 9/20/05. Effective 10/1/05.

## Slide 6: Recommendations Related to Balancing Energy Market - Cont’d
Recommendation | Sponsor | Status
9. Eliminating the load and generation plateau in the middle of the interval by changing the modeling approach for load and generation. | WMS | PRR 601 (15 Minute Ramping for BES and Base Power Schedule) Category C. Remanded to TAC by BOD on 9/20/05. Remanded to PRS by BOD on 10/6/05. Will be addressed by TAC on 11/3
10. Require that QSEs submit physically feasible energy schedules. It would be difficult to automatically validate the schedules for feasibility since they can be submitted well before the operating hour. However, it could be monitored and enforced through ex post validation of compliance. | ERCOT | PRR 525 (SCE Performance and Monitoring). Category C Approved by BOD on 4/19/05. Partial implementation effective 5/1/05. Full implementation and enforcement effective upon system implementation.

## Slide 7: Recommendations Related to Balancing Energy Market - Cont’d
Recommendation | Sponsor | Status
11. Implement uninstructed deviation charges that allocate a portion of the regulation costs to the QSEs exhibiting large SCEs in the periods during each hour with the largest regulation needs. In particular, we propose specific changes to PRR 356 that has been pending for more than two years. | PUCT WMO | PRR 586 (SCE Performance and Regulation Cost Re-Allocation). Category B. Urgency Status denied. ERCOT Backcast reviewed at 4/21/05 WMS meeting. PRR again discussed at 4/17/05 WMS meeting. PRS considered the PRR on 5/19/05 and 7/21/05. PRR is remanded the PRR to ROS and WMS.
12. Consider a specific modification of ERCOT’s portfolio ramp rate methodology that would recognize the changes in energy schedules. | None | Due to complexity and cost, the issue deferred until after the PUCT decision on the nodal market design. Category C.

## Slide 8: Recommendations Related to Balancing Energy Market - Cont’d
Recommendation | Sponsor | Status
13. ERCOT modify the limit on the quantity of responsive reserves provided from a single unit to make it less binding on relatively small units. | ROS | OGRR 164 (Responsive Reserve MW Limit). Category B On 5/12/05, ROS voted to reject this OGRR.
14. ERCOT institute procedures to monitor whether QSEs are meeting their reserve obligations in real time. | ERCOT | PRR 590 (Update Unit Telemetry Requirements). OGRR 165 (Update Unit Telemetry Requirements). Category A. PRR approved by the BOD on 8/16/05. OGRR is being address by ROS

## Slide 9: In Summary:
Recommendations 5 and 12 delayed pending Commission decision regarding future market design.
Recommendations 1, 2, 3, 4, 6, 7, 8, 10, and 13 completed.
Recommendation 9 remanded pending development of CBA.
Recommendations 11 and 14 in progress.
Complete report will be posted on the ERCOT website.