| PRR Number | 371PRR | PRR Title | Define OOME as Instructed Deviation and Portfolio Out of Merit Energy Service |
| --- | --- | --- | --- |
| Date | November 18, 2002 |
| Submitter’s Information |
| Name | Paul Messerschmidt |
| E-mail Address | Psmesserschmidt@tecoenergy.com |
| Company | Frontera Generation Limited Partnership |
| Company Address | P.O. Box 111, Tampa, FL 33601 |
| Phone Number | 813-228-4974 |
| Fax Number | 813-228-1289 |

Comments

Frontera Generation strongly supports the comments submitted by Larry Gurley for the QSE Managers Working Group with the change indicated below.  However, Frontera Generation sees this as only the first step towards adequate compensation when an OOMC instruction is received.  Frontera would point out that as written, the PRR is in effect from the time the unit reaches its Minimum Sustainable Limit and as a result market participants are not compensated for Ramp Energy which must also be dumped into the grid to reach the Minimum Sustainable Limit necessary to comply with the OOMC instruction.  Both Ramp Energy and energy which is dumped during the time the unit is at the Minimum Sustainable Limit should be fairly compensated.  There are still other changes which must be made to the compensation mechanism to make the market participant which provides this reliability service whole, but this PRR, with the inclusion of compensation for Ramp Energy is definitely a step in the right direction and Frontera wholeheartedly supports it.

Adoption of this PRR does not change the fact that compensation for costs outside of the protocol formula are at the discretion of the ERCOT Board of Directors.  This discretionary function on the part of ERCOT remains problematic.

Comments

This PRR was reviewed at the November 7 QSE Project Managers Working Group meeting, and the group agreed to the following modifications.  The original language is problematic for determining what the OOME instruction is at settlement because the Resource Plan at the end of the Adjustment Period will contain the OOMC’ed unit shown to be operating at minimum load or more.  The proposed modification to the settlement calculation of the hourly operating cost of the unit should address the issue raised in the PRR.  Additionally the group agreed to address the issue of OOMC settlement when there is not a Replacement bid for the unit.  Currently, a zero is inserted for the Replacement bid term in the settlement calculation for OOMC.

#### 6.8.2.2 Capacity Payments

- OOMC Service may be used by ERCOT as a procured Replacement Reserve Resource in the Adjustment Period where necessary to support emergency operations and provide voltage support, stability or to manage localized transmission limitations All Resources that are available and plan to be off-line during the interval for which ancillary services are being procured are eligible to be selected to provide OOMC Service.  OOMC Service may be used only if there is no resource available through the Specific Process for Replacement Reserve Service procurement defined in section 6.6.3.2.1 or through contracted RMR Service.

- Resources selected to provide OOMC Service that actually reconnect to the ERCOT transmission grid and start the unit in order to provide the OOMC service will be paid both the Resource Category Generic Capacity Cost for starting the unit as well as the Resource Category Generic Operational Cost for operating during the instructed interval(s).

- Resources that are connected to the ERCOT transmission grid when instructed to provide OOMC Service will be paid the Resource Category Generic Operational Cost for operating during the instructed interval(s).

- Resources that receive an instruction to provide OOMC service greater than the Generating unit Minimum Sustainable Limit as reported in the resource plan will be paid for an OOME instruction for the amount of the instruction greater than the Generating unit Minimum Sustainable Limit as reported in the resource plan.

- Any energy which the unit must generate to reach its Minimum Sustainable Limit (“Ramp Energy”) will be compensated as an OOME instruction.

- If a Resource is called to provide OOMC service and the payment for OOMC service is insufficient to cover all costs of providing the Service and provide a premium, then that Resource will be paid all verifiable, costs in excess of the OOMC payment that are directly attributable to the OOMC Service plus a premium.  These costs may include the cost of exceeding swing gas contract limits, additional gas demand costs set by fuel supply or transportation contracts, and any additional costs to purchase emissions credits or other costs incurred due to environmental regulations.    The premium to be provided shall be the product of the costs of providing the service times 10%.    Verification of these costs must be submitted to ERCOT to allow resolution by the end of the dispute process for Settlement True-Up as defined in Section 9.2.6, True-Up Statement.  QSEs requesting such cost recovery shall perform the following:

(a)	Submit a settlement dispute in accordance with the dispute process outlined in Section 9.5.  In addition to the standard information required on the entry form on the ERCOT Portal, the dispute should clearly indicate:

(i)	The deployment instruction received from ERCOT to provide services.

(ii)	The payment received for providing the service.

(iii)	The actual cost of providing the service.

(iv)	A reference to the documentation to be provided in writing as indicated in section 6.8.2.2(4)(b).

(b)	Requests for additional compensation shall provide documentation in writing to allow for verification of the claimed amounts.  Documentation requirements for each cost type are as follows:

(i)	Fuel cost for providing the service shall be determined by taking the product of the fuel consumption (MMBtu) at the normal minimum operating level of the resource and it’s associated fuel cost ($/MMBtu).

(ii)	Fuel consumption at the normal minimum operating level shall be based upon a heat rate curve for the resource from the most recently conducted heat rate tests.  Test data shall be provide in sufficient detail to allow for the validation of the heat rate curve provided.

(iii)	Fuel cost, including transportation cost, will require supporting documentation of sufficient detail to allow for the verification of the cost of fuel consumed at the deployed resource.  Documentation may include contracts, invoices or other documents all of which will be treated as confidential.  All copies of such documentation will be returned upon completion of the review.  For gas fired resources, such documentation will not be required if the requested incremental fuel cost is less than 115% of the Fuel Index Price.

(iv)	Compensation for additional types of cost, not outlined above, must be reviewed and approved by the ERCOT Board of Directors during an Executive Session of their next regularly scheduled meeting.  Requests must be presented in person by a representative of the company submitting the request and must also include language suitable to be included in the Protocols to define the documentation requirements for future request of a similar nature.  Subsequent to the approval of such costs, the requesting company shall submit a Protocol Revision Request, in accordance with Protocol 21, incorporating the necessary documentation standards provided to the ERCOT Board.

- The calculation for capacity payments of Out –of Merit Service is as follows:

PCOOMRPqi	=	SUM (PCOOMRPqui)u

Given:

If BPRpqui exists,

Then:

PCOOMRPqui	 =	-1* MIN [BPRpqui * COOMRPui, MAX [0, (PSui + POui - RCui)]]

Else:

PCOOMRPqui	 =	-1* MAX [0, (PSui + POui - RCui)]

If the unit is deemed to be online as described in 6.8.2.1(3)

Then:

PSui	=   0

If the unit is deemed to be offline as described in 6.8.2.1(2)

Then:

PSui	=	RCGCCc

POui	=	SUM {MAX [0, (RCGFCc - MCPEjz) * MINCAPui]}j / 4

RCui	=	SUM {[MAX (0, (MCPEjz – (16 * FIP)))] * COOMRPui/4}j

The equation below will be used to determine the Total OOM Capacity Payments to be allocated to each QSE as described in Section 6.9.7.1, OOM Capacity Charge.

PCOOMRPqi	 = 	SUM (PCOOMRPqui)q

Where:

c:	Resource Category

i:	hourly interval

j:	Settlement intervals within the hourly interval i

u:	single Resource

z:		zone

q:		QSE

PCOOMRPqui: 	OOM Replacement Reserve Capacity Payments by single Resource by interval for that QSE

PCOOMRPqi:	Total OOM Replacement Reserve Capacity Payment ($) by interval for that QSE (All OOM single Resources added together for that QSE)

BPRPui:	Bid Price for Replacement Reserve ($/MW) of the unit per interval

COOMRPui: 	Out of Merit Replacement Reserve Capacity awarded capacity (MW) per single Resource per interval

PCOOMRPi:	Summation of OOM Replacement Capacity Payment ($) per interval for all QSEs in the market

RCGCCc:	Resource Category Generic Capacity Cost for a specific category of generation unit.  RCGCCc = RCGSC/(number of hours).

RCGOCc:	Resource Category Generic Operational Cost for a specific category of generation unit.

PSui:	Price for starting a unit that is selected out of merit order to provide balancing energy.

POui:	Price for operating a unit that is selected out of merit order to provide balancing energy.

RCui:	Revenue credit for unit deployed

MINCAPu	Generating unit Minimum Sustainable Limit as reported in the Resource Plan.