## Slide 1: EMMS Release 4 Market Wrap-up
WMS
January 18th, 2006

## Slide 2: Release 4 Market Wrap-up
R4 Market Components
A/S Simultaneous Selection PRR 342
Replacement Reserve Service PRR 413/491
Resource Plan improvements PRR 359
Resource Specific Bid Limits PRR 485
OOM Enhancements PRR 422, 423
Modification of Ancillary Services Allocation

## Slide 3: EMMS Release 4 Market Wrap-up
Simultaneous Selection of Ancillary Services
Replacement Reserve Service

## Slide 4: Simultaneous Selection of Ancillary Services
Original Savings Estimate
Observed Results

## Slide 5: Simultaneous Selection of Ancillary Services
Original Savings Estimate
Production Cost = Offer price multiplied by MW Cleared
Cost to Market = MCPC multiplied by MW Cleared
Expected Savings assumes 1 year of identical results
 | Production Cost | Cost to Market
Studied Savings ~ 162.3 days | $ 1,083,719 | $ 8,965,858
Expected Savings (1 yr) | $ 2,436,074 | $ 20,154,199
Notes: Estimate presented at WMS meeting 21 September 2005
162.3 days in study which compared actual market results with the same input data run through the new R4 Market Clearing Engine.
Studied savings * 365 days in year / days in study = Expected Savings

## Slide 6: Simultaneous Selection of Ancillary Services
 | URS | RRS | NSRS
R4 MCE | $16.87 | $14.27 | $5.66
Production | $15.87 | $15.39 | $8.22
 | $1.00 | ($1.12) | ($2.56)
Original Savings Estimate - MCPC
Notes: Estimate presented at WMS meeting 21 September 2005
Slide hidden to conserve time.

## Slide 7: Simultaneous Selection of Ancillary Services
Observed Results
Production Cost = Offer price multiplied by MW Cleared
Cost to Market = MCPC multiplied by MW Cleared
Expected Savings assumes 1 year of identical results
 | Production Cost | Cost to Market
Observed Savings ~ 79 days | $ 878,232 | $ 9,440,413
Expected Savings (1 yr) | $ 4,057,656 | $ 43,617,101
Notes: 79 days in study which compared actual results (R4) with the same data run through a market clearing engine which simulated the pre-R4 sequential selection.
Studied savings * 365 days in year / days in study = Expected Savings

## Slide 8: Simultaneous Selection of Ancillary Services
Observed Results – MCPC
 | URS |  | DRS |  | RRS |  | NSRS | 
 | R3 | R4 | R3 | R4 | R3 | R4 | R3 | R4
Average | $22.13 | $23.95 | $25.88 | $25.88 | $20.26 | $16.20 | $27.06 | $17.29
Difference | $1.82 |  | $0.00 |  | -$4.05 |  | -$9.77 | 

## Slide 9: Replacement Reserve Service
Status
Current Activities
Remaining Challenges
Observations from Testing
Transmittal of Test Data
No-Earlier-Than Date

## Slide 10: Replacement Reserve Service
Status
Final Stages of Testing
RPRS Market Clearing Engine (MCE)
and
Simultaneous Feasibility Test (SFT)
  January 4th, 2006 Patch Installed
  Vital Functions Operational
  Additional Patch Expected
Notes: Final Stages of testing means that we have wrapped up the planned software tests and are evaluating market results.
“Vital Functions Operational” means that the pieces of RPRS and SFT which are mandatory are working. There are some extra features which could allow ERCOT operations some additional flexibility and/or improve RPRS/SFT performance which are expected to be fixed.

## Slide 11: Replacement Reserve Service
Current Activities
Daily Verification of Results
  Comparison between OOMC and RPRS
    For each difference, an explanation
  MCPC Verification
    Correct
  Unstructured Testing
    Evaluate RPRS unit selection, dispatch
    Everything has been as expected
Notes: OOMC and RPRS Comparison – Each list of procurements and constraints is analyzed. These comparisons have led to ERCOT’s discovery of the network model inconsistencies. There are expected to be differences due to the offline nature of the OOMC studies and the economics of the RPRS studies.
MCPC Verification – An MCPC is generated whenever RPRS detects a capacity deficit (or zonal congestion) after the evaluation of local congestion (step 1). When there is a deployment for Step 2, an analyst manually calculates the MCPC for that hour and compares with the RPRS calculated MCPC. All calculations have been correct since the January 4th Patch.
Unstructured Testing – Several ERCOT analysts conduct tests on the RPRS results each day. These tests vary a great deal and are based on each analyst’s experience. One example would be to determine reasons for every deployment – or to look to see why SFT identified a certain constraint.

## Slide 12: Replacement Reserve Service
Remaining Challenges
Network Model Inconsistencies
  Normal Breaker Status (ETA 1/20/06)
  LaaR Modeling (ETA 2/28/06)
SFT Patch (ETA 2/15/06)
Visibility in SFT
Notes: There have been about 25 fixes to RPRS put in place since R4 implementation. These are the most crucial remaining issues.
Normal Breaker Status – Through daily verification of RPRS, ERCOT has discovered several inconsistencies with regard to normal status settings. ERCOT Network Model group has been actively working with TDSPs to resolve the inconsistencies.
LaaR Modeling – Through daily verification of RPRS, ERCOT has discovered that stations with LaaR in the network model do not always have the correct MW flow represented in SFT. This results in additional MW load at certain stations, leading to inaccurate SFT results. This problem is exacerbated by Private Network generation with the LaaR.
SFT Patch – There are some additional features in SFT that ERCOT is expecting. While these features are not necessary for the initial deployment of RPRS, they will improve SFT performance, thus improving RPRS performance in order to get deployments out sooner.
Visibility in SFT – During ERCOT’s evaluation of RPRS it was found necessary to understand what SFT sees in its study. While there are some workarounds that our Engineers can perform which have allowed us to find some errors, it is still not completely visible. Efforts are underway to determine the best way to ‘see inside the box.’ It remains to be seen if this issue will prevent RPRS from becoming a fully functional market before it is resolved. It is possible that the coming improvements to the Network Model and SFT may allow ERCOT to proceed in the short term without a fix in this area.

## Slide 13: Replacement Reserve Service
Observations from Testing
OOMC and RPRS Comparison
  Generally more efficient set of resources
MCPC Verification – All Good
Use of Base Load Generation
  Solves local constraints by reducing before buying
Notes: OOMC and RPRS Comparison – Based on preliminary results, ERCOT expects that RPRS will order more efficient set of units online than our present day OOMC procedures. Sometimes the efficiency is gained due to more cost effective generation being selected, and at others it is because less generation is needed with RPRS. It is important to note that sometimes we have seen additional resources brought on with RPRS than we have brought on with OOMC.
MCPC Verification – An MCPC is generated whenever RPRS detects a capacity deficit (or zonal congestion) after the evaluation of local congestion (step 1). In preliminary results, ERCOT has observed few MCPCs, and the range has been large – from $11 to $245. The main reason for the large observed gap is the lack of lower priced bids.
Use of Base Load Generation – It has been observed that RPRS will assume that base load generation is always available to move down to solve local constraints before committing additional units. ERCOT does expect that this can lead to the reduction (via OOME or LBES) in generation from traditionally base loaded generation such as coal and lignite. This is because RPRS only commits based on the startup and operational cost, not on the incremental costs for each resource. In Texas Nodal, a similar approach is planned.
Protocol 6.6.3.2.1 (4) “ERCOT will solve security violations using a transmission security-constrained ... objective is to minimize based on Resource Category Generic Cost, capacity price, operation price, and Resource Shift Factors, as described in Section 4.4.16, ERCOT receipt of Replacement Reserve Bids, …” (this indicates that RPRS can only use the capacity and operation price from the RPRS bid.)

## Slide 14: Replacement Reserve Service
Transmittal of Test Data
Must wait until results are accurate
  Market Clearing Price for Capacity
  MW Procured for each step
Notes: WMS will be informed as to how the reports will be transmitted.

## Slide 15: Replacement Reserve Service
No-Earlier-Than Date
March 15th, 2006
Assumptions
  Network Model is correct
  LaaR Modeling solution is implemented
  Results are satisfactory

## Slide 16: EMMS Release 4 Market Wrap-up
Questions?