## Slide 1
Lessons Learned from Block Load Transfers following Hurricane Rita
Reliability and Operations Subcommittee Meeting
January 13, 2006

## Slide 2: Lesson’s Learned
Purpose: Brief evaluation of Block Load Transfers (BLTs) in the aftermath of Hurricane Rita to pick up load in Entergy Gulf States Service territory
Involved Parties:
TXU Energy Delivery – Deep East Texas Cooperative BLT (≈10 MWs)
Centerpoint – Crosby Station BLT (≈80 MWs)
Entergy Gulf States

## Slide 3: Lesson’s Learned
Physical Issues:
Very little ERCOT can do. Work needed to block load over and all closely associated activities are between TDSPs.
One-line drawings delivered ASAP are very important for a timely transfer (acceptable format)
Contractual issues between the TDSP’s (how to compensate TDSPs for work) can slow up transfer

## Slide 4: Lesson’s Learned
Commercial Issues:
Need to create a LSE in ERCOT’s system was a hindrance
Contractual Issues between the TDSPs should be considered in advance of the need to use an emergency BLT
Settlement quality metering during a BLT for emergency restoration (.2% vs .6% CT accuracy)
Frequency for providing metering data as well as method for providing data

## Slide 5: Lesson’s Learned
Recommendations:
ERCOT will investigate the creation entities and their relationships ahead of time (LSE for BLT into ERCOT; RE for BLT into other control area).
Metering CT accuracy (.6%) will be allowed for emergency load restoration.
ERCOT recommends actual meter data be provided before initial settlement run. Use of default profiles would introduce significant error if used.
ERCOT will be flexible as to the format for data submittal (Loadstar, Excel, etc.).
Investigate clearing Interstate Commerce issues in advance for BLTs that could block loads across state lines.
Develop checklist for entities to use as a guide to prepare for an emergency.