## Slide 1: Updated Cost/Benefit Analysis for PRR 567 Multi-Part A/S Bidding
PRS January Meeting
January 19, 2006

## Slide 2: What We Want to Accomplish Today
  Review methodology used to calculate benefits of PRR 567
  Review input data and assumptions
  Review results
  Review revised CBA

## Slide 3: Input data requirements
Typical Unit Data
  Start Cost - ($)
  Unit Max (MW)
  Unit Min (MW)
  AGC Max (MW)
  AGC Min (MW)
  Avg HR at Unit Max (MMBtu/MWh)
  Avg HR at Unit Min (MMBtu/MWh)
  Avg HR at AGC Max (MMBtu/MWh)
  Avg HR at AGC Min (MMBtu/MWh)
  Min Run (Hours)
  Min Down (Hours)
  AGC Range Ramp Rate (MW/min)
Market Data (Actual)
  Hourly energy prices for next day
    Used the previous 10 day average of North zone MCPE as a proxy
  Daily gas prices
    Used Gas Daily prices for HSC
  ERCOT historic deployment data
    Used previous 10 days for URS
    Used same month for RRS
  ERCOT day-ahead A/S market data for following: (hourly for URS and RRS)
    MCPC
    Procured MW
    Aggregated bid stack
  Note: all data except gas prices were obtained from the ERCOT Public Market Information web page.

## Slide 4: Methodology for Calculating Market Cost Savings
Using the input data calculate the following for a typical conventional steam unit and CCCT unit for both URS and RRS:
    Offer bids ($/MW)
    Minimum running cost ($)
    Start Costs ($)
    Offer capacity (MW)
Offers from these typical units are inserted into the RRS and URS supply stack and re-clear the RRS and URS markets for all hours
Calculate daily savings based on the lower MCPC resulting from the new bid stack
Determine if any “make whole payments” are required to cover start up and minimum running costs
Subtract “make whole payments” from daily savings to determine market savings for the day
Repeat for each day from 11/01/2004 through 10/31/2005
Take the maximum daily saving between URS and RRS for each type of unit and sum the market savings for the 12 months.

## Slide 5: Assumed Unit Parameters Used in Model
 | Large Steam | CCCT | Small Drum
Start Cost ($) | 3000+9*Max*Gas | 6810+2200*Gas | 2160+9*Max*Gas
Unit Max (MW) | 500 | 500 | 239
Unit Min (MW) | 35 | 130 | 37
AGC Max (MW) | 490 | 500 | 230
AGC Min (MW) | 50 | 130 | 37
Avg HR at Unit Max (MMBtu/MWh) | 9.8 | 7.1 | 11.0
Avg HR at Unit Min (MMBtu/MWh) | 14.0 | 7.8 | 15.0
Avg HR at AGC Max (MMBtu/MWh) | 10.0 | 7.1 | 11.0
Avg HR at AGC Min (MMBtu/MWh) | 13.4 | 7.8 | 14.9
Min Run (Hours) | 5 | 10 | 3
Min Down (Hours) | 4 | 4 | 2
AGC Range Ramp Rate (MW/min) | 30 | 10 | 14

## Slide 6: Market Savings Model Results
Steam

## Slide 7: Market Savings by Day
# Days > 0 218
% Days > 0 60%
Max Savings $2,618,889
Min Savings > 0 $427

## Slide 8: Analysis of Resource Plan Availability of Gas Fired Steam Units
Number of days in the month unit available but not on-line

## Slide 9: Analysis of Resource Plan Availability of CCCT Units
Number of days in the month unit available but not on-line

## Slide 10
Revised PRR 567 CBA