## Slide 1: The Need for PRR 647
Properly Modeling the Reactive Behavior of Generators

## Slide 2: Presentation Order
Current State of Affairs
  Protocols
  Model
Problem
Proposed Solution

## Slide 3: Current State of Affairs in ERCOT (Protocol)
(1) A QSE representing a Generation Entity that has Generation Resources connected to a TDSP shall provide the following Real Time data to ERCOT for each individual generating unit at a Generation Resource plant location and ERCOT will make the data available to the Generation Resource’s host TDSP (at TDSP expense):
(a) gross or net real power;
(b) gross or net Reactive Power;
(c) if gross quantities are provided, the plant auxiliary Load data will also be supplied;

## Slide 4: Pictorial Protocol
QSE must provide
Net MW/MVAr OR
Gross & Plant MW/MVAr
Net = Gross – Plant - XFMR
Gross
Aux/Plant
XFMR Consumption
Net

## Slide 5: Model “Reality”
Gross
Aux/Plant
XFMR Consumption
Net
Net used
As Gross

## Slide 6: Problem: As System Becomes More Vulnerable to Voltage Collapse, Reactive Reserve Modeling Becomes Crucial

## Slide 7: How Generator MVArs are Modeled
Gross Generator Output
Net Generator Output
True Reactive Reserve
Modeled Reactive Reserve
If Net output is incorrectly
used in place of Gross Output
Q
(MVAr)
P(MW)
Aux/Plant Load
Gross Reactive Capability Curve (CURL)
Usually Created by Generator Manufacturer

## Slide 8: Solution
Gross
Aux/Plant
XFMR
Loss
Net (High Side)
Net (Low Side)
Provided
Calculated

## Slide 9: Metering Freq/Accuracy
Frequency (To be placed in operating guides)
  Net MW RTU (Same as current)
  Gross/Net MVAr, Gross MW ICCP or RTU
Accuracy
  No change to 6.5.1.1(6) “Real Time data for reliability purposes must be accurate to within three percent (3%). This telemetry may be provided from relaying accuracy instrumentation transformers.”